## Slide 1
Control Engineering I
Signal Flow Graphs

## Slide 2: Mason’s Rule (Mason, 1953)
The block diagram reduction technique requires successive application of fundamental relationships in order to arrive at the system transfer function.
On the other hand, Mason’s rule for reducing a signal-flow graph to a single transfer function requires the application of one formula.
The formula was derived by S. J. Mason when he related the signal-flow graph to the simultaneous equations that can be written from the graph.

## Slide 3: Mason’s Rule:
The transfer function, C(s)/R(s), of a system represented by a signal-flow graph is;
Where
n = number of forward paths.
Pi = the i th forward-path gain.
∆ = Determinant of the system
∆i = Determinant of the ith forward path
∆ is called the signal flow graph determinant or characteristic function. Since ∆=0 is the system characteristic equation.

## Slide 4: Mason’s Rule:
∆ = 1- (sum of all individual loop gains) + (sum of the products of the gains of all possible two loops that do not touch each other) – (sum of the products of the gains of all possible three loops that do not touch each other) + … and so forth with sums of higher number of non-touching loop gains
∆i = value of Δ for the part of the block diagram that does not touch the i-th forward path (Δi = 1 if there are no non-touching loops to the i-th path.)

## Slide 5
Systematic approach
Calculate forward path gain Pi for each forward path i.
Calculate all loop transfer functions
Consider non-touching loops 2 at a time
Consider non-touching loops 3 at a time
etc
Calculate Δ from steps 2,3,4 and 5
Calculate Δi as portion of Δ not touching forward path i

## Slide 6: Example 1: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
Therefore,
There are three feedback loops

## Slide 7: Example 1: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
∆ = 1- (sum of all individual loop gains)
There are no non-touching loops, therefore

## Slide 8: Example 1: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
∆1 = 1- (sum of all individual loop gains)+...
Eliminate forward path-1
∆1 = 1
∆2 = 1- (sum of all individual loop gains)+...
Eliminate forward path-2
∆2 = 1

## Slide 9: Example 1: Continue

## Slide 10: Example 2: Apply Mason’s Rule to calculate the transfer function of the system represented by following Signal Flow Graph
2. Calculate all loop gains.
3. Consider two non-touching loops.
L1L3 L1L4
L2L4 L2L3
1. Calculate forward path gains for each forward path.
P1
P2

## Slide 11: Example 2: continue
Consider three non-touching loops.
None.
Calculate Δ from steps 2,3,4.

## Slide 12
Example 2: continue
Eliminate forward path-1
Eliminate forward path-2

## Slide 13
Example 2: continue

## Slide 14: Example 3
Find the transfer function, C(s)/R(s), for the signal-flow graph in figure below.

## Slide 15: Example 3
There is only one forward Path.

## Slide 16: Example 3
There are four feedback loops.

## Slide 17: Example 3
Non-touching loops taken two at a time.

## Slide 18: Example 3
Non-touching loops taken three at a time.

## Slide 19: Example 3
Eliminate forward path-1