## Slide 1: PI Compensation (PI Controller)

## Slide 2: PI Control
Integral control to improve e(), (increases type by one)  worse transient response or instability.
Add proportional control  controller has a pole and a zero.
Transfer function of proportional-plus-integral (PI) controller

## Slide 3: PI Remarks
Used in cascade compensation (integral term in the feedback path is equivalent to a differentiator in the forward path)
PI design for a plant transfer function G(s) = PD design of G(s)/ s.
A better design is often possible by "almost canceling" the controller zero and the controller pole (negligible effect on time response).

## Slide 4: Procedure 5.3
Design a proportional controller for the system to meet the transient response specifications, i.e. place the dominant closed-loop system poles at scl =  z wn  j wd .
Add a PI controller with the zero location (- a)  = small angle ( 3  5).
Tune the gain of the system to move the closed-loop pole closer to scl.

## Slide 5: Comments
Use PI control only if P-control meets the transient response but not the steady-state error specifications. Otherwise, use another control.
Use pole-zero diagram to prove zero location formula.

## Slide 6: Pole-zero Diagram of PI Controller

## Slide 7: Proof
Controller angle at scl
From Figure

## Slide 8: Proof (Cont.)
Solve for x
x = ( a/ n) Multiplying by n gives a.
Trig. identity

## Slide 9: Controller Angle at scl  (< 3) vs. 

## Slide 10: Example 5.6
Design a controller for the position control system to perfectly track a ramp input with a dominant pair with  = 0.7 & wn =4 rad/s.

## Slide 11: Solution
Procedure 5.1 with modified transfer function.
Unstable for all gains (see root locus plot).
Controller must provide an angle  249 at the desired closed-loop pole location.
Zero at 1.732.
Cursor at desired pole location on compensated system RL gives a gain of about 40.6.

## Slide 12: RL of System With Integrator

## Slide 13: RL of PI-compensated System

## Slide 14: Analytical Design
Values obtained earlier, approximately.
Closed-loop characteristic polynomial
Notes: Equate coefficients and solve

## Slide 15: MATLAB
» scl = 4*exp(j*(pi  acos( 0.7)) )
scl =
-2.8000 + 2.8566i
» theta = pi + angle( polyval( [ 1, 10, 0, 0], scl ) )
theta =
1.9285
» a = 4*sqrt(1-.7^2)/tan(theta)+ 4*.7
a =
1.7323
» k = abs(polyval( [ 1, 10, 0,0], scl )/ polyval([1,a], scl) )
k =
40.6400

## Slide 16: Design I Results
Closed-loop transfer function for Design I
Zero close to the closed-loop poles  excessive PO
(see step response together with the response for a later design: Design II).

## Slide 17: Step Response of PI-compensated System
Design I (dotted), Design II (solid).

## Slide 18: Design II: Procedure 5.3
 = 0.7, K  51.02 & n = 7.143 rad/s. (acceptable design)
zero location
Closed-loop transfer function
Gain slightly reduced to improve response.
Dominant poles  0.7, n= 6.6875 rad/s
Time response for Designs I and II
PO for Design II (almost pole-zero cancellation) << Design I (II better)