## Slide 1: PD Compensation

## Slide 2: PD Control
L= loop gain = N / D.
scl = desired closed-loop pole location.
Find a controller C s.t.  L C(scl) = 180 or its odd multiple (angle condition).
Controller Angle for scl
Zero location

## Slide 3: Remarks
Graphical procedures are no longer needed.
CAD procedure to obtain the design parameters for specified  & n.
» evalfr(l,scl) % Evaluate l at scl
» polyval( num,scl) % Evaluate num at scl
The complex value and its angle can also be evaluated using any hand calculator.

## Slide 4: Procedure:MATLAB or Calculator
Calculate   L (scl)
»theta = pi  angle(evalfr(l, scl) )
Calculate zero location using (5.14).
Calculate new loop gain (with zero)
» lc = tf( [1, a],1)*l
Calculate gain (magnitude condition)
» K = 1/abs( evalfr( lc, scl))
5. Check time response of PD-compensated system. Modify the design to meet the desired specifications if necessary (MATLAB).

## Slide 5: Procedure 5.2: Given e() & 
Obtain error constant Ke from e() and determine a system parameter Kf that remains free after Ke is fixed for the system with PD control.
2- Rewrite the closed-loop characteristic equation of the PD controlled system as

## Slide 6: Procedure 5.2 (Cont.)
Obtain Kf corresponding to the desired closed-loop pole location. As in Procedure 5.1, Kf can be obtained by clicking on the MATLAB root locus plot or applying the magnitude condition using MATLAB or a calculator.
Calculate the free parameter from the gain Kf .
Check the time response of the PD compensated system and modify the design to meet the desired specifications if necessary.

## Slide 7: Example 5.5
Use a CAD package to design a PD controller for the type I system
to meet the following specifications
(a)  = 0.7 & n = 10 rad/s.
(b)  = 0.7 & e()= 4% due to a unit ramp.

## Slide 8: (a)  =0.7 & n=10 rad/s
MATLAB: calculate pole location & corresponding gain
» scl = 10*exp( j*( pi-acos(0.7) ) )
scl =
7.0000 + 7.1414I
» g=zpk([ ],[0,-4],1); theta=pi( angle( evalfr( g, scl) ) )
theta =
1.1731
» a = 10 * sqrt(1-0.7^2)/ tan(theta) + 7
a =
10.0000
» k =1/abs(evalfr(tf( [1, a],1)*l,scl)) % Gain at scl
k =
10.0000

## Slide 9: RL of Uncompensated System

## Slide 10: RL of PD-compensated System

## Slide 11: (b)  =0.7, e()=4% for unit ramp
Closed-loop characteristic equation with PD
Assume that K varies with K a fixed, then
RL= circle centered at the origin

## Slide 12: RL of PD-compensated System
K  a fixed

## Slide 13: (b) Design Cont.
Desired location: intersection of root locus with  = 0.7 radial line.
K = 10, a =10 (same values as in Example 5.3).
MATLAB command to obtain the gain
» k = 1/abs( evalfr( tf([1,10],[ 1, 4, 0]), scl) )
k =
10.0000
Time responses of two designs are identical.