## Slide 1
  PID Compensation

## Slide 2
Different Types of Feedback Control
On-Off Control
This is the simplest form of control.

## Slide 3
Proportional Control
A proportional controller attempts to perform better than the On-off type by applying power in proportion to the difference in temperature between the measured and the set-point. As the gain is increased the system responds faster to changes in set-point but becomes progressively underdamped and eventually unstable. The final temperature lies below the set-point for this system because some difference is required to keep the heater supplying power.

## Slide 4
Proportional, Derivative Control
The stability and overshoot problems that arise when a proportional controller is used at high gain can be mitigated by adding a term proportional to the time-derivative of the error signal. The value of the damping can be adjusted to achieve a critically damped response.

## Slide 5
Proportional+Integral+Derivative Control
Although PD control deals neatly with the overshoot and ringing problems associated with proportional control it does not cure the problem with the steady-state error. Fortunately it is possible to eliminate this while using relatively low gain by adding an integral term to the control function which becomes

## Slide 6
The Characteristics of P, I, and D controllers
A proportional controller (Kp) will have the effect of reducing the rise time and will reduce, but never eliminate, the steady-state error.
An integral control (Ki) will have the effect of eliminating the steady-state error, but it may make the transient response worse.
A derivative control (Kd) will have the effect of increasing the stability of the system, reducing the overshoot, and improving the transient response.

## Slide 7
Proportional Control
By only employing proportional control, a steady state error occurs.
Proportional and Integral Control
The response becomes more oscillatory and needs longer to settle, the error disappears.
Proportional, Integral and Derivative Control
All design specifications can be reached.

## Slide 8
CL RESPONSE
RISE TIME
OVERSHOOT
SETTLING TIME
S-S ERROR
Kp
Decrease
Increase
Small Change
Decrease
Ki
Decrease
Increase
Increase
Eliminate
Kd
Small Change
Decrease
Decrease
Small Change
The Characteristics of P, I, and D controllers

## Slide 9
Tips for Designing a PID Controller
1. Obtain an open-loop response and determine what needs to be improved
2. Add a proportional control to improve the rise time
3. Add a derivative control to improve the overshoot
4. Add an integral control to eliminate the steady-state error
Adjust each of Kp, Ki, and Kd until you obtain a desired overall response.
Lastly, please keep in mind that you do not need to implement all three controllers (proportional, derivative, and integral) into a single system, if not necessary. For example, if a PI controller gives a good enough response (like the above example), then you don't need to implement derivative controller to the system. Keep the controller as simple as possible.

## Slide 10
  num=1;
  den=[1 10 20];
  step(num,den)
Open-Loop Control - Example

## Slide 11
Proportional Control - Example
The proportional controller (Kp) reduces the rise time, increases the overshoot, and reduces the steady-state error.
MATLAB Example
Kp=300;
num=[Kp];
den=[1 10 20+Kp];
t=0:0.01:2;
step(num,den,t)
K=300
K=100

## Slide 12
Kp=300;
Kd=10;
num=[Kd Kp];
den=[1 10+Kd 20+Kp];
t=0:0.01:2;
step(num,den,t)
Proportional - Derivative - Example
The derivative controller (Kd) reduces both the overshoot and the settling time.
MATLAB Example
Kd=10
Kd=20

## Slide 13
Proportional - Integral - Example
The integral controller (Ki) decreases the rise time, increases both the overshoot and the settling time, and eliminates the steady-state error
MATLAB Example
Kp=30;
Ki=70;
num=[Kp Ki];
den=[1 10 20+Kp Ki];
t=0:0.01:2;
step(num,den,t)
Ki=70
Ki=100

## Slide 14
Syntax
    rltool
    rltool(sys)
    rltool(sys,comp)
RLTOOL

## Slide 15
RLTOOL

## Slide 16
RLTOOL

## Slide 17
RLTOOL

## Slide 18
RLTOOL

## Slide 19
Consider the following configuration:
Example - Practice

## Slide 20
The design a system for the following specifications:
· Zero steady state error
· Settling time within 5 seconds
· Rise time within 2 seconds
· Only some overshoot permitted
Example - Practice