## Slide 1: The 8085 Programming Model

## Slide 2: The 8085 Microprocessor
The 8085 is an 8-bit microprocessor made by Intel.
It has:
  6 general purpose registers
  An accumulator
  A flag register
  A stack pointer
  A program counter
H L
Program Counter
Accumulator | Flags
B | C
D | E
Stack Pointer | 

## Slide 3: The 8085 Programming Model
The Registers
  The 6 general purpose registers are 8-bits wide each.
    They are to be used as needed.
    They are called B, C, D, E, H, and L.
    They can be used as 16-bit register pairs: BC, DE, HL.
  The accumulator is technically part of the ALU.
    It is 8-bits wide.
    It is one of the inputs to every ALU operation.
    The result of any operation is always stored in it.
    It is known as Register A.

## Slide 4: The 8085 Programming Model
The ALU includes five flag flip-flops that are set or reset after an operation.
  They are Z (zero), CY (carry), S (sign), P (parity) and AC
(Auxiliary Carry).
  These flags are used when the microprocessor tests for data conditions.
  These make up the Flags Register.

## Slide 5: The 8085 Instructions
Since the 8085 is an 8-bit device it can have up to 28 (256) instructions.
  However, the 8085 only uses 246 combinations that
represent a total of 74 instructions.
– Most of the instructions have more than one format.
These instructions can be grouped into five
different groups:
  Data Transfer Operations
  Arithmetic Operations
  Logic Operations
  Branch Operations
  Machine Control Operations

## Slide 6: Instruction and Data Formats
Each instruction has two parts.
  The first part is the task or operation to be performed.
    This part is called the “opcode” (operation code).
  The second part is the data to be operated on
    Called the “operand”.

## Slide 7: Operand Types
There are different ways for specifying the operand:
  There may not be an operand (implied operand)
    CMA
  The operand may be an 8-bit number (immediate data)
    ADI 4FH
  The operand may be an internal register (register)
    SUB B
  The operand may be a 16-bit address (memory address)
    LDA 4000H

## Slide 8: Instruction Size
Depending on the operand type, the instruction may have different sizes. It will occupy a different number of memory bytes.
  Typically, all instructions occupy one byte only.
  The exception is any instruction that contains immediate data or a memory address.
    Instructions that include immediate data use two bytes.
      One for the opcode and the other for the 8-bit data.
    Instructions that include a memory address occupy three bytes.
      One for the opcode, and the other two for the 16-bit address.

## Slide 9: Instruction with Immediate Date
Operation: Load an 8-bit number into the accumulator.
  MVI A, 32
    Operation: MVI A
    Operand: The number 32
    Binary Code:
0011 1110 3E 1st byte.
2nd
0011 001032 byte.

## Slide 10: Instruction with a Memory Address
Operation: go to address 2085.
  Instruction: JMP 2085
    Opcode: JMP
    Operand: 2085
    Binary code:
1100 0011 C3
1st
byte.
1000 0101 | 85 | 2nd byte
0010 0000 | 20 | 3rd byte
Note: Error in book on page 146.

## Slide 11: Addressing Modes
The microprocessor has different ways of specifying the data for the instruction. These are called “addressing modes”.
The 8085 has four addressing modes:
Implied
Immediate
Direct
Indirect
CMA
MVI B, 45
LDA 4000 LDAX B
Load the accumulator with the contents of the memory
location whose address is stored in the register pair BC).

## Slide 12: Data Formats
In an 8-bit microprocessor, data can be represented in one of four formats:
  ASCII
  BCD
  Signed Integer
  Unsigned Integer.
It is important to recognize that the microprocessor deals with 0’s and 1’s.
  It deals with values as strings of bits.
  It is the job of the user to add a meaning to these strings.

## Slide 13: Data Formats
Assume the accumulator contains the following value: 0100 0001.
  There are four ways of reading this value:
    It is an unsigned integer expressed in binary, the equivalent decimal number would be 65.
    It is a number expressed in BCD (Binary Coded Decimal)
format. That would make it, 41.
    It is an ASCII representation of a letter. That would make it the letter A.
    It is a string of 0’s and 1’s where the 0th and the 6th bits are set to 1 while all other bits are set to 0.
ASCII stands for American Standard Code for Information Interchange.