## Slide 1: Intel x86 Architecture
Computer Organization and Assembly Languages
Yung-Yu Chuang
Notes: <number>

## Slide 2: Intel microprocessor history
Notes: <number>

## Slide 3: Early Intel microprocessors
<number>
Intel 8080 (1972)
  64K addressable RAM
  8-bit registers
  CP/M operating system
  5,6,8,10 MHz
  29K transistros
Intel 8086/8088 (1978)
  IBM-PC used 8088
  1 MB addressable RAM
  16-bit registers
  16-bit data bus (8-bit for 8088)
  separate floating-point unit (8087)
  used in low-cost microcontrollers now
my first computer (1986)
Notes: <number>

## Slide 4: The IBM-AT
<number>
Intel 80286 (1982)
  16 MB addressable RAM
  Protected memory
  several times faster than 8086
  introduced IDE bus architecture
  80287 floating point unit
  Up to 20MHz
  134K transistors
Notes: <number>

## Slide 5: Intel IA-32 Family
<number>
Intel386 (1985)
  4 GB addressable RAM
  32-bit registers
  paging (virtual memory)
  Up to 33MHz
Intel486 (1989)
  instruction pipelining
  Integrated FPU
  8K cache
Pentium (1993)
  Superscalar (two parallel pipelines)
Notes: <number>

## Slide 6: Intel P6 Family
<number>
Pentium Pro (1995)
  advanced optimization techniques in microcode
  More pipeline stages
  On-board L2 cache
Pentium II (1997)
  MMX (multimedia) instruction set
  Up to 450MHz
Pentium III (1999)
  SIMD (streaming extensions) instructions (SSE)
  Up to 1+GHz
Pentium 4 (2000)
  NetBurst micro-architecture, tuned for multimedia
  3.8+GHz
Pentium D (2005, Dual core)
Notes: <number>

## Slide 7: IA32 Processors
Totally Dominate Computer Market
Evolutionary Design
  Starting in 1978 with 8086
  Added more features as time goes on
  Still support old features, although obsolete
Complex Instruction Set Computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!

## Slide 8: IA-32 Architecture
Notes: <number>

## Slide 9: IA-32 architecture
<number>
Lots of architecture improvements, pipelining, superscalar, branch prediction, hyperthreading and multi-core.
From programmer’s point of view, IA-32 has not changed substantially except the introduction of a set of high-performance instructions
Notes: <number>

## Slide 10: Modes of operation
<number>
Protected mode
  native mode (Windows, Linux), full features, separate memory
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer
Notes: <number>

## Slide 11: Addressable memory
<number>
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address
Notes: <number>

## Slide 12: General-purpose registers
<number>
Notes: <number>

## Slide 13: Accessing parts of registers
<number>
Use 8-bit name, 16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX
Notes: <number>

## Slide 14: Index and base registers
<number>
Some registers have only a 16-bit name for their lower half (no 8-bit aliases). The 16-bit registers are usually used only in real-address mode.
Notes: <number>

## Slide 15: Some specialized register uses (1 of 2)
<number>
General-Purpose
  EAX – accumulator (automatically used by division and multiplication)
  ECX – loop counter
  ESP – stack pointer (should never be used for arithmetic or data transfer)
  ESI, EDI – index registers (used for high-speed memory transfer instructions)
  EBP – extended frame pointer (stack)
Notes: <number>

## Slide 16: Some specialized register uses (2 of 2)
<number>
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit (set or clear)
Some other system registers such as IDTR, GDTR, LDTR etc.
Notes: <number>

## Slide 17: Status flags
<number>
Carry
  unsigned arithmetic out of range
Overflow
  signed arithmetic out of range
Sign
  result is negative
Zero
  result is zero
Auxiliary Carry
  carry from bit 3 to bit 4
Parity
  sum of 1 bits is an even number
Notes: <number>

## Slide 18: Floating-point, MMX, XMM registers
<number>
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations
Notes: <number>

## Slide 19: Programmer’s model
<number>

## Slide 20: Programmer’s model
<number>

## Slide 21: IA-32 Memory Management
Notes: <number>

## Slide 22: Real-address mode
<number>
1 MB RAM maximum addressable (20-bit address)
Application programs can access any area of memory
Single tasking
Supported by MS-DOS operating system
Notes: <number>

## Slide 23: Segmented memory
<number>
Segmented memory addressing: absolute (linear) address is a combination of a 16-bit segment value added to a 16-bit offset
linear addresses
one segment
(64K)
Notes: <number>

## Slide 24: Calculating linear addresses
<number>
Given a segment address, multiply it by 16 (add a hexadecimal zero), and add it to the offset
Example: convert 08F1:0100 to a linear address
Adjusted Segment value: 0 8 F 1 0
Add the offset: 0 1 0 0
Linear address: 0 9 0 1 0
A typical program has three segments: code, data and stack. Segment registers CS, DS and SS are used to store them separately.
Notes: <number>

## Slide 25: Example
<number>
What linear address corresponds to the segment/offset address 028F:0030?
028F0 + 0030 = 02920
Always use hexadecimal notation for addresses.
Notes: <number>

## Slide 26: Protected mode (1 of 2)
<number>
4 GB addressable RAM (32-bit address)
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows
Notes: <number>

## Slide 27: Protected mode (2 of 2)
<number>
Segment descriptor tables
Program structure
  code, data, and stack areas
  CS, DS, SS segment descriptors
  global descriptor table (GDT)
MASM Programs use the Microsoft flat memory model
Notes: <number>

## Slide 28: Flat segmentation model
<number>
All segments are mapped to the entire 32-bit physical address space, at least two, one for data and one for code
global descriptor table (GDT)
Notes: <number>

## Slide 29: Multi-segment model
<number>
Each program has a local descriptor table (LDT)
  holds descriptor for each segment used by the program
multiplied by
1000h
Notes: <number>

## Slide 30: Translating Addresses
The IA-32 processor uses a one- or two-step process to convert a variable's logical address into a unique memory location.
The first step combines a segment value with a variable’s offset to create a linear address.
The second optional step, called page translation, converts a linear address to a physical address.

## Slide 31: Converting Logical to Linear Address
The segment selector points to a segment descriptor, which contains the base address of a memory segment. The 32-bit offset from the logical address is added to the segment’s base address, generating a 32-bit linear address.

## Slide 32: Indexing into a Descriptor Table
Each segment descriptor indexes into the program's local descriptor table (LDT). Each table entry is mapped to a linear address:

## Slide 33: Paging (1 of 2)
Virtual memory uses disk as part of the memory, thus allowing sum of all programs can be larger than physical memory
Only part of a program must be kept in memory, while the remaining parts are kept on disk.
The memory used by the program is divided into small units called pages (4096-byte).
As the program runs, the processor selectively unloads inactive pages from memory and loads other pages that are immediately required.

## Slide 34: Paging (2 of 2)
OS maintains page directory and page tables
Page translation: CPU converts the linear address into a physical address
Page fault: occurs when a needed page is not in memory, and the CPU interrupts the program
Virtual memory manager (VMM) – OS utility that manages the loading and unloading of pages
OS copies the page into memory, program resumes execution

## Slide 35: Page Translation
A linear address is divided into a page directory field, page table field, and page frame offset. The CPU uses all three to calculate the physical address.