## Slide 1: First Course of Special Machine
Department of Electrical Power and Machine Engineering
By Qasim Al Azze 2018

## Slide 2
1398
Electrical Technology
  What could be the reasons if a split-phase motor fails to start and hums loudly ? Ans. It could be due to the starting winding being open or grounded or burnt out.
  What could be the reasons if a split-phase motor runs too slow ? Ans. Any one of the following factors could be responsible :
    wrong supply voltage and frequency
    overload
    grounded starting and running windings
    short-circuited or open winding in field circuit.
1. The starting winding of a single-phase mo- tor is placed in the
(a) rotor
(c) armature
(b) stator
(d) field.
One of the characteristics of a single- phase motor is that it
  is self-starting
  is not self-starting
  requires only one winding
  can rotate in one direction only.
After the starting winding of a single- phase induction motor is disconnected from supply, it continues to run only on ............winding.
(a) rotor
(c) field
(b) compensating
(d) running
If starting winding of a single-phase induction motor is left in the circuit, it will
  draw excessive current and overheat
  run slower
  run faster
  spark at light loads.
The direction of rotation of a single-phase mo- tor can be reversed by
  reversing connections of both windings
  reversing connections of starting winding
  using a reversing switch
  reversing supply connections.
If a single-phase induction motor runs slower than normal, the more likely defect is
  improper fuses
  shorted running winding
  open starting winding
  worn bearings.
The capacitor in a capacitor-start induction- run ac motor is connected in series with ...... winding.
(a) starting (b) running
(c) squirrel-cage (d) compensating
A permanent-split single-phase capacitor motor does not have
  centrifugal switch
  starting winding
  squirrel-cage rotor
  high power factor.
The starting torque of a capacitor-start induction-run motor is directly related to the angle  between its two winding currents by the relation
(a) cos 
(c) tan 
(b) sin 
(d) sin /2.
In a two-value capacitor motor, the capacitor used for running purposes is a/an
  dry-type ac electrolytic capacitor
  paper-spaced oil-filled type
  air-capacitor
  ceramic type.
If the centrifugal switch of a two-value capacitor motor using two capacitors fails to open, then
  electrolytic capacitor will, in all probabil- ity, suffer breakdown
  motor will not carry the load
  motor will draw excessively high current
  motor will not come upto the rated speed.
Each of the following statements regarding a shaded-pole motor is true except
  its direction of rotation is from un- shaded to shaded portion of the poles
  it has very poor efficiency
  it has very poor p.f.
  it has high starting torque.
Compensating winding is employed in an ac series motor in order to
OBJECTIVE TESTS – 36

## Slide 3
Single-phase Motors
1399
compensate for decrease in field flux
increase the total torque
reduce the sparking at brushes
reduce effects of armature reaction.
A universal motor is one which
  is available universally
  can be marketed internationally
  can be operated either on dc or ac supply
  runs at dangerously high speed on no-load.
In a single-phase series motor the main purpose of inductively-wound compensating winding is to reduce the
  reactance emf of commutation
  rotational emf of commutation
  transformer emf of commutation
  none of the above.
(Power App.-II, Delhi Univ. Jan. 1987)
A repulsion motor is equipped with
  a commutator (b) slip-rings
a repeller
neither (a) nor (b).
A repulsion-start induction-run single- phase motor runs as an induction motor only when
  brushes are shifted to neutral plane
  short-circuiter is disconnected
  commutator segments are short- circuited
  stator winding is reversed.
If a dc series motor is operated on ac supply, it will
  have poor efficiency
  have poor power factor
  spark excessively
  all of the above
  none of the above.
An outstanding feature of a universal motor is its
  best performance at 50 Hz supply
  slow speed at all loads
excellent performance on dc. supply
highest output kW/kg ratio.
The direction of rotation of a hysteresis motor is determined by the
  retentivity of the rotor material
  amount of hysteresis loss
  permeability of rotor material
  position of shaded pole with respect to the main pole.
Speed of the universal motor is
  dependent on frequency of supply
  proportional to frequency of supply
  independent of frequency of supply
  none of the above.
(Elect. Machines, A.M.I.E. Sec. B, 1993)
In the shaded pole squirrel cage induction motor the flux in the shaded part always
  leads the flux in the unshaded pole segment
  is in phase with the flux in the unshaded pole segment
  lags the flux in the unshaded pole segment
  none of the above.
(Elect. Machines, A.M.I.E. Sec. B, 1993)
Which of the following motor is an interesting example of beneficially utilizing a phenomenon that is often considered undesirable ?
  hysteresis motor
  reluctance motor
  stepper motor
  shaded-pole motor.
Usually, large motors are more efficient than small ones. The efficiency of the tiny motor used in a wrist watch is approximately.......... per cent.
  1
  10
  50
  80
ANSWERS
11. a 12. d 13. d 14. c 15. d 16. a
1. b 2. b 3. d 4. a 5. b 6. d 7. a 8. a 9. b 10. b
17. c 18. d 19. d 20. d 21. a 22. c 23. a 24. a