## Slide 1: First Course of Special Machine
Department of Electrical Power and Machine Engineering
By Qasim Al Azze 2018

## Slide 2
Single-phase Motors
1381
36.8. Capacitor Start-and-Run Motor
This motor is similar to the capacitor-start motor [Art.36.4 (ii)] except that the starting winding
and capacitor are connected in the circuit at all times. The advantages of leaving the capacitor permanently in circuit are (i) improvement of over-load capacity of the motor (ii) a higher power factor (iii) higher efficiency and (iv) quieter running of the motor which is so much desirable for small power drives in offices and laboratories. Some of these motors which start and run with one value of capacitance in the circuit are called single-value capacitor-run motors. Other which start with high value of capacitance but run with a low value of
capacitance are known as two-value capacitor-run motors.
(i) Single-value capacitor-Run Motor
It has one running winding and one starting winding in series with a capacitor as shown in Fig.
36.28. Since capacitor remains in the circuit permanently, this motor is often referred to as permanent-
Fig. 36.28 Fig. 36.29 Fig. 36.30
split capacitor-run motor and behaves practically like an unbalanced 2-phase motor. Obviously, there is no need to use a centrifugal switch which was necessary in the case of capacitor-start motors. Since the same capacitor is used for starting and running, it is obvious that neither optimum starting nor optimum running performance can be obtained because value of capacitance used must be a compro- mise between the best value for starting and that for running. Generally, capacitors of 2 to 20 F capacitance are employed and are more expensive oil or pyranol-insulated foil-paper capacitors be- cause of continuous-duty rating. The low value of the capacitor results in small starting torque which is about 50 to 100 per cent of the rated torque (Fig. 36.29). Consequently, these motors are used where the required starting torque is low such as air - moving equipment i.e. fans, blowers and voltage regulators and also oil burners where quiet operation is particularly desirable.
One unique feature of this type of motor is that it can be easily reversed by an external switch provided its running and starting windings are identical. One serves as the running winding and the other as a starting winding for one direction of rotation. For reverse rotation, the one that previously served as a running winding becomes the starting winding while the former starting winding serves as the running winding. As seen from Fig. 36.30 when the switch is in the forward position, winding B serves as running winding and A as starting winding. When switch is in ‘reverse’ position, winding A becomes the running winding and B the starting winding.
Capacitor starts and run motor

## Slide 3
1382
Electrical Technology
Such reversible motors are often used for operating devices that must be moved back and forth very frequently such as rheostats, induction regulations, furnace controls, valves and arc-welding controls.
(ii) Two-value capacitor-Run Motor
This motor starts with a high capacitor in series with the starting winding so that the starting torque is high. For running, a lower capacitor is substituted by the centrifugal switch. Both the running and starting windings remain in circuit.
The two values of capacitance can be obtained as follows:
by using two capacitors in parallel at the start and then switching out one for low-value run. (Fig. 36.31) or
by using a step-up auto-transformer in conjunction with one capacitor so that effective capacitance value is increased for starting purposes.
In Fig. 36.31, B is an electrolytic capacitor of high capacity (short duty) and A is an oil capacitor of low value (continuous duty). Generally, starting capacitor B is 10 to 15 times the running capacitor A . At the start, when the centrifugal switch is closed, the two capacitors are put in parallel, so that their combined capacitance is the sum of their individual
capacitances. After the motor has reached 75 per cent full-load speed, the switch opens and only capacitor A remains in the starting winding circuit. In this
way, both optimum starting and running performance is achieved in such motors. If properly designed, such motors have operating characteristics very closely resembling those displayed by two-phase motors. Their performance is characterised by
ability to start heavy loads
extremely quiet operation
higher efficiency and power factor
ability to develop 25 per cent overload capacity
Hence, such motors are ideally suited where load require- ments are severe as in the case of compressors and fire strokers etc.
The use of an auto-transformer and single oil-type capacitor is illustrated in Fig.36.32. The transformer and capacitor are sealed in a rectangular iron box and mounted on top of the motor. The idea behind using this combination is that a capacitor of value C connected to the secondary of a step- up transformer, appears to the primary as though it had a value of K2C where K is voltage transforma- tion ratio. For example, if actual value of C = 4 F and K = 6, then low-voltage primary acts as if it had a 144 F ( = 62  4) capacitor connected across its terminals. Obviously, effective value of capacitance has increased 36 times. In the ‘start’ position of the switch, the connection is made to the
Fig. 36.31 Fig.36.32
Auto-transformer

## Slide 4
Single-phase Motors
1383
mid-tap of the auto-transformer so that K = 2. Hence, effective value of capacitance at start is 4 times the running value and is sufficient to give a high starting torque. As the motor speeds up, the centrifu- gal switch shifts the capacitor from one voltage tap to another so that the voltage transformation ratio changes from higher value at starting to a lower value for running. The capacitor which is actually of the paper-tinfoil construction is immersed in a high grade insulation like wax or mineral oil.
36.9. Shaded-pole Single- phase Motor
In such motors, the necessary phase-splitting is produced by induction. These motors have salient poles on the stator and a squirrel-cage type rotor Fig.
36.33 shows a four-pole motor with the field poles connected in series for alternate polarity. One pole of such a motor is shown separately in Fig. 36.34. The laminated pole has a slot cut across the laminations approximately one-third distance from one edge. Around the small part of the pole is placed a short- circuited Cu coil known as shading coil. This part of the pole is known as shaded part and the other as
unshaded part. When an alternating current is passed through the exciting (or field) winding surrounding the whole pole, the axis of the pole shifts from the unshaded part a to the shaded part b. This shifting of the magnetic axis is, in effect, equivalent to the actual physical movement of the pole. Hence, the rotor starts rotating in the direction of this shift i.e. from unshaded part to the shaded part.
Fig. 36.33 Fig. 36.34
Let us now discuss why shifting of the magnetic axis takes place. It is helpful to remember that the shading coil is highly inductive. When the alternating current through exciting coil tends to increase, it induces a current in the shading coil by transformer action in such a direction as to oppose its growth. Hence, flux density decreases in the shaded part when exciting current increases. However, flux density increases in the shaded part when exciting current starts decreasing (it being assumed that exciting current is sinusoidal).
In Fig. 36.35 (a) exciting current is rapidly increasing along OA (shown by dots). This will
produce an e.m.f. in the shading coil. As shading coil is of low resistance, a large current will be set up in such a direction (according to Lenz’s law) as to oppose the rise of exciting current (which is responsible for its production). Hence, the flux mostly shifts to the unshaded part and the magnetic axis lies along the middle of this part i.e. along NC.
Next, consider the moment when exciting current is near its peak value i.e. from point A to B [Fig. 36.35 (b)]. Here, the change in exciting current is very slow. Hence, practically no voltage and, therefore, no current is induced in the shading coil. The flux produced by exciting current is at its maximum value and is uniformly distributed over the pole face. So the magnetic axis shifts to the centre of the pole i.e. along positions ND.
Shaded pole single phase motor