## Slide 1
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
The Slope-Deflection Method
Introduction
As pointed out earlier, there are two distinct methods of analysis for statically indeterminate structures depending on how equations of equilibrium, load displacement and compatibility conditions are satisfied: 1) force method of analysis and (2) displacement method of analysis. In the last module, force method of analysis was discussed. In this module, the displacement method of analysis will be discussed. In the force method of analysis, primary unknowns are forces and compatibility of displacements is written in terms of pre-selected redundant reactions and flexibility coefficients using force displacement relations. Solving these equations, the unknown redundant reactions are evaluated. The remaining reactions are obtained from equations of equilibrium.
As the name itself suggests, in the displacement method of analysis, the primary unknowns are displacements. Once the structural model is defined for the problem, the unknowns are
automatically chosen unlike the force method. Hence this method is more suitable for computer implementation. In the displacement method of analysis, first equilibrium equations are satisfied. The equilibrium of forces is written by expressing the unknown joint displacements in terms of load by using load displacement relations. These equilibrium equations are solved for unknown joint displacements. In the next step, the unknown reactions are computed from compatibility equations using force displacement relations. In displacement method, three methods which are closely related to each other will be discussed.
Slope-deflection method
Moment distribution
Direct stiffness method
Degrees of Freedom
In the displacement method of analysis, primary unknowns are joint displacements, which are commonly referred to as the degrees of freedom of the structure. It is necessary to consider all the independent degrees of freedom while writing the equilibrium equations. These degrees of freedom are specified at supports, joints and at the free ends

## Slide 2
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
The following examples illustrated who to determine the degree of freedom
A
B
Is kinematically indeterminate to 2nd degree, unknowns are θA,and θB
A
B
Is kinematically indeterminate to 1st degree, unknowns is θB
A
B
Is kinematically indeterminate to 2nd degree, unknowns are θB, and ΔB
A
B
Is kinematically indeterminate to 1st degree, unknowns is θA,because θB=- θA due to symmetry
A
B
C
Is kinematically indeterminate to 2nd degree, unknowns are θB,and θC

## Slide 3
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Fixed-end moments
Moment with clockwise will be considered positive moment
A
B
C
Is kinematically indeterminate to 3rd degree, unknowns are θB, θC andΔ
Δ
A
B
P
a b
L
Pab2/L2
Pba /L
2 2
A
B
W kNlm
L
WL2/12
WL2/12
A
B
W kNlm
L
WL2/30
WL2/20
A
B
m
a
b
L
mb(2a-b)/L
2
ma(2b-a)/L2
b,a ≥L/3
θ
A
B
L
4EIθ/L
2EIθ/L
A
B
L
Δ
6EIΔ/L
6EIΔ/L

## Slide 4
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Slope-deflection method
This method is applicable to indeterminate beams and frames
Sign convention
M,θ, Δ/L=+ clockwise
A
B
θA
θB
L,EI
Δ
MFAB
MFBA
θA
4EIθA/L
2EIθA/L
θB
4EIθB/L
2EIθB/L
Δ
6EIΔ/L2
6EIΔ/L2

## Slide 5
Solution
1-unknowns θB, θC and θD 2-F.E.M
B
C D
A E
5 kN
25 kN.m
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Example(1):- write the F.E.M for the beam shown, due to the applied loading and:
A settlement at support D=18 mm downward , rotational slip at E=0.002 rad C.C.W. use EI=3(104) kN.m2
18 kN
12 kN/m
2 m
6 m
4 m
2 m
5 m
I 2I
3I

## Slide 6
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Example(2):- Analysis the following beam using slope-deflection method. EI constant
Solution
1- Unknown is θB 2- F.E.M
3-Slope-deflection equations
3- Joint conditions
Joint B MBA+MBC=0
MBC=-4(12)=-48(C.C.W)
A
B
C
12m
4m
2.5 kN/m
12 kN

## Slide 7
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Solution
1- Unknown are θB, θC 2- F.E.M
A
B
12
m
2.5 kN/m
21
48
12.75
17.25
C
4m
12 kN
48
12 kN
A
B
C
12m
4m
2.5 kN/m
12 kN
21
12.75
Example(3):- Analysis the following beam using slope-deflection method. The support at B settles 45mm.E=200GPa and I=3200(106) mm2
29.25 kN
A
B
C
6m
9m
5 kN/m
4 kN/m

## Slide 8
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
3-S-D-E
4-joint condition
MBA+MBC=0
3554.7
275.1
A
B
6m
4 kN/m
983.4
959.4
B
C
9m
2273.4 2273.4
230.1
A
B
C
6m
9m
5 kN/m
4 kN/m
3554.7
983.45 kN/m
1189.5
275.1

## Slide 9
Solution
1-unknown, θ
θA=- θB= θ 2-F.E.M
3-S.D.E
4- joint condition
5-final moments
A
B
C
D
5m
8m
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Example(4):- using slope-deflection method, analysis the frame shown in figure.EI constant
120 kN/m
A
B
C
D
5m
8m
120 kN/m
A
B
C
D
5m
8m
120 kN/m
487.62
243.81
480
144.76

## Slide 10
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Example(5):- Analysis the frame shown using slope-deflection method.E=200GPa, I=800E6 mm4. The support at D settles 10 mm
solution
1- Unknown θB1, θB2, θB3 2- F.E.M
3-slope deflection equations
4-joint conditions
D
A
B
C
3m
3m
4m
15 kN/m
D
A
C
3
m
3
m
4
m
15 kN/m
0.01
0.01B

## Slide 11
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
5-final moments

## Slide 12
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Side sway Frame
The frame is said to be side sway ,if
The frame or loading acting on it is non symmetric
There are at least two points in frame can move freely
The following examples to illustrate the side sway topic
No side sway
side sway
a
b Δ
c Δ
4
3
5/4Δ
3/4Δ
3
5
4
4
a
d
b'
C'
C"
Δc
Δ b
3
Δ 4
5
Δab=-Δ
Δbc=(5/4)Δ
Δcd=-(3/4)Δ

## Slide 13
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Example:- Analysis the frame shown in figure.EI constant
The frame is sidesway
Unknown θb, θc, Δ
F.E.M
3-slope deflection equations
(
)
( )
(
)
b
c
d
3.6m
6m
3m
a 60o
30kN/m
d
3.6m
6m
3m
a 60o
b Δ
cΔ
Δ
60o

## Slide 14
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
(
)
(
)
(
)
3- joint condition
--------1
Moment about o =0
------3
b
c
d
3.6m
6m
3m
60o
30o
o
6.235m
---------2
7.2
Mab
a 60o
Mdc
Vab
Vdc

## Slide 15
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Solving equations 1-3,gives
a
b
c
d
3
3
4
4
30
Example:- using slope deflection method, analysis the shown frame
The frame is sidesway
100
a
b
c
d
3
3
4
4
3
5
Δ 4

## Slide 16
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Unknown θb, θc, Δ
F.E.M
3-slope deflection equations
(
)
(
)
(
)
(
)
(
)
(
)
4- joint condition

## Slide 17
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
--------1
---------2
Moment about o =0
a
b
c
3
3
4
4
30
100
2.667
3.333
------3
o
Mab
Vab
Mdc
d Vdc

## Slide 18
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Solving equations 1-3,gives