## Slide 1
Water Resources Engineering
for 4th Class
By
Dr. Saad Shauket Sammen
Diyala University
College of Engineering
Department of Civil Engineering

## Slide 2
Irrigation and Drainage Networks
The direct irrigation scheme using a weir or a barrage, as well as the storage irrigation scheme using a dam or a reservoir, required a network of irrigation channels to supply the water to the irrigated areas and network of drainage to remove unwanted surface and subsurface in such a way that water-logging and salinity do not occur. The entire network as irrigation channels is called channel system.
Irrigation Network: - The channel system consists of:
1-Main canal
It is the principal channel of a canal system taking off from the headworks or reservoir or tail reach of a feeder. Also called main line. It is a large capacity channel and usually there is no direct irrigation from it. Small capacity ditch distributaries running parallel to the canal are taken off from the main canal to irrigate the adjoining areas. Main canal deliver supply to branch canal and main distributaries.

## Slide 3
2-Branch canal
Branch canals of capacity over 10 cumecs take their supply from the main canal and convey to the distributaries. Very little direct irrigation is done from the branch canals. (sub-branch) is a canal which takes off from branch canal but has capacity higher than distributary.
3-Distributary canal
A canal which taking off from a main canal or branch canal and distribute their supply through outlets into miners. They are aligned either as watershed channels or as side slope channels.
4-Minors
It is a small capacity channel usually taking its supply from a distributary canal. It supplies water to water courses.

## Slide 4
5-Water course
A channel taking off from a distributary or minor canal and serving farm channels or field channels.
6-Farm channel (Field channel)
A very small channel taking off from the water course and irrigating field. Generally it is unlined and has triangular cross-section.
7-Water course unit
It is the area irrigated by one water course and divided into farm units. Water course unit is bounded at the sides by open collector drains and at one end by a distributary canal and at the other end by a secondary or branch drain.

## Slide 5
Drainage System:- The drainage system consist of :-
1-Main drain
Open drain which removes drainage water from the project area to the outfall drain.
2-Branch drain
Receive water from main collector drain and discharging water into a main drain.
3-Main collector drain
Also was called secondary drain, receive water from collector drains and discharging water into branch or main drains.
4-Collector drain
A small open drain receive water from surface and sub-surface field drains and is discharging water into main collector drain and may be also take the escape flow at the tail of distributary canal.

## Slide 6
5-Field drain
Smallest drain of the system controlling the water table under the field or below root zone, and discharging water into collector drain.(usually use perforated P.V.C. pipe).