## Slide 1
Water Resources Engineering
for 4th Class
By
Dr. Saad Shauket Sammen
Diyala University
College of Engineering
Department of Civil Engineering

## Slide 2
Example: The rainfall hyetograph and the storm hydrograph for a 495 km2 basin are given. Assuming that the base flow is constant at 100 m3/sec, determine the Q – index for the basin and ordinates of the unit hydrograph.
Time (hr) | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Rainfall Intensity (mm/hr) | 10 | 20 | 20 |  |  |  |  | 
Storm Hydrograph (m3/sec) | 100 | 100 | 200 | 500 | 400 | 300 | 200 | 100
Solution:
Since the base flow is assumed to be constant and equal to 100 m3/sec, direct runoff hydrograph ordinates can be calculated in Column (4) as the storm hydrograph values given in Column (3) minus 100 m3/sec.

## Slide 3
Time (hr) (1) | Storm Hydrograph (m3/sec) (2) | DRH (m3/sec) (3) | UH2 (m3/sec) (4)
1 | 100 | 0 | 
2 | 100 | 0 | 0
3 | 200 | 100 | 12.5
4 | 500 | 400 | 50
5 | 400 | 300 | 37.5
6 | 300 | 200 | 25
7 | 200 | 100 | 12.5
8 | 100 | 0 | 0
 |  | Total = 1100 | 
The area under the direct runoff hydrograph is the total volume of excess rainfall. This volume should be equal to the whole drainage basin filled with water to a depth

## Slide 4
Thus, the total effective rainfall for this storm is 8 mm. Referring to the rainfall hyetograph below, the Q – index can be obtained as follows:
now we found Q – index is larger than 10 mm
And the runoff will occur only when rainfall intensity is larger than
Q – index, therefore, the value of Q – index must be recalculation as follow:

## Slide 5
This shows that the duration of the runoff producing rainfall starts at 2 hours and its intensity is constant at 20 – 16 = 4mm.Since the duration of the effective rain is 2 hrs , the net rainfall is 2 * 4 = 8mm, which of course equals the rainfall depth determined previously. This particular unit hydrograph for the basin will be for a 2-hour duration and will be denoted by UH2. The ordinates of the 2-hour unit hydrograph are obtained by dividing the direct runoff values given in Column (3) by 8.
Example: Given the unit hydrographic in Table below:
Time (hr) | 0 | 0.5 | 1.0 | 1.5 | 2.0 | 2.5 | 3.0
Storm Hydrograph (m3/sec) | 0 | 20 | 40 | 30 | 20 | 10 | 0
Determine the composite direct runoff hydrograph for the given rainfall pattern.

## Slide 6
Solution:
The given rainfall pattern consists of four segments of duration 1 heach and excess rainfall depths of 1.25, 1.25, 5, and 2.5mm. The hydrographs corresponding to the different segments of excess rainfall depths are calculated in Columns (2) to (5). The composite

## Slide 7
Time (hr) (1) | 1.25UH1 (m3/sec) (2) | 1.25UH1 (m3/sec) (3) | 5UH1 (m3/sec) (4) | 2.5UH1 (m3/sec) (5) | DRH m3/sec) (5)
0 | 0 |  |  |  | 0
0.5 | 25 |  |  |  | 25
1.0 | 50 | 0 |  |  | 50
1.5 | 37.5 | 25 |  |  | 62.5
2.0 | 25 | 50 | 0 |  | 75
2.5 | 12.5 | 37.5 | 100 |  | 150
3.0 | 0 | 25 | 200 | 0 | 225
3.5 |  | 12.5 | 150 | 50 | 212.5
4.0 |  | 0 | 100 | 100 | 200
4.5 |  |  | 50 | 75 | 125
5.0 |  |  | 0 | 50 | 50
5.5 |  |  |  | 25 | 25
6.0 |  |  |  | 0 | 0

## Slide 8
4.3 Unit Hydrographs of Different Duration
For a given unit hydrograph of a specific duration, another one with different duration can be derived for the same watershed by two methods.
Lagging Method
Using a unit hydrograph of duration a hours, another one with duration b hours can be obtained by lagging UHa by a hours as many as b/a times and superposing all these hydrographs together. The sum of these hydrographs must be divided by b/a to obtain UHb. This method requires b/a to be integer; therefore, this method is also called Integral Multiples Method.
Example: For the given 4 h unit hydrograph, obtain the 12 h unit hydrograph ordinates using the lagging method.

## Slide 10
S-hydrograph Method
For a storm with excess rainfall duration not being an integral multiple of the unit hydrograph, the S-hydrograph method can be used. S-hydrograph is a direct runoff hydrograph for a continuous rainfall duration and constant intensity.
Example: For the given 4 h unit hydrograph, obtain the 12 h unit hydrograph ordinates using the S-hydrograph method