## Slide 1
Water Resources Engineering
for 4th Class
By
Dr. Saad Shauket Sammen
Diyala University
College of Engineering
Department of Civil Engineering

## Slide 2
Example
Soil sample had the following data:- V=100cm3, γw=9800N/m3, WS = 1.45N, Rs= 2.6. find the apparent specific density and the porosity and the solid volume
Solution
V = VV + VS >>> VV = V – VS = 100 – 56.9 = 43.1 cm3

## Slide 3
Example
Soil sample has a dry weight 1.1N, total volume 75cm3, wet weight 1.3N, find soil water content as percentage by volume, dry weight, and wet weight
Solution
Pv = (Vw/V) × 100%, Ww = W – Ws = 1.3 – 1.1 = 0.2N,
Vw = (Ww/γw) = (0.2× 106/9800) = 20.4cm3, Pv = (20.4/75)× 100% = 27.2%
Pw= (Ww/Ws)× 100% = (0.2/1.1)× 100% = 18.2%
Pww= (Ww/W)× 100% = (0.2/1.3)× 100% = 15.2%

## Slide 4
Soil Moisture Behavior
When water is added to the soil by rain or irrigation, the soil surface becomes saturated, the pores are filled and the air is drawer out. The water then travels downwards under gravity and capillarity. If the water supply is discontinued water still tends to travel downwards through the soil, is drainage takes place. Water moves between two points if there is a force or potential gradient acting between them, the direction of flow being from the higher to the lower potential. In the soil, the potential acting on the moisture are:-
1-Nature potential due to capillary forces.
2-Osmotic potential due to dissolved salts in the water.
3-The gravity and pressure potential due to the position of the moisture with respect to a fixed datum level.
Classification of Soil Moisture (water)
Soil water can be divided into three categories:
(i) Gravity (or gravitational or free) water,
(ii) Capillary water, and
(iii) Hygroscopic water

## Slide 5
Gravity (or gravitational or free) water:-
is that water which drains away under the influence of gravity. Soon after irrigation (or rainfall) this water remains in the soil and saturates the soil, thus preventing circulation of air in void spaces. The upper limit of gravitational water is when the soil is saturated. The saturation capacity is then equal to the porosity of the soil which may be expressed as
Where: P: porosity % by volume
γS : density of the soil
γb : bulk density of the dry soil
Capillary Water:-
This water is held in the soil pores between the particles due to the surface tension forces (against gravity). The upper limit is when all the gravitational water has drained away. Soil in this state is said to be at field capacity.

## Slide 6
Hygroscopic Water:-
This Water attached to soil particles through loose chemical bonds and it is unavailable to the plant. But, the plant roots can use a very small fraction of this moisture under drought conditions.
Relationships between the various terms used in identifying classes and availability of soil water are shown in Figure below:

## Slide 7
Field Capacity:-
When gravitational water has been removed, the moisture content of the soil is called field capacity. In practices, field capacity is usually determined soil several days after an irrigation. Samples from the soil profile are taken initially and the moisture content determined by drying in an oven. The field capacity is found from the equation:-
Permanent Wilting Point (P.W.P):-
The soil – moisture content when plant´s permanently wilt is called the permanent wilting point. It is at the lower end of the available moisture rage. As an approximation, the permanent wilting point can be estimated as:-
Where: P.W.P: Permanent wilting point (percentage)
F.C: Field capacity

## Slide 8
F: Factor varying from 2.0 to 2.4 depending upon the amount of silt in the soil. (2 for low silt content and 2.4 for high silt content).
Available Moisture Content (A.M.C)
It is the moisture at field capacity minus that at permanent wilting point or:-
(A.M.C)W = F.C – P.W.P
Available moisture can be expressed as weight (eq. above), and as volume as:-
(A.M.C)W = (F.C – P.W.P)×A (where AS is the cross sectional area)
or as depth as:-
(A.M.C) = (F.C – P.W.P)×D (where D is the depth of the soil)
Readily Available Moisture Content (R.A.M.C)
Soil moisture content near the wilting point is not readily available to the plant. It has been used to refer to that portion of the available moisture that is most easily extract by plant, approximately 75 percent of available moisture or
R.A.M.C = 0.75 (A.M.C)