## Slide 1
AERODYNAMICS

## Slide 2: Contents
Aerodynamics: Some Introductory Thoughts
Aerodynamics: Some Fundamental Principles and Equations
Fundamentals of Inviscid, Incompressible Flow
Incompressible Flows Over Airfoils
Incompressible Flows Over Finite Wings

## Slide 3: Chap.1
Aerodynamics: Some Introductory Thoughts

## Slide 4: OUTLINE
Classification and practical objectives
Some fundamental aerodynamic variables
Aerodynamic forces and moments
Center of pressure
Dimensional analysis
Flow similarity
Types of flow

## Slide 5: Classification and practical objectives
Distinction between Solid and Fluid
Under application of shear force
  Solid: finite deformation
  Fluid: continuously increasing deformation
Classification of fluid dynamics
  Hydrodynamics: flow of liquids
  Gas dynamics: flow of gases
  Aerodynamics: flow of air

## Slide 6
Practical objectives of aerodynamics
  The prediction of forces and moments on, and heat transfer to, bodies moving through a fluid (usually air).
  Determination of flows moving internally through ducts. (ex. Flow properties inside rocket and air-breathing jet engines)

## Slide 7: Some fundamental aerodynamic variables
Pressure:
Density:
Temperature, T
Flow velocity, V

## Slide 8: Aerodynamic forces and moments
Aerodynamic forces and moments are due to
  Pressure distribution
  Shear stress distribution
Nomenclature
  R  resultant force
  L  lift
  D  drag
  N  normal force
  A  Axial force

## Slide 9
Relation between L,D and N,A
Representation of N´, A´and M´LE in terms of pressure p and shear stress 
  Primes denote force per unit span
  Subscript ‘u’ denote upper surface while ‘l’ denote lower surface

## Slide 11
Dimensionless force and moment coefficient
  S = reference area ( planform area for wing)
  l = reference length (chord length for wing)
  Dynamic pressure
  Lift coefficient
  Drag coefficient
  Normal force coefficient
  Axial force coefficient
  Moment coefficient

## Slide 12: Center of pressure
Definition
  The point on the body about which the aerodynamic moment is zero.
Location of center of pressure
  , if  is small 

## Slide 13: Dimensional analysis
Factors affecting aerodynamic force R
  Free stream velocity V
  Free stream density 
  Viscosity of the fluid 
  The size of the body (usually represented by the chord length c)
  The compressibility of the fluid a
R=f(, V, c, , a). Dimensional analysis can reduce the number of independent parameters affecting R, such that can save the cost of wind tunnel test.

## Slide 14
Buckingham pi theorem
  Fundamental dimensions :
    m = dimension of mass
    l = dimension of length
    t = dimension of time
  Variables and their dimensions

## Slide 15
   products
  For 1, assume that
  Equating the exponents sum of m to be zero, and similarly for l and t, we can obtain simultaneous equations of b, d, e, solving these equations leads to

## Slide 16
  b = -2, d = -1, e = -2.
  Results form 1
  Similarly for 2
  Re, Reynolds number, is a measure of the ratio of inertial forces to viscous forces in a flow.

## Slide 17
  For 3
  M, Mach number, is the ratio of the flow velocity to the speed of sound.
  CR (also for CL, CD, CM) is function of Re and M.
  Re and M are called similarity parameters.

## Slide 18: Flow similarity
Definition of dynamically similar for two different flows
  The streamline patterns are geometrically similar.
  The distributions of V/V, p/p, etc. are the same when plotted against common non-dimensional coordinates.
  The force coefficients are the same.
Criteria
  The bodies and any other solid boundaries are geometrically similar.
  Same similarity parameters (Re and M).

## Slide 19
Example
  Assume
  Similar flows

## Slide 20: Types of flow
Inviscid vs. viscous flow
  Inviscid: assume no friction, thermal conduction and diffusion.
  viscous: consider effects of friction, thermal conduction and diffusion.
Incompressible vs. compressible
  Incompressible: density  is constant.
  Compressible: density  is variable.

## Slide 21
Mach number regimes
  Subsonic flow: M<1 everywhere
  Transonic flow: mixed regions where M<1 and M>1
  Supersonic flow: M>1 everywhere
  Hypersonic flow: very high supersonic speeds, usually M>5.

## Slide 22: Chap.2
Aerodynamics: Some Fundamental Principles and Equations

## Slide 23: OUTLINE
Review of vector relations
Control volumes and fluid elements
Continuity equation
Momentum equation
Pathlines and streamlines
Angular velocity, vorticity and circulation
Stream function and velocity potential

## Slide 24: Review of vector relations
Vector algebra
  Scalar product:
  Vector product:

## Slide 25
Orthogonal coordinate systems
  Cartesian coordinate system

## Slide 26
  Cylindrical coordinate system

## Slide 27
  Spherical coordinate system

## Slide 28
Gradient of a scalar field
  Definition of gradient of a scalar p
    Its magnitude is the maximum rate of change of p per unit length.
    Its direction is the maximum rate of change of p.
  Isoline: a line of constant p values
  Gradient line: a line along which p is tangent at every point.
  Directional derivative:
  where n is the unit vector in the s direction.

## Slide 29
  Expression for p in Cartesian coordinate system

## Slide 30
Divergence of a vector field
  If V is the velocity of a flow, the divergence of V will be the time rate of volume change per unit volume.
  Expression for divergence of V, V, in Cartesian coordinate system

## Slide 31
Curl of a vector field
  The angular velocity  of a fluid element translating along a streamline is equal to one-half of the curl of V, denoted by V.
  Expression for curl of V in Cartesian coordinate system

## Slide 32
Relations between line, surface and volume integrals
  Stokes’ theorem
  Divergence theorem
  Gradient theorem

## Slide 33: Control volumes and fluid elements
Control volume approach
Fluid element approach

## Slide 34: Continuity equation
Fixed control volume
Mass flow equation
Continuity equation in a finite space
Continuity equation at a point

## Slide 35: Momentum equation
Fixed control volume
Original form is Newton’s second law
Momentum equation in integral form
  f is body force; Fviscous is viscous force on control surface
X-component of the momentum equation in differential form (similar form for y- and z-component).

## Slide 36
Navier-Stokes equations
  The momentum equations for a viscous flow.
Euler equations
  The momentum equations for a steady inviscid flow.

## Slide 37: Pathlines and streamlines
Pathline
  Path of a fluid element.
Streamline
  A curve whose tangent at any point is in the direction of the velocity vector at that point.
For steady flow, pathlines and streamlines are identical.

## Slide 38
Streamline equation for steady flow
  By definition, flow velocity V is parallel to directed segment of the streamline ds, so dsxV=0
  For two-dimensional flow

## Slide 39: Angular velocity, vorticity and circulation
Angular velocity and vorticity
  As a fluid element translate along a streamline, it may rotate as well as shape distorted.
  Angular velocity 
  Vorticity  is defined to be 2, also equal to xV.
  If xV≠0, the flow is rotational, and ≠0.
  If xV=0, the flow is irrotational, and =0.

## Slide 40
Circulation Γ
  Definition
  Relation with lift: if an airfoil is generating lift, the circulation taken around a closed curve enclosing the airfoil will be finite.
  By Stokes’ theorem

## Slide 41
  If the flow is irrotational (xV=0) everywhere with the contour of integration, then Γ= 0.

## Slide 42: Stream function and velocity potential
Stream function
  For two-dimensional steady flow, a streamline equation is given by setting the stream function equal to a contant.
  For incompressible flow

## Slide 43
Velocity potential
  For an irrotational flow
  We can find a scalar function φ such that V is given by the gradient of φ which is therefore called velocity potential.

## Slide 44
Relation between  and φ
  Equipotential lines (φ= constant) and streamlines ( = constant) are mutually prependicular.

## Slide 45: Chap.3
Fundamentals of Inviscid, Incompressible Flow

## Slide 46: OUTLINE
Bernoulli’s equation and its application
Pressure coefficient
Laplace’s equation for irrotational, incompressible flow
Elementary flows
Combination of elementary flows

## Slide 47: Bernoulli’s equation and its application
Bernoulli’s equation
  Relation between pressure and velocity in an inviscid, incompressible flow.
  Equation form along a streamline
  If the flow is irrotational,
  throughout the flow

## Slide 48
Flow in a duct
  Continuity equation for quasi-one-dimensional flow in a duct
  For incompressible flow

## Slide 49
The venturi and low-speed wind tunnel
  In aerodynamic application, venturi can be used to measure the velocity of inlet flow V1.
  From Bernoulli’s equation:

## Slide 50
  A low-speed wind tunnel is a large venturi where the airflow is driven by a fan.
  The test section flow velocity can be derived from Bernoulli’s equation

## Slide 51
Pitto tube
  Stagnation point: a point in a flow where V = 0. (ex. Point B in the figure.)
  Stagnation pressure p0: pressure at a stagnation point, also called total pressure.
  To measure the flight velocity of an airplane.

## Slide 52: Pressure coefficient
Pressure coefficient is defined as
where
For incompressible flow
  Cp can be reduced to be in terms of velocity only.

## Slide 53: Laplace’s equation for irrotational, incompressible flow
For incompressible flow
For irrotational flow ( is velocity potential)
Laplace’s equation
The stream function  also satisfies Laplace’s equation.

## Slide 54
Solution of Laplace’s equation
  Solutions of Laplace’s equation are called harmonic functions.
  Superposition principle is applicable since Laplace’s equation is linear.
  A complicated flow pattern can be synthesized by adding together a number of elementary flows.

## Slide 55
Boundary contions
  Infinity boundary conditions
  Wall boundary conditions (wall tangency conditions)

## Slide 56: Elementary flows
Uniform flow
  A uniform flow is a physically possible incompressible and irrotational flow.
  Boundary condition for 
  Solution for 

## Slide 57
  Boundary condition for 
  Solution for 

## Slide 58
Source flow
  Cylindrical coordinate system is applied.
  Incompressible at every point except the origin.
  Irrotational at every point.
  Velocity field
  where  is the source strength, defined as the volume flow rate per unit length.

## Slide 59
   is positive for a source flow, whereas negative for a sink flow.
  Solution for  and 

## Slide 60
Doublet flow
  A pair of source-sink with the same strength, while the distance l between each other tends to zero.
  Stream function 
  where =const. is the strength of the doublet.

## Slide 61
  Solution for  and 
  The direction of a doublet is designated by an arrow draw form the sink to the source.

## Slide 62
Vortex flow
  A flow where all the streamlines are concentric circles, and the velocity along any circular streamline is constant.
  Incompressible at every point.
  Irrotational at every point except the origin.

## Slide 63
  Velocity field
  where  is the circulation.
  Solution for  and 

## Slide 64: Combination of elementary flows
Superposition of a uniform flow and a source
  Stream function 

## Slide 65
  Velocity field
  Stagnation point
  The streamline goes through the stagnation point is described by =/2, shown as curve ABC .

## Slide 66
  Streamline ABC separates the fluid coming from the free stream and the fluid emanating from the source.
  The entire region inside ABC could be replaced with a solid body of the same shape.

## Slide 67
Superposition of a uniform flow and a source-sink pair
  Stream function 

## Slide 68
  Two stagnation points A and B are found by setting V=0.
  The stagnation streamline is given by =0, i.e.
  which is the equation of an oval, called Rankine oval.
  The region inside the oval can be replaced by a solid body with the same shape.

## Slide 69
Nonlifting flow over a circular cylinder
  Superposition of a uniform flow and a doublet
  Stream function 

## Slide 70
  Velocity field
  The stagnation streamline is given by =0, i.e.
  The stagnation streamline includes the circle described by r=R, and the entire horizontal axis through points A and B.

## Slide 71
  We can replace the flow inside the circle by a solid body. Consequently, a flow over a circular cylindrical of radius R can be synthesized by this superposition, where
  The pressure distribution is symmetric about both axes. As a result, there is no net lift, as well as no net drag which makes no sense in real world.

## Slide 72: Chap.4
Incompressible Flow over Airfoils

## Slide 73: OUTLINE
Airfoil nomenclature and characteristics
The vortex sheet
The Kutta condition
Kelvin’s circulation theorem
Classical thin airfoil theory
The cambered airfoil
The vortex panel numerical method

## Slide 74: Airfoil nomenclature and characteristics
Nomenclature

## Slide 75
Characteristics

## Slide 76: The vortex sheet
Vortex sheet with strength =(s)
  Velocity at P induced by a small section of vortex sheet of strength ds
  For velocity potential (to avoid vector addition as for velocity)

## Slide 77
  The velocity potential at P due to entire vortex sheet
  The circulation around the vortex sheet
  The local jump in tangential velocity across the vortex sheet is equal to .

## Slide 78
  Calculate (s) such that the induced velocity field when added to V will make the vortex sheet (hence the airfoil surface) a streamline of the flow.
  The resulting lift is given by Kutta-Joukowski theorem
  Thin airfoil approximation

## Slide 79: The Kutta condition
Statement of the Kutta condition
  The value of  around the airfoil is such that the flow leaves the trailing edge smoothly.
  If the trailing edge angle is finite, then the trailing edge is a stagnation point.
  If the trailing edge is cusped, then the velocity leaving the top and bottom surface at the trailing edge are finite and equal.
  Expression in terms of 

## Slide 80: Kelvin’s circulation theorem
Statement of Kelvin’s circulation theorem
  The time rate of change of circulation around a closed curve consisting of the same fluid elements is zero.

## Slide 81: Classical thin airfoil theory
Goal
  To calculate (s) such that the camber line becomes a streamline.
  Kutta condition (TE)=0 is satisfied.
  Calculate  around the airfoil.
  Calculate the lift via the Kutta-Joukowski theorem.

## Slide 82
Approach
  Place the vortex sheet on the chord line, whereas determine =(x) to make camber line be a streamline.
  Condition for camber line to be a streamline
  where w'(s) is the component of velocity normal to the camber line.

## Slide 83
  Expression of V,n
  For small 

## Slide 84
  Expression for w(x)
  Fundamental equation of thin airfoil theory

## Slide 85
For symmetric airfoil (dz/dx=0)
  Fundamental equation for ()
  Transformation of , x into 
  Solution

## Slide 86
  Check on Kutta condition by L’Hospital’s rule
  Total circulation around the airfoil
  Lift per unit span

## Slide 87
  Lift coefficient and lift slope
  Moment about leading edge and moment coefficient

## Slide 88
  Moment coefficient about quarter-chord
  For symmetric airfoil, the quarter-chord point is both the center of pressure and the aerodynamic center.

## Slide 89: The cambered airfoil
Approach
  Fundamental equation
  Solution
  Coefficients A0 and An

## Slide 90
Aerodynamic coefficients
  Lift coefficient and slope
  Form thin airfoil theory, the lift slope is always 2 for any shape airfoil.
  Thin airfoil theory also provides a means to predict the angle of zero lift.

## Slide 91
  Moment coefficients
  For cambered airfoil, the quarter-chord point is not the center of pressure, but still is the theoretical location of the aerodynamic center.

## Slide 92
  The location of the center of pressure
  Since
  the center of pressure is not convenient for drawing the force system. Rather, the aerodynamic center is more convenient.
  The location of aerodynamic center

## Slide 93: The vortex panel numerical method
Why to use this method
  For airfoil thickness larger than 12%, or high angle of attack, results from thin airfoil theory are not good enough to agree with the experimental data.
Approach
  Approximate the
  airfoil surface by
  a series of straight
  panels with strength
  which is to be
  determined.

## Slide 94
  The velocity potential induced at P due to the j th panel is
  The total potential at P
  Put P at the control point of i th panel

## Slide 95
  The normal component of the velocity is zero at the control points, i.e.
  We then have n linear algebraic equation with n unknowns.

## Slide 96
  Kutta condition
  To impose the Kutta condition, we choose to ignore one of the control points.
  The need to ignore one of the control points introduces some arbitrariness in the numerical solution.

## Slide 97: Chap.5
Incompressible Flow over Finite Wings

## Slide 98: OUTLINE
Downwash and induced drag
The Biot-Savart law and Helmholtz’s theorems
Prandtl’s classical Lifting-line theory
Elliptical lift distribution
General lift distribution

## Slide 99: Downwash and induced drag
Aerodynamic difference between finite wing and airfoil
  For finite wing, the flow near wing tips tends to curl around the tip, being forced from the high- pressure just underneath the tips to the low- pressure region on top.

## Slide 100
  Due to the spanwsie component of flow from tip toward to root, the streamlines over the top surface are bent toward root. In contrast, the streamlines over bottom surface toward tip.
  A trailing vortex is created at each win tip.

## Slide 101
Effect of downwash
  Wing-tip vortices downstream of the wing induce a small component of air velocity, called downwash which is denoted by the symbol w.
  Downwash causes inclining the local relative wind in the downward direction.

## Slide 102
  Effective angle of attack
  The tilting backward of the lift vector induce a drag, called induced drag Di which is a type of pressure drag.
  Total drag = Profile drag + Induce drag, therefore

## Slide 103: The Biot-Savart law and Helmholtz’s theorems
The Biot-Savart law
  The velocity at point P, dV, induced by a small directed segment dl of a curved filament with strength  is
  The velocity at P by a
  straight vortex filament
  of infinite length is

## Slide 104
  The magnitude of V
  The velocity at P by a semi-infinite vortex filament

## Slide 105
Holmholtz’s vortex theorem
  The strength of a vortex filament is constant along its length.
  A vortex filament cannot end in a fluid; it must extend to the boundaries of the fluid (which can be ) or form a closed path.
Lift distribution
  Different airfoil sections may have geometric and aerodynamic twist, that results in a lift distribution along the span.

## Slide 106: Prandtl’s classical Lifting-line theory
Horseshoe vortex
  Horseshoe vortex consists of a bound vortex and two free vortex.
  The bound vortex induces no velocity along itself, however, the two free vortices contribute to the downward velocity along the bound vortex.

## Slide 107
Downwash
  Downwash at point y along the bound vortex is

## Slide 108
Lifting-line theory
  Instead of a single horseshoe vortex, infinite number of horseshoe vortices with a vanishing small strength d are superimposed to form the bound vortices a single line which is called lifting line.

## Slide 109
  The trailing vortices become a continuous vortex sheet trailing downstream of the lifting line.
  The velocity w induced at y0 by the entire trailing vortex sheet is
  The induce angle of attack is

## Slide 110
  The lift coefficient at y=y0 is
  From the Kutta-Joukowski theorem, lift for the local airfoil section located at y0 is
  Expression of effective angle of attack

## Slide 111
  Fundamental equation of Prandtl’s lifting-line theory (integro-differential equation of )
  The solution  gives the three main aerodynamic characteristics of a finite wing

## Slide 112
  The lift distribution
  The lift coefficient
  The induced drag coefficient

## Slide 113: Elliptical lift distribution
Charateristic
  Elliptical circulation distribution
  where 0 is the circulation at the origin.
  Elliptical lift distribution
  Zero lift at the wing tips

## Slide 114
Resulting aerodynamic properties
  By using the transformation y=b/2 cos, we obtain
  which states that downwash is constant over the span for an elliptical lift distribution.
  Induced angle of attack

## Slide 115
  Induced drag coefficient
  which states that CD,I is proportional to the square of CL and inversely proportional to AR.
  For an elliptical lift distribution, the chord must vary elliptically along the span; that is, the wing planform is elliptical.

## Slide 116: General lift distribution
Characteristic
  Consider the transformation
  and assume
  Fundamental equation at a given location

## Slide 117
  We may choose N different spanwise stations, then we can obtain N independent algebraic equations with N unknowns, namely, A1, A2, AN.
Resulting aerodynamic properties
  Lifting coefficient
  Induced drag coefficient

## Slide 118
  Define span efficiency factor e
  Note that =0 and e=1 for the elliptical lift distribution. Hence, the lift distribution which yields minimum induced drag is the elliptical lift distribution.