## Slide 1
University of Diyala College of Engineering
Department of Communications Engineering
Electronics II: 3ed Year - 2015/2016 By: Hussein Ahmed Mahmood
GENERAL FREQUENCY CONSIDERATIONS
Typical Frequency Response
The magnitudes of the gain response curves of an RC-coupled and direct- coupled, amplifier system are provided in Fig. 1. Note that the horizontal scale is a logarithmic scale to permit a plot extending from the low to the high frequency regions. For each plot, a low, a high, and a mid-frequency region have been defined. For the RC-coupled amplifier, the drop at low frequencies is due to the increasing reactance of CC, CS, or CE, whereas it’s upper frequency limit is determined by either the parasitic capacitive elements of the network or the frequency dependence of the gain of the active device. For the direct-coupled amplifier, there are no coupling or bypass capacitors to cause a drop in gain at low frequencies. As the figure indicates, it is a flat response to the upper cutoff frequency.
Frequency Response of Amplifiers:
  Terms and Definitions
In real amplifiers, gain changes with frequency. “Frequency response" is changing the Voltage gain (amplitude& phase) withe frequency:
Both |AV| and ∟AV are functions of frequency and can be plotted.

## Slide 2
University of Diyala College of Engineering
Department of Communications Engineering
Electronics II: 3ed Year - 2015/2016 By: Hussein Ahmed Mahmood
Magnitude Response:
A plot of |AV| is called the magnitude response of the amplifier.
Phase Response:
A plot of ∟AV is called the phase response of the amplifier.
Frequency Response:
Taken together the two responses are called the frequency response.
Fig.1
Gain versus frequency: (a) RC-coupled amplifiers; (b) direct-coupled amplifiers

## Slide 3
University of Diyala College of Engineering
Department of Communications Engineering
Electronics II: 3ed Year - 2015/2016 By: Hussein Ahmed Mahmood
For each system of Fig.1, there is a band of frequencies in which the magnitude of the gain is either equal or relatively close to the midband value. To fix the frequency boundaries of relatively high gain, 0.707AV mid was chosen to be the gain at the cutoff levels. The corresponding frequencies f1 and f2 are generally called the corner, cutoff, band, break, or half-power frequencies. The multiplier 0.707 was chosen because at this level the output power is half the midband power output, that is, at midfrequencies,
And at the half-power frequencies,
And
The bandwidth (or passband) of each system is determined by fH and fL, that is,
With fH and fL defined in each curve of Fig. 1.