## Slide 1: Chemical Process Industries University of Diyala Chemical Engineering Department
Lecture (2)
د. أديبة النعيمي

## Slide 2: Raw materials
The primary raw materials and future energy and chemical sources: Natural gas and crude oils are the basic raw materials for the manufacture of petrochemicals.

## Slide 3
Secondary raw materials, are obtained from natural gas and crude oils through different processing schemes. The intermediates may be light hydrocarbon compounds such as methane and ethane, or heavier hydrocarbon mixtures such as naphtha or gas oil. Both naphtha and gas oil are crude oil fractions with different boiling ranges.

## Slide 4
Two petrochemical classes are olefins including ethylene and propylene, and
aromatics including benzene, toluene and xylene isomers.

## Slide 5
Oil refineries produce olefins and aromatics by fluid catalytic cracking of petroleum fractions. Chemical plants produce olefins by steam cracking of natural gas liquids like ethane and propane.

## Slide 6
Aromatics are produced by catalytic reforming of naphtha. Olefins and aromatics are the building blocks for a wide range of materials such as solvents, detergents, and
adhesives. Olefins are the basis for polymers and oligomers used in plastics, resins, fibers, elastomers, lubricants, and gels.

## Slide 7
  Benzene is a raw material for dyes and synthetic detergents, benzene and toluene raw material for isocyanates MDI and TDI used in making polyurethanes. Manufacturers use xylenes to produce plastics and synthetic fibers.

## Slide 8
  Synthesis gas is a mixture of carbon monoxide and hydrogen used to make ammonia and methanol. Ammonia is used to make the fertilizer, urea and methanol is used as a solvent and chemical intermediate.

## Slide 9
Practical design of steam cracking and operating conditions depends on feed.
If the raw material: Ethane-gas oil :then operating conditions are:

## Slide 10
Temp:750-850 oC
Residence time(RT)=0.2-0.3 sec. Steam: feed 0.2-1 Pressure:1-3 bar.