## Slide 1: Chemical Process Industries University of Diyala Chemical Engineering Department
Lecture (7)
د. أديبة النعيمي

## Slide 2
Liquid feed: cooling is carried out first using direct wash with oil such as gas oil
then fractional distillation is carried out to for fuel oil separation from heavy gasoline
fraction. During direct washing products temp. decrease to 200-220oC then products
are introduced to primary disitlation tower to separate fuel oil and washing gas ,temp.
of product is reduced to about 100-1100C,Final cooling is about 40oC.

## Slide 3
Third:Compression:
Pyro.gas contains some impurities with different concentrations differs according to
feed type and operating conditions. Impurities are acids gases(H2S,CO2) ,acetylene
and water

## Slide 4
The compression of gas to 34 atm. occur in multi stages (4-5).condense HCS are
removed from these stages. Acids gases removal is usually carried out during
compression using soda or amine wash unit, then gas is dried to prevent hydride and
ice formation when the gas is cooled to low temp. during the distillation under
pressure

## Slide 5
Fourth: Acid gases removal:
Purity requirement in low olefins need to reduce the contain of H2S(1-2)ppm and
CO2(10-15) ppm.

## Slide 6
Resonces for acid gas removal:
1-To avoid corrosion problems, and limit solid CO2 precipitation at low temp. 2-
Prevent catalyst (pd) poisoning. Catalyst is used in acetylene hydrogenation.

## Slide 7
Washing process :
Treated gas from the second stage is washed with water in a separated region in a
tower contain several trays for contact .The water is recycle with different speed to
obtained effective washing of gas from residual soda and impurities.