## Slide 1: Chemical Process Industries University of Diyala Chemical Engineering Department
Lecture (5)
د. أديبة النعيمي

## Slide 2
Polymer-grade propylene is recovered in a propylene fractionators (13)
- Methylacetylene and propadiene are hydrogenated in the depropanizer using CD
Hydro catalytic distillation hydrogenation technology. The depropanizer bottoms is
separated into mixed C4 and light gasoline streams (14).

## Slide 4: First: Steam cracking process:
treatment of HCS with steam at high temp and low contact time and pressure.:
8
Mechanism:
1- Dehydrogenation of ethane:
CH3-CH3→CH2=CH2
Ethane Ethylene
CH3CH2CH3 → CH2=CH2+ CH4
Propane Ethylene

## Slide 5
2-Dehydrogenation of propane:
CH3CH2CH3 → CH2=CHCH3+ H2
Furnace design:

## Slide 6: Furnace design:
Furnaces: tubular furnace: tube arranged either vertical or horizontal, and made of
S.S: which is alloy of nickel and chrome and contain burners mounted in the bottom
or on a side of these furnace. NG, reduced crude or fuel oil burns to give heat.

## Slide 7: Operating conditions(OC):
Practical design of steam cracking and operating conditions depends on feed.
If the raw material: Ethane-gas oil :then operating conditions are: Temp:750-850 oC
Residence time(RT)=0.2-0.3 sec. Steam: feed 0.2-1 Pressure:1-3 bar.