## Slide 1
HYDROSTATIC FORCES ON SUBMERGED CURVED SURFACES
For a submerged curved surface, the determination of the resultant hydrostatic force is more involved since it typically requires the integration of the pressure forces that change direction along the curved surface. The easiest way to determine the resultant hydrostatic force FR acting on a two-dimensional curved surface is to determine the horizontal and vertical components FH and FV separately. This is done by considering the free-body diagram of the liquid block enclosed by the curved surface and the two plane surfaces (one horizontal and one vertical) passing through the two
ends of the curved surface, as shown in Fig. 1.
Liquid
Horizontal projection
of the curved surface
Vertical projection
of the curved surface
Curved
surface
Free-body diagram
of the enc osed
liquid block
Figure 1: Determination of the hydrostatic force acting on a submerged curved surface.
The force acting on the imaginary horizontal or vertical plane surface and its line of action can be determined as discussed before. The weight of the enclosed liquid block of volume V is simply W = pgV, and it acts downward through the centroid of this volume. Noting that the fluid block is in static equilibrium, the force balances in the horizontal and vertical directions give.
Horizontal force component on curved surface: FH = Fx
Vertical force component on curved surface: Fv = Fy + W
1

## Slide 2
where the summation Fy + W is a vector addition (i.e., add magnitudes if both act in the same direction and subtract if they act in opposite directions). Thus, we conclude that The magnitude of the resultant hydrostatic force acting on the curved surface is FR = ^Fy + Ffi, and the tangent of the angle it makes with the horizontal is tan a = FV /FH. The exact location of the line of action of the resultant force (e.g., its distance from one of the end points of the curved surface) can be determined by taking a moment about an appropriate point. These discussions are valid for all curved surfaces regardless of whether they are above or below the liquid. Note that in the case of a curved surface above a liquid, the weight of the liquid is subtracted from the vertical component of the hydrostatic force since they act in opposite directions (Fig.2).
weight of the liquid and the vertical component of the hydrostatic force act in the opposite directions.
2

## Slide 3
EXAMPLE3-9 A Gravity-Controlled Cylindrical Gate
A long solid cylinder of radius 0.8 m hinged at point A is used as an automatic gate, as shown in Fig. 3-36. When the water level reaches 5 m, the gate opens by turning about the hinge at point A. Determine (a) the hydrostatic force acting on the cylinder and its line of action when the gate opens and (b) the weight of the cylinder per m length of the cylinder.
SOLUTION The height of a water reservoir is controlled by a cylindrical gate hinged to the reservoir. The hydrostatic force on the cylinder and the weight of the cylinder per m length are to be determined.
Assumptions 1 Friction at the hinge is negligible. 2 Atmospheric pressure acts on both sides of the gate, and thus it cancels out.
Properties We take the density of water to be 1000 kg/m3 throughout. Analysis (a) We consider the free-body diagram of the liquid block enclosed by the circular surface of the cylinder and its vertical and horizontal projections. The hydrostatic forces acting on the vertical and horizontal plane surfaces as well as the weight of the liquid block are determined as Horizontal force on vertical surface:
3

## Slide 4
5 m
0.8 m
FIGURE 3-36
Schematic tor Example 3-9 and
the tree-body diagram of the fluid
underneath the cylinder.
Weight of fluid block per m length (downward):
W = mg = pgl/ = pg(R2 - 7TRV4)(1 m)
1 kN
= (1000 kg/m )(9.81 m/s£)(0.8 m)"(1 - m)
1000 kg • m/s
Therefore, the net upward vertical force is
Then the magnitude and direction of the hydrostatic force acting on the
cylindrical surface become
FR = VFH + F; = V36.r + 37.9 = 52.3 kN
tan 0 = RTF,, = 37.9/36.1 = 1.05
0 = 46.4
Therefore, the magnitude of the hydrostatic force acting on the cylinder is
52.3 kN per m length of the cylinder, and its line of action passes through
the center of the cylinder making an angle 46.4 with the horizontal.
(b) When the water level is 5 m high, the gate is about to open and thus the
reaction force at the bottom of the cylinder is zero. Then the forces other
than those at the hinge acting on the cylinder are its weight, acting through
the center, and the hydrostatic force exerted by water. Taking a moment
about point A at the location of the hinge and equating it to zero gives
FrR sin 0 - Wcvi R = 0 -» W™. = Fs sin 9 = (52.3 kN) sin 46.4 = 37.9 kN
Discussion The weight of the cylinder per m length is determined to be
37.9 kN.
can be shown that this corresponds to a mass of 3863 kg per m
length and to a density of 1921 kg/m3 for the material of the cylinder.
Reference:
Cimbala, John M., and Yunus A. £engel. Essentials of fluid mechanics: fundamentals and applications. McGraw-Hill Higher Education, 2008.
4