## Slide 1
THE BERNOULLI EQUATION
The Bernoulli equation is an approximate relation between pressure, velocity, and elevation, and is valid in regions of steady, incompressible flow where net frictional forces are negligible (Fig. 1). Despite its simplicity, it has proven to be a very powerful tool in fluid mechanics. In this section, we derive the Bernoulli equation by applying the conservation of linear momentum principle.
Figure 1: The Bernoulli equation is an approximate equation that is valid only in inviscid regions of flow where net viscous forces are negligibly small compared to inertial, gravitational, or pressure forces. Such regions occur outside of boundary layers and wakes.
Derivation of the Bernoulli Equation
Consider the motion of a fluid particle in a flow field in steady flow described in detail previously. Applying Newton’s second law (which is referred to as the conservation of linear momentum relation in fluid mechanics) in the s-direction on a particle moving along a streamline gives
(5-35)
Figure 2: The forces acting on a fluid particle along a streamline.
1

## Slide 2
In regions of flow where net frictional forces are negligible, the significant forces acting in the ^-direction are the pressure (acting on both sides) and the component of the weight of the particle in the ^-direction (Fig. 2).Therefore, Eq. 5-35 becomes
P dA - (P + dP) dA - W sin 0 = mV
dV
ds
(5-36)
where 6 is the angle between the normal of the streamline and the vertical z-axis at that point, m = pW = p dA ds is the mass, W = mg = pg dA ds is the weight of the fluid particle, and sin 0 = dz/ds. Substituting,
-dP dA - pg dA ds ^ = p dA ds V ^
's ds r ds
Canceling dA from each term and simplifying,
-dP - pg dz = pV dV
Noting that V dV = \ d(V2) and dividing each term by p gives
dP
(5-37)
(5-38)
— + jd(V2) + g dz = 0
(5-39)
Integrating (Fig. 5-24),
, dP V2
Steady flow:
— + — + gz = constant (along a streamline)
(5-40)
since the last two terms are exact differentials. In the case of incompressible flow, the first term also becomes an exact differential, and its integration gives
P V2
Steady, incompressible flow: — + — + gz = constant (along a streamline) (5^tD
This is the famous Bernoulli equation, which is commonly used in fluid mechanics for steady, incompressible flow along a streamline in inviscid
2

## Slide 3
Figure 3: The Bernoulli equation is derived assuming incompressible flow, and thus it should not be used for flows with significant compressibility effects.
The Bernoulli equation can also be written between any two points on the same streamline as
P V2 P V2
Steady, incompressible flow: —1 H—-1 -h gzn = — + —- + gz2 (5^2)
Conclusions about Bernoulli equation:
The sum of the kinetic, potential, and flow energies of a fluid particle is constant along a streamline during steady flow when the compressibility and frictional effects are negligible.
Static, Dynamic, and Stagnation Pressures
The Bernoulli equation states that the sum of the flow, kinetic, and potential energies of a fluid particle along a streamline is constant. Therefore, the kinetic and potential energies of the fluid can be converted to flow energy (and vice versa) during flow, causing the pressure to change. This phenomenon can be made more visible by multiplying the Bernoulli equation by the density p,
V2
P + p— + pgz = constant (along a streamline)
(5-45)
Each term in this equation has pressure units, and thus each term represents some kind of pressure:
3

## Slide 4
• P is the static pressure (it does not incorporate any dynamic effects); it represents the actual thermodynamic pressure of the fluid. This is the same as the pressure used in thermodynamics and property tables.
• pV2/2 is the dynamic pressure; it represents the pressure rise when the fluid in motion is brought to a stop isentropically.
• pgz is the hydrostatic pressure, which is not pressure in a real sense since its value depends on the reference level selected; it accounts for the elevation effects, i.e., of fluid weight on pressure.
The sum of the static, dynamic, and hydrostatic pressures is called the total pressure. Therefore, the Bernoulli equation states that the total pressure along a streamline is constant.
The sum of the static and dynamic pressures is called the stagnation pressure, and it is expressed as
V2
P sLan = P + P— (kPa) (5-4&)
The stagnation pressure represents the pressure at a point where the fluid is brought to a complete stop isentropically. The static, dynamic, and stagnation pressures are shown in Fig. 5. When static and stagnation pressures are measured at a specified location, the fluid velocity at that location can be calculated from
V =
2(Ps,g - PI
\ P
Figure 5: The static, dynamic, and stagnation pressures.
Figure 4: Close-up of a Pitot-static probe, showing the stagnation pressure hole and two of the five static circumferential pressure holes. Photo by Po-Ya Abel Chuang. Used by permission.
Equation 5-47 is useful in the measurement of flow velocity when a combination of a static pressure tap and a Pitot tube is used, as illustrated in Fig.5 &4. A static pressure tap is simply a small hole drilled into a wall such that the plane of the hole is parallel to the flow direction. It measures the static pressure. A Pitot tube is a small tube with its open end aligned into the flow so as to sense the full impact pressure of the flowing fluid.
4

## Slide 5
Limitations on the Use of the Bernoulli Equation
The Bernoulli equation (Eq. 5-41) is one of the most frequently used and misused equations in fluid mechanics.
It is important to understand the restrictions on its applicability and observe the limitations on its use, as explained here:
1. Steady flow: The first limitation on the Bernoulli equation is that it is applicable to steady flow. Therefore, it should not be used during the transient start-up and shut-down periods, or during periods of change in the flow conditions.
2. Frictionless flow: Every flow involves some friction, no matter how small, and frictional effects may or may not be negligible. The situation is complicated even more by the amount of error that can be tolerated. In
general, frictional effects are negligible for short flow sections with large cross sections, especially at low flow velocities.
3. No shaft work: The Bernoulli equation was derived from a force balance on a particle moving along a streamline. Therefore, the Bernoulli equation is not applicable in a flow section that involves a pump, turbine, fan, or any other machine or impeller since such devices destroy the streamlines and carry out energy interactions with the fluid particles.
4. Incompressible flow: One of the assumptions used in the derivation of the Bernoulli equation is that p = constant and thus the flow is incompressible. This condition is satisfied by liquids and also by gases at Mach numbers less than about 0.3 since compressibility effects and thus density variations of gases are negligible at such relatively low velocities.
5. No heat transfer: The density of a gas is inversely proportional to temperature, and thus the Bernoulli equation should not be used for flow sections that involve significant temperature change such as heating or cooling sections.
6. Flow along a streamline: Strictly speaking, the Bernoulli equation P/p +V2/2 + gz = C is applicable along a streamline, and the value of the constant C, in general, is different for different streamlines. But when a region of the flow is irrotational, and thus there is no vorticity in the flow field, the value of the constant C remains the same for all streamlines, and, therefore, the Bernoulli equation becomes applicable across streamlines as well.
Sudden
expansion
© rVvVi ©
Figure 6: Frictional effects and components that disturb the streamlined structure of flow in a flow section make the Bernoulli equation invalid.
A heating section

## Slide 6
Hydraulic Grade Line (HGL) and Energy Grade Line (EGL)
It is often convenient to represent the level of mechanical energy graphically using heights to facilitate visualization of the various terms of the Bernoulli equation. This is done by dividing each term of the Bernoulli equation by g to give
P V2
— + — + z = H = constant falonq a streamline) (5^4&)
Each term in this equation has the dimension of length and represents some kind of "head" of a flowing fluid as follows:
■ P/pg is the pressure head; it represents the height of a fluid column that produces the static pressure P.
* V2/2g is the velocity head; it represents the elevation needed for a fluid to reach the velocity V during frictionless free fall.
■ z is the elevation head; it represents the potential energy of the fluid.
Figure 7: The hydraulic grade line (HGL) and the energy grade line (EGL) for free discharge from a reservoir through a horizontal pipe with a diffuser.
The line that represents the sum of the static pressure and the elevation heads, P/pg + z, is called the hydraulic grade line. The line that represents the total head of the fluid, P/pg + V2/2g + z, is called the energy grade line. The difference between the heights of EGL and HGL is equal to the dynamic head, V2/2g figure (8).
Figure 8: In an idealized Bernoulli-type flow, EGL is horizontal and its height remains constant. But this is not the case for HGL when the flow velocity varies along the flow.

## Slide 7
EXAMPLE5-5 Spraying Water into the Air
Water is flowing from a hose attached to a water maiin at 400 kPa gage (Fig, 5-38), A child places his thumb to cover most of the hose outlet, causing a thin jet of high-speed water to emerge, If the hose is held upward, what is the maximum height that the jet could achieve?
SOLUTION Water from a hose attached to the water main is sprayed into the air, The maximum height the water jet can rise is to be determined, Assumptions 1 The flow exiting into the air is steady, incompressible, and irrotational [so that the Bernoulli equation is applicable), 2 The water pressure
in the hose near the outlet is equal to the water main pressure. 3 The surface tension effects are negligible. 4 The friction between the water and air is negligible. 5 The irreversibilities that may occur at the outlet of the hose due to abrupt expansion are negligible.
Piopeities We take the density of water to be 1000 kg/m3.
Analysis This problem involves the conversion of flow, kinetic, and potential energies to each other without involving any pumps, turbines, and wasteful components with large frictional losses, and thus it is suitable for the use of the Bernoulli equation. The water height will be maximum under the stated assumptions. The velocity inside the hose is relatively low (V: = 0) and we take the hose outlet as the reference level (Zj = 0). At the top of the water trajectory V2 = 0, and atmospheric pressure pertains. Then the Bernoulli equation simplifies to
Solving for z2 and substituting,
^1. gage 400 kPa f'lOOO N/mA/] kg - m/sJ\
Pg (1000 kg/m3)(9.31 m/s2) V 1 Wa J\ 1N /
= 40.8 m
Therefore, the water jet can rise as high as 40.8 m into the sky in this case. Discussion The result obtained by the Bernoulli equation represents the upper limit and should be interpreted accordingly. It tells us that the water cannot possibly rise more than 40.8 m, and, in all likelihood, the rise will be much less than 40.8 m due to irreversible losses that we neglected.
■2)
7

## Slide 8
EXAMPLE5-6 Water Discharge from a Large Tank
A large tank open to the atmosphere is filled with water to a height of 5 m from the outlet tap (Fig. 5-39). A tap near the bottom of the tank is now opened, and water flows out from the smooth and rounded outlet. Determine the water velocity at the outlet.
SOLUTION A tap near the bottom of a tank is opened. The exit velocity of water from the tank is to be determined.
Assumptions 1 The flow is incompressible and irrotational (except very close to the walls). 2 The water drains slowly enough that the flow can be approximated as steady (actually quasi-steady when the tank begins to drain). Analysis This problem involves the conversion of flow, kinetic, and potential energies to each other without involving any pumps, turbines, and wasteful components with large frictional losses, and thus it is suitable for the use of the Bernoulli equation. We take point 1 to be at the free surface of water so that Pj = patm (open to the atmosphere), Vx “ 0 (the tank is large relative to the outlet), and zx = 5 m and z2 = 0 (we take the reference level at the center of the outlet). Also, P2 = Patni (water discharges into the atmosphere). Then the Bernoulli equation simplifies to
H V^° Pi VI
-F + — tz, = ft- + K 2g fa 2g
—»
Vf
zg
Solving for V2 and substituting,
V2 - \ 2gZ| ■ \ 2(9.81 m/s2)(5 m) - 9.9 m/s
The relation V = \ 2gz is called the Toricelli equation.
Therefore, the water leaves the tank with an initial velocity of 9.9 m/s. This is the same velocity that would manifest if a solid were dropped a distance of 5 m in the absence of air friction drag. (What would the velocity be if the tap were at the bottom of the tank instead of on the side?)
Discussion If the orifice were sharp-edged instead of rounded, then the flow would be disturbed, and the velocity would be less than 9.9 m/s, especially near the edges. Care must be exercised when attempting to apply the Bernoulli equation to situations where abrupt expansions or contractions occur since the friction and flow disturbance in such cases may not be negligible.
8

## Slide 9
2
FIGURE 5-40
Schematic for Example 5-7.
EXAMPLE5-7 Siphoning Out Gasoline from a Fuel Tank
During a trip to the beach (Patni = 1 atm = 101.3 kPa), a car runs out of gasoline, and it becomes necessary to siphon gas out of the car of a Good Samaritan (Fig. 5-40). The siphon is a small-diameter hose, and to start the siphon it is necessary to insert one siphon end in the full gas tank, fill the hose with gasoline via suction, and then place the other end in a gas can below the level of the gas tank. The difference in pressure between point 1 (at the free surface of the gasoline in the tank) and point 2 (at the outlet of the tube) causes the liquid to flow from the higher to the lower elevation. Point 2 is located 0.75 m below point 1 in this case, and point 3 is located 2 m above point 1. The siphon diameter is 4 mm, and frictional losses in the siphon are to be disregarded. Determine (a) the minimum time to withdraw 4 L of gasoline from the tank to the can and (b) the pressure at point 3. The density of gasoline is 750 kg/m3.
SOLUTION Gasoline is to be siphoned from a tank. The minimum time it takes to withdraw 4 L of gasoline and the pressure at the highest point in the system are to be determined.
Assumptions 1 The flow is steady and incompressible. 2 Even though the Bernoulli equation is not valid through the pipe because of frictional losses, we employ the Bernoulli equation anyway in order to obtain a best-case estimate. 3 The change in the gasoline surface level inside the tank is negligible compared to elevations zx and z2 during the siphoning period.
Piopeities The density of gasoline is given to be 750 kg/m3.
Analysis [a) We take point 1 to be at the free surface of gasoline in the tank so that P, = Patm (open to the atmosphere), Vj o (the tank is large relative to the tube diameter), and z2 = 0 (point 2 is taken as the reference level). Also, Pi = P*tm £ gasoline discharges into the atmosphere). Then the Bernoulli equation simplifies to
p; v^° p2 \/i /°
29 f9 29
Solving for V2 and substituting,
V2 = \ 2gz, = V 2(9.81 m/s2)(0.75 m) = 3.84 m/s
9

## Slide 10
The cross-sectional area of the tube and the flow rate of gasoline are A = TTD2/4 = TT(5 X 10 m)?/4 = 1.96 X 1D_im2
t> = V;A = (3.34 m/s)(1.96 X 10-5 m-) = 7.53 X ID-5 rrffe = 0.0753 L/s Then the time needed to siphon 4 L of gasoline becomes
lb) The pressure at point 3 can be determined by writing the Bernoulli equation between points 2 and 3. Noting that V2 = V3 (conservation of mass), z2
0, and P2 = P,
attni
0
p2 % y P] ys
■+ i-i
pg ' /g ' "z pg
Solving Tor P3 and substituting,
P3 = P^im - f>g*3
= 101.3 kPa - (750 kg/m5)(9,31 m/s2)(2.75 m)
= 81.1 kPa
Pitm _ P3 , ,
“1“ Z ^
pg pg
{ 1 N
Vi kq - r
_ / 1 kPa
kg ■ m/s2Al000 N/m2
Discussion The siphoning time is determined by neglecting frictional effects, and thus this is the minimum time required. In reality, the time will be longer than 53.1 s because of friction between the gasoline and the tube surface. Also, the pressure at point 3 is below the atmospheric pressure. If the elevation difference between points 1 and 3 is too high, the pressure at point 3 may drop below the vapor pressure of gasoline at the gasoline temperature, and some gasoline may evaporate (cavitate). The vapor then may form a pocket .at the top and halt the flow of gasoline.
10

## Slide 11
EXAMPLE5-8 Velocity Measurement by a Pitot Tube
A piezometer and a Pitot tube are tapped into a horizontal water pipe, as shown in Fig. 5-41, to measure static and stagnation (static + dynamic) pressures. For the indicated water column heights, determine the velocity at the center of the pipe,
SOLUTION The static and stagnation pressures in a horizontal pipe are measured. The velocity at the center of the pipe is to be determined. Assumptions 1 The flow is steady and incompressible. 2 Points 1 and 2 are close enough together that the irreversible energy loss between these two points is negligible, and thus we can use the Bernoulli equation.
Analysis We take points 1 and 2 along the centerline of the pipe, with point 1 directly under the piezometer and point 2 at the tip of the Pitot tube. This is a steady flow with straight and parallel streamlines, and the gage pressures at points 1 and 2 can be expressed as
Pi = pg(hi + hz)
P, = pgpi, + h2 + hj
FIGURE 5-41 Schematic for Example 5-8.
Noting that point 2 is a stagnation point and thus V2 = 0 and zx = z2, the application of the Bernoulli equation between points 1 and 2 gives
P, V? ^ _P2 V^0 V, _ P2 - P,
rt+2i + f'~S+2i V, - 2^—
Substituting the Px and P2 expressions gives
V I2 _ p? - Pi _ f>g(h, + h2 + hi) - f,g(h, + hj _
2g pg pg 3
Solving for \Jl and substituting,
V, = V 2gih = \ 2(9.81 m/s^O.^m) = 1.53 m/s
Discussion Note that to determine the flow velocity, all we need is to measure the height of the excess fluid column in the Pitot tube.
11

## Slide 12
EXAMPLE 5-10 Bernoulli Equation for Compressible Flow
Derive the Bernoulli equation when the compressibility effects are not negligible for an ideal gas undergoing (a) an isothermal process and (b) an isen-tropic process.
SOLUTION The Bernoulli equation for compressible flow is to be obtained for an ideal gas for isothermal and isentropic processes.
Assumptions 1 The flow is steady and frictional effects are negligible. 2 The fluid is an ideal gas, so the relation P = pRT is applicable. 3 The specific heats are constant so that P/pk = constant during an isentropic process. Analysis (a) When the compressibility effects are significant and the flow cannot be assumed to be incompressible, the Bernoulli equation is given by Eq. 5-40 as
" dP V2
— + ~2 + gz = constant (along a streamline)
(1)
The compressibility effects can be properly accounted for by expressing p in terms of pressure, and then performing the integration JdP/p in Eq. 1. But this requires a relation between P and p for the process. For the isothermal expansion or compression of an ideal gas, the integral in Eq. 1 can be performed easily by noting that T = constant and substituting p = PIRT. It gives
" dP j P
dP
J P/RT
= RT In P
Substituting into Eq. 1 gives the desired relation,
Isothermal process:
RT In P +
V!
2
+ gz = constant
(2)
(b) A more practical case of compressible flow is the isentropic flow of ideal gases through equipment that involves high-speed fluid flow such as nozzles, diffusers, and the passages between turbine blades. Isentropic (i.e., reversible and adiabatic) flow is closely approximated by these devices, and it is characterized by the relation Plpk = C = constant, where k is the specific heat ratio of the gas. Solving for p from Plpk = C gives p = C~llkPllk. Performing the integration,
dP
j P
ci/kp-m C|P =
D 1ft+1 1A 1 _
-i/k +1
p 1A p-lfllt+1
~p~ - i/k +1
p
13)
Substituting, the Bernoulli equation for steady, isentropic, compressible flow of an ideal gas becomes
Isentropic flow:
(rh)!>+T ~ sz - “nstam
(4a)
(4b)
A common practical situation involves the acceleration of a gas from rest (stagnation conditions at state 1) with negligible change in elevation. In that case we have z1 = z2 and Vj = 0. Noting that p = P/RT for ideal

## Slide 13
gases, Plpk = constant for isentropic flow, and the Mach number is defined as Ma = V/c where c = VkRT is the local speed of sound for ideal gases, Eq. 4b simplifies to
Pi
P2
(4c)
where state 1 is the stagnation state and state 2 is any state along the flow. Discussion It can be shown that the results obtained using the compressible and incompressible equations deviate no more than 2 percent when the Mach number is less than 0.3. Therefore, the flow of an ideal gas can be considered to be incompressible when Ma ^ 0.3. For atmospheric air at normal conditions, this corresponds to a flow speed of about 100 m/s or 360 km/h, which covers our range of interest.
Reference:
Cimbala, John M., and Yunus A. £engel. Essentials of fluid mechanics: fundamentals and applications. McGraw-Hill Higher Education, 2008.
13