## Slide 1
VISCOSITY
When two solid bodies in contact move relative to each other, a friction force develops at the contact surface in the direction opposite to motion. To move a table on the floor, for example, we have to apply a force to the table in the horizontal direction large enough to overcome the friction force. It appears that there is a property that represents the internal resistance of a fluid to motion or the “fluidity,” and that property is the viscosity. The force a flowing fluid exerts on a body in the flow direction is called the drag force, and the magnitude of this force depends, in part, on viscosity
Figure 1: A fluid moving relative to a body exerts a drag force on the body, partly because of friction caused by viscosity.
The fluid in contact with the upper plate sticks to the plate surface and moves with it at the same velocity, and the shear stress t acting on this fluid layer is
F
x =
A
where A is the contact area between the plate and the fluid. Note that the fluid layer deforms continuously under the influence of shear stress. In steady laminar flow, the fluid velocity between the plates varies linearly between 0 and V, and thus the velocity profile and the velocity gradient are
and
du _V
dy l
where y is the vertical distance from the lower plate.
Figure 2: The behavior of a fluid in laminar flow between two parallel plates when the upper plate moves with a constant velocity.
1

## Slide 2
During a differential time interval dt, the sides of fluid particles along a vertical line MN rotate through a differential angle d$ while the upper plate moves a differential distance da = Vdt. The angular displacement or deformation (or shear strain) can be expressed as
„ da V dt du 6/1 ~ tan^ = T = — = ^dt
Rearranging, the rate of deformation under the influence of shear stress t becomes
d/3 = du dt dy
Thus we conclude that the rate of deformation of a fluid element is equivalent to the velocity gradient du/dy. Further, it can be verified experimentally that for most fluids the rate of deformation (and thus the velocity gradient) is directly proportional to the shear stress t,
d|p du
T -• — or T (r ——
Fluids for which the rate of deformation is proportional to the shear stress are called Newtonian fluids after Sir Isaac Newton, who expressed it first in 1687. In one-dimensional shear flow of Newtonian fluids, shear stress can be expressed by the linear relationship
Shear stress: r = fi— (N/nF)
dy
where the constant of proportionality m is called the coefficient of viscosity or the dynamic (or absolute) viscosity of the fluid, whose unit is kg/m • s, or equivalently, N • s/m2 (or Pa ! s where Pa is the pressure unit pascal). A common viscosity unit is poise, which is equivalent to 0.1 Pa . s (or centipoise, which is one-hundredth of a poise). The viscosity of water at 20°C is 1 centipoise, and thus the unit centipoise serves as a useful reference. A plot of shear stress versus the rate of deformation (velocity gradient) for a Newtonian fluid is a straight line whose slope is the viscosity of the fluid, as shown in Fig.3. Note that viscosity is
independent of the rate of deformation.
2
Rate of deformation, du/dy

## Slide 3
Figure 3: The rate of deformation (velocity gradient) of a Newtonian fluid is proportional to shear stress, and the constant of proportionality is the viscosity.
The shear force acting on a Newtonian fluid layer (or, by Newton’s third law, the force acting on the plate) is
Then the force F required to move the upper plate in Fig. 2 at a constant velocity of V while the lower plate remains stationary is
This relation can alternately be used to calculate m when the force F is measured. Therefore, the experimental setup just described can be used to measure the viscosity of fluids. Note that under identical conditions, the force F will be very different for different fluids.
In fluid mechanics and heat transfer, the ratio of dynamic viscosity to density appears frequently. For convenience, this ratio is given the name kinematic viscosity v and is expressed as v = p/p. Two common units of kinematic viscosity are m2/s and stoke (1 stoke = 1 cm2/s = 0.0001 m2/s).
Air at 20^0 and 1 atm:
/i = 1.83 x IO-s kg/m ■ s r = 1,52 x 1Or* mzft
Air at 20°C and 4 atm:
fi = 1.33 x 1CT5 kg/m ■ s v = 0.380 x ICTS m2/s
Figure 4: Dynamic viscosity, in general, does not depend on pressure, but kinematic viscosity does.
3

## Slide 4
The viscosity of a fluid is directly related to the pumping power needed to transport a fluid in a pipe or to move a body (such as a car in air or a submarine in the sea) through a fluid.
Viscosity
Castor oil
Glycerin
Crude oil (5G 0.86!
Kerosei
Aniline
Mercury-
Carbon tetrachlorici
Benzene
Helium
Carbon Dioxidi
TABLE 2-3 | 
Dynamic viscosities of some fluids at 1 atm and 20°C {unless otherwise stated) | 
 | Dynamic Viscosity
Fluid | n, kg/m - s
Glycerin: | 
-20=C | 134.0
o°c | 10,5
20° C | 1.52
40° C | 0,31
Engine oil: | 
SAE low | 0.10
SAE 10W 30 | 0.17
SAE 30 | 0,29
SAE 50 | 0,86
Mercury | 0,0015
Ethyl alcohol | 0,0012
Water: | 
o°c | 0,0018
2D°C | 0,0010
LOQ’C (liquid) | 0,00028
lQQX (vapor) | 0,000012
Blood, 37aC | 0,00040
Gasoline | 0,00029
Ammonia | 0,00015
Air | 0,000018
Hydrogen, G°C | 0,0000088
SAI 10 oil
0.06
0.04
0.03
0.02
e 5: The visco he viscosity o erature.
SAE 30 o
0.0
1 xKT3
Ethyl alcohol 'Water
Gasoline (SG 0.68)
i xur1
Figure 6: The variation of dynamic (absolute) viscosities of common fluids with temperature at 1 atm (1 N = s/m2 = 1 kg/m = s ! 0.020886 lbf = s/ft2). F. M. White, Fluid Mechanics 4e. Copyright © 1999 The McGraw-Hill Companies, Inc. Used by permission.

## Slide 5
Consider a fluid layer of thickness l within a small gap between two concentric cylinders, such as the thin layer of oil in a journal bearing. The gap between the cylinders can be modeled as two parallel flat plates separated by a fluid. Noting that torque is T = FR (force times the moment arm, which is the radius R of the inner cylinder in this case), the tangential velocity is V = mR (angular velocity times the radius), and taking the wetted surface area of the inner cylinder to be A = 2nRL by disregarding the shear stress acting on the two ends of the inner cylinder, torque can be expressed as
T rn 2TTR\^L 4TT2R3 riL = = ^ -(;-= V--2-
where L is the length of the cylinder and n . is the number of revolutions per unit time, which is usually expressed in rpm (revolutions per minute). Note that the angular distance traveled during one rotation is 2n rad, and thus the relation between the angular velocity in rad/min and the rpm is m = 2nn.
5

## Slide 6
FIGURE 2-18
Schematic for Example 2-4.
EXAMPLE2-4 Determining the Viscosity of a Fluid
The viscosity of a fluid is to be measured by a viscometer constructed of two 40-cm-long concentric cylinders (Fig. 2-18). The outer diameter of the inner cylinder is 12 cm, and the gap between the two cylinders is 0.15 cm. The inner cylinder is rotated at 300 rpm, and the torque is measured to be 1.8 N ■ m. Determine the viscosity of the fluid.
SOLUTION The torque and the rpm of a double cylinder viscometer are given. The viscosity of the fluid is to be determined.
Assumptions 1 The inner cylinder is completely submerged in oil. 2 The viscous effects on the two ends of the inner cylinder are negligible.
Analysis The velocity profile is linear only when the curvature effects are negligible, and the profile can be approximated as being linear in this case since (IR « 1. Solving Eq. 2-34 for viscosity and substituting the given values, the viscosity of the fluid is determined to be
Discussion Viscosity is a strong function of temperature, and a viscosity value without a corresponding temperature is of little value. Therefore, the temperature of the fluid should have also been measured during this experiment, and reported with this calculation.
Reference:
Cimbala, John M., and Yunus A. £engel. Essentials of fluid mechanics: fundamentals and applications. McGraw-Hill Higher Education, 2008.
6