## Slide 1
Lecture 5: Transistor Bias Circuits
5.1 The DC Operating Point
The purpose of biasing a circuit is to establish a proper stable dc operating point or quiescent point (Q-point).
The Q-point of a circuit is defined by specific values for 𝐼C and �CE. These values are called the coordinates of the Q-point.
Improper biasing can cause distortion in the output signal,
  limiting of the positive portion of ���� as a result of a Q-point being too close to cutoff.
  limiting of the negative portion of ���� as a result of a Q-point being too close to saturation.
A dc load line passes through the Q-point on a transistor’s collector curves intersecting the vertical axis at approximately 𝐼C(sat) and the horizontal axis at �CE(off).
The linear (active) operating region of a transistor lies along the load line below saturation and above cutoff.
EXAMPLE 5-1: Determine the Q-point for the circuit in Figure 5-1 and draw the dc load line. Find the maximum peak value of base current for linear operation. Assume 𝛽DC = 200.
FIGURE 5-1
Solution The Q-point is defined by the values of 𝐼C and �CE.
𝐼B =
�BB − �BE
𝑅
B
= = 198 𝜇A
10 V − 0.7 V
47 kΩ
𝐼C = 𝛽DC𝐼B = (200)(198 𝜇A) = 39.6 mA
�CE = �CC − 𝐼C𝑅C = 20 V − (39.6 mA)(330 Ω) = 10 V − 13.07 V = 6.93 V
The Q-point is at 𝐼C = 39.6 mA and at �CE = 6.93 V.
Since 𝐼C(cutoff) = 0, we need to know 𝐼C(sat) to determine how much variation in collector current
can occur and still maintain linear operation of the transistor.
𝐼C(sat) = 𝑅
�CC
C
20 V
= = 60.6 mA 330 Ω
The dc load line is graphically illustrated in Figure 5-2, showing that before saturation is reached,
𝐼C can increase an amount ideally equal to
𝐼C(sat) − 𝐼CQ = 60.6 mA − 39.6 mA = 21.0 mA
However, 𝐼C can decrease by 39.6 mA before cutoff (𝐼C = 0) is reached. Therefore, the limiting excursion is 21 mA because the Q-point is closer to saturation than to cutoff. The 21 mA is the

## Slide 2
maximum peak variation of the collector current. Actually, it would be slightly less in practice because �CE(sat) is not quite zero.
FIGURE 5-2
We determine the maximum peak variation of the base current as follows:
𝐼�(�𝑒�𝑘) =
𝐼�(�𝑒�𝑘)
𝛽
DC
= = 105 𝜇A
21 mA
200
5.2 Voltage-Divider Bias
This is the most widely used biasing method of biasing a transistor for linear operation of using a single-source resistive voltage divider, as shown in Figure 5-3.
A voltage divider in which the base current is small compared to the current in 𝑅2 is said to be a stiff voltage divider because the base voltage is relatively independent of different transistors and temperature effects.
Loading effects are neglected for a stiff voltage divider.
The dc input resistance at the base of a BJT is approximately 𝛽DC𝑅E.
Voltage-divider bias provides good Q-point stability with a single-polarity supply voltage. It is the most common bias circuit.
FIGURE 5-3: Voltage-divider bias.
To analyze a voltage-divider circuit in which 𝐼B is small compared to 𝐼2, first we calculate the voltage on the base using the unloaded voltage-divider rule:
𝑽� ≅ (𝑹
𝑹�
� �
+ 𝑹) 𝑽��
Equation 5– 1
Once we know the base voltage, we can find the voltages and currents in the circuit, as follows:

## Slide 3
𝑽� = 𝑽� − 𝑽��
Equation 5– 2
and
𝑰� ≅ 𝑰� = 𝑹
𝑽�
�
Equation 5– 3
Equation 5– 4
Then,
𝑽� = 𝑽�� − 𝑰�𝑹�
Once we know �C and �E, we can determine �CE.
�CE = �C − �E
EXAMPLE 5-2: Determine �CE and 𝐼C in the stiff voltage-divider biased transistor circuit of Figure 5-4 if 𝛽DC = 100.
FIGURE 5-4
Solution The base voltage is
�B ≅ (𝑅
𝑅2
1 2
+ 𝑅) �CC = (10 kΩ + 5.6 kΩ
5.6 kΩ
) 10 V = 3.59 V
So, �E = �B − �BE = 3.59 V − 0.7 V = 2.89 V
And
�E 2.89 V
𝐼E = 𝑅= 560 Ω = 5.16 mA
E
Therefore, 𝐼C ≅ 𝐼E = 5.16 mA
And �C = �CC − 𝐼C𝑅C = 10 V − (5.16 mA)(1.0 kΩ) = 4.84 V
�CE = �C − �E = 4.84 V − 2.89 V = 1.95 V
To determine if the divider is stiff, we need to examine the dc input resistance looking in at the base as shown in Figure 5-5.
FIGURE 5-5: Voltage divider with load.

## Slide 4
Loading Effects of Voltage-Divider Bias: DC Input Resistance at the Transistor Base is proportional to 𝛽DC so it will change for different transistors.
𝑹��(����) =
𝜷��𝑽�
𝑰
�
Equation 5– 5
This is the effective load on the voltage divider illustrated in Figure 5-5.
We can quickly estimate the loading effect: If 𝑹��(����) is at least ten times larger than
𝑹�, the loading effect will be 10% or less and the voltage divider is stiff. If 𝑹��(����) is less than ten times 𝑹�, it should be combined in parallel with 𝑹�.
EXAMPLE 5-3: Determine the dc input resistance looking in at the base of the transistor in Figure 5-6. 𝛽DC = 125 and �B = 4 V.
Solution
�BE = �B − �E
0.7 V = �B − 𝐼E𝑅E
FIGURE 5-6
𝐼E =
�B − 0.7 V
𝑅
E
=
4 V − 0.7 V
1.0 kΩ
= 3.3 mA
𝑅IN(BASE) =
𝛽DC�B
𝐼
E
= = 152 kΩ
125 (4 V)
3.3 mA
Thevenin’s Theorem Applied to Voltage-Divider Bias: To analyze a voltage-divider biased transistor circuit for base current loading effects, we will apply Thevenin’s theorem to evaluate the circuit. First, let’s get an equivalent base-emitter circuit for the circuit in Figure 5-6(a) using Thevenin’s theorem. Looking out from the base terminal, the bias circuit can be redrawn as shown in Figure 5-6(b).
𝑰� = 𝑹
𝑽�� − 𝑽��
�
+ 𝑹⁄𝜷
�� ��
Equation 5– 6
FIGURE 5-6: Thevenizing the bias circuit.

## Slide 5
If 𝑅TH⁄𝛽DC is small compared to 𝑅E, the result is the same as for an unloaded voltage divider.
Voltage-divider bias is widely used because reasonably good bias stability is achieved with a single supply voltage.
Voltage-Divider Biased PNP Transistor requires bias polarities opposite to the npn. This can
be accomplished with a negative collector supply voltage, as in Figure 5-7(a), or with a positive emitter supply voltage, as in Figure 5-7(b).
FIGURE 5-7: Voltage-divider biased pnp transistor.
In a schematic, the pnp is often drawn upside down so that the supply voltage is at the top of the schematic and ground at the bottom, as in Figure 5-7(c).
The analysis procedure is the same as for an npn transistor circuit using Thevenin’s theorem and Kirchhoff’s voltage law: For Figure 5-7(a), the equation for 𝐼E is
𝑰� = 𝑹
−𝑽�� + 𝑽��
� �� ��
+ 𝑹⁄𝜷
Equation 5– 7
For Figure 5-7(b), The equation for 𝐼E is
𝑰� =
𝑽�� + 𝑽�� − �EE
𝑹� + 𝑹��⁄𝜷��
Equation 5– 8
EXAMPLE 5-4: Find 𝐼C and �EC for the pnp transistor circuit in Figure 5-8.
FIGURE 5-8
Solution This circuit has the configuration of Figures 5-7(b) and (c). Apply Thevenin’s theorem.
�TH = (𝑅
𝑅1
1 2
+ 𝑅) �EE = (22 kΩ + 10 kΩ ) 10 V
22 kΩ
�TH = (0.688)10 V = 6.88 V
𝑅TH = 𝑅
𝑅1𝑅2
1 2
= = 6.88 kΩ
+ 𝑅22 kΩ + 10 kΩ
(22 kΩ)(10 kΩ)
Use Equation 5–8 to determine 𝐼E.

## Slide 6
𝐼E =
�TH + �BE − �EE
𝑅+ 𝑅⁄𝛽= 1.0 kΩ + 6.88 kΩ⁄150 = 1.0 kΩ + 45.9 Ω = −2.31 mA
E TH DC
6.88 V + 0.7 V − 10 V −2.42 V
The negative sign on 𝐼E indicates that the assumed current direction in the Kirchhoff’s analysis is opposite from the actual current direction. From 𝐼E, we can determine 𝐼C and �EC as follows:
𝐼C = 𝐼E = 2.31 mA
�C = 𝐼C𝑅C = (2.31 mA)(2.2 kΩ) = 5.08 V
�E = �EE − �𝑅E = �EE − 𝐼E𝑅E = 10 V − (2.31 mA)(1.0 kΩ) = 7.68 V
�EC = �E − �C = 7.68 V − 5.08 V = 2.6 V
EXAMPLE 5-5: Find 𝐼C and �CE for a pnp transistor circuit with these values:𝑅1 = 68 kΩ, 𝑅2 = 47 kΩ, 𝑅C = 1.8 kΩ, 𝑅E = 2.2 kΩ, �CC = −6 V, and 𝛽DC = 75. Refer to Figure 5-7(a), which shows the schematic with a negative supply voltage.
Solution Apply Thevenin’s theorem.
�TH = (𝑅
𝑅2
1
+ 𝑅) �CC = (68 kΩ + 47 kΩ
2
47 kΩ
) (−6 V) = (0.409)(−6 V) = −2.45 V
𝑅TH = 𝑅
𝑅1𝑅2
1 2
+ 𝑅= 68 kΩ + 47 kΩ = 27.8 kΩ
(68 kΩ)(47 kΩ)
Use Equation 5–7 to determine 𝐼E.
𝐼E = 𝑅
−�TH + �BE
E TH DC
+ 𝑅⁄𝛽
= 2.2 kΩ + 27.8 kΩ⁄75 = 2.2 kΩ + 371 Ω = 1.23 mA
−(−2.45 V) + 0.7 V 3.15 V
From 𝐼E, we can determine 𝐼C and �CE as follows:
𝐼C = 𝐼E = 1.23 mA
�C = −�CC − �𝑅C = −�CC + 𝐼C𝑅C = −6 V + (1.23 mA)(1.8 kΩ) = −3.79 V
�E = �EE − �𝑅E = �EE − 𝐼E𝑅E = 0 − (1.23 mA)(2.2 kΩ) = −2.71 V
�CE = �C − �E = −3.79 V − (−2.71 V) = −1.08 V
5.3 Other Bias Methods
In this section, four additional methods for dc biasing a transistor circuit are discussed.
Emitter Bias: provides excellent bias stability in spite of changes in 𝛽or temperature but requires both positive and negative supply voltages.
To obtain a reasonable estimate of the key dc values in an emitter-biased circuit, analysis is quite easy. In an npn circuit, such as shown in Figure 5-9, we can obtain the 𝐼E as
𝑰� = 𝑹
−𝑽�� − 𝑽��
�
+ 𝑹⁄𝜷
� ��
Equation 5– 9
�E = �EE + �𝑅E = �EE + 𝐼E𝑅E
�B = �E + �BE
�C = �CC − �𝑅C = �CC − 𝐼C𝑅C

## Slide 7
FIGURE 5-9: An npn transistor with emitter bias. Polarities are reversed for a pnp transistor. Single subscripts indicate voltages with respect to ground.
EXAMPLE 5-6: Calculate 𝐼E and �CE for the circuit in Figure 5-10 using the approximations
�E ≅ −1 V and 𝐼C ≅ 𝐼E.
FIGURE 5-10
Solution
�E ≅ −1 V
𝐼E =
−�EE − 1 V
𝑅
E
=
−(−15 V) − 1 V
10 kΩ
14 V
= 10 kΩ = 1.4 mA
�C = �CC − �𝑅C = �CC − 𝐼C𝑅C = +15 V − (1.4 mA)(4.7 kΩ) = 8.4 V
�CE = �C − �E = 8.4 V − (−1 V) = 9.4 V
EXAMPLE 5-7: Determine how much the Q-point (𝐼C, �CE) for the circuit in Figure 5-11 will change if 𝛽DC increases from 100 to 200 when one transistor is replaced by another.
FIGURE 5-11
Solution For 𝛽DC = 100,
𝐼C(1) ≅ 𝐼E = 𝑅
−�EE − �BE
E B DC
+ 𝑅⁄𝛽= 10 kΩ + 47 kΩ⁄100 = 1.37 mA
−(−15V) − 0.7 V
�C = �CC − 𝐼C(1)𝑅C = 15 V − (1.37 mA)(4.7 kΩ) = 8.56 V
�E = �EE + 𝐼E𝑅E = −15 V + (1.37 mA)(10 kΩ) = −1.3 V
Therefore, �CE(1) = �C − �E = 8.56 V − (−1.3) = 9.83 V
For 𝛽DC = 200,

## Slide 8
𝐼C(2) ≅ 𝐼E = 𝑅
−�EE − �BE
E B DC
+ 𝑅⁄𝛽= 10 kΩ + 47 kΩ⁄200 = 1.38 mA
−(−15V) − 0.7 V
�C = �CC − 𝐼C(2)𝑅C = 15 V − (1.38 mA)(4.7 kΩ) = 8.51 V
�E = �EE + 𝐼E𝑅E = −15 V + (1.38 mA)(10 kΩ) = −1.2 V
Therefore, �CE(2) = �C − �E = 8.51 V − (−1.2) = 9.71 V
The percent change in 𝐼C as 𝛽DC changes from 100 to 200 is
%∆𝐼C = (
𝐼C(2) − 𝐼C(1)
𝐼
C(1)
) 100% = (
1.38 mA − 1.37 mA
1.37 mA
) 100% = 0.730%
The percent change in �CE is
�CE(2) − �CE(1)
%∆�CE = (
𝑉
CE(1)
) 100% = ( ) 100% = −1.22%
9.71 V − 9.83 V
9.83 V
Base Bias: has poor stability because its Q-point varies widely with 𝛽DC.
This method of biasing is common in switching circuits. Figure 5-12 shows a base-biased transistor. The analysis of this circuit for the linear region is directly dependent on 𝛽DC.
𝑽�� = 𝑽�� − 𝑰�𝑹�
Equation 5– 10
Equation 5– 11
𝑰� = 𝜷�� (
𝑽�� − 𝑽��
𝑹
�
)
FIGURE 5-12: Base bias.
EXAMPLE 5–8: Determine how much the Q-point (𝐼C, �CE) for the circuit in Figure 5-13 will change over a temperature range where 𝛽DC increases from 100 to 200.
FIGURE 5-13
Solution
For 𝛽DC = 100,
𝐼C(1) = 𝛽DC (
�CC − �BE
𝑅
B
) = 100 (
12 V − 0.7 V
330 kΩ
) = 3.42 mA
�CE(1) = �CC − 𝐼C(1)𝑅C
For 𝛽DC = 200,
= 12 V − (3.42 mA)(560 Ω) = 10.1 V

## Slide 9
𝐼C(2) = 𝛽DC (
�CC − �BE
𝑅
B
) = 200 ( ) = 6.84 mA
12 V − 0.7 V
330 kΩ
�CE(2) = �CC − 𝐼C(2)𝑅C = 12 V − (6.84 mA)(560 Ω) = 8.17 V
The percent change in 𝐼C as 𝛽DC changes from 100 to 200 is
%∆𝐼C = (
𝐼C(2) − 𝐼C(1)
𝐼
C(1)
) 100% = (
6.84 mA − 3.42 mA
3.42 mA
) 100% = 100% (an increase)
The percent change in �CE is
�CE(2) − �CE(1)
%∆�CE = (
𝑉
CE(1)
) 100% = ( ) 100% = −19.1% (a decrease)
8.17 V − 10.1 V
10.1 V
As we can see, the Q-point is very dependent on 𝛽DC in this circuit and therefore makes the base bias arrangement very unreliable. Consequently, base bias is not normally used if linear operation is required. However, it can be used in switching applications.
Emitter-Feedback Bias: combines base bias with the addition of an emitter resistor, as shown in Figure 5-14.
The idea is to help make base bias more predictable with negative feedback, which negates any attempted change in collector current with an opposing change in base voltage.
𝑰� = 𝑹
𝑽�� − 𝑽��
�
+ 𝑹⁄𝜷
� ��
Equation 5– 12
FIGURE 5-14: Emitter-feedback bias.
EXAMPLE 5-9: The base-bias circuit from Example 5-8 is converted to emitter-feedback bias by the addition of a 1 kΩ emitter resistor. All other values are the same, and a transistor with a
𝛽DC = 100 is used. Determine how much the Q-point will change if the first transistor is replaced with one having a 𝛽DC = 200. Compare the results to those of the base-bias circuit.
Solution
For 𝛽DC = 100,
𝐼C(1) = 𝐼E = 𝑅
�CC − �BE
E B DC
+ 𝑅⁄𝛽
12 V − 0.7 V
= 1 kΩ + 330 kΩ⁄100 = 2.63 mA
�CE(1) = �CC − 𝐼C(1)(𝑅C + 𝑅E) = 12 V − (2.63 mA)(560 Ω + 1 kΩ) = 7.90 V
For 𝛽DC = 200,

## Slide 10
𝐼C(2) = 𝐼E = 𝑅
�CC − �BE
E B DC
+ 𝑅⁄𝛽
12 V − 0.7 V
= 1 kΩ + 330 kΩ⁄200 = 4.26 mA
�CE(2) = �CC − 𝐼C(2)(𝑅C + 𝑅E) = 12 V − (4.26 mA)(560 Ω + 1 kΩ) = 5.35 V
The percent change in 𝐼C is
%∆𝐼C = (
𝐼C(2) − 𝐼C(1)
𝐼
C(1)
) 100% = ( ) 100% = 62.0%
4.26 mA − 2.63 mA
CE(1)
2.63 mA
5.35 V − 7.90 V
%∆�CE = (
�CE(2) − �CE(1)
𝑉
7.90 V
) 100% = ( ) 100% = −32.3%
Although the emitter-feedback bias significantly improved the stability of the bias for a change in 𝛽DC compared to base bias, it still does not provide a reliable Q-point.
Collector-Feedback Bias: provides good stability using negative feedback from collector to base.
In Figure 5-15, the base resistor 𝑅B is connected to the collector rather than to �CC, as it was in the base bias arrangement discussed earlier.
𝑰� = 𝑹
𝑽�� − 𝑽��
�
+ 𝑹⁄𝜷
� ��
Equation 5– 13
Since the emitter is ground, �CE = �C .
𝑽�� = 𝑽�� − 𝑰�𝑹�
Equation 5– 14
FIGURE 5-15: Collector-feedback bias.
EXAMPLE 5-10: Calculate the Q-point values (𝐼C and �CE) for the circuit in Figure 5-16.
FIGURE 5-16
Solution Using Equation 5–13, the collector current is
𝐼C = 𝑅
�CC − �BE
C B DC
+ 𝑅⁄𝛽
10 V − 0.7 V
= 10 kΩ + 180 kΩ⁄100 = 788 𝜇A
Using Equation 5–14, the collector-to-emitter voltage is
= �CC − 𝐼C𝑅C = 10 V − (788 𝜇A)(10 kΩ) = 2.12 V
�CE
10