## Slide 1: Combined Pressing and Sintering
Hot isostatic pressing accomplishes compaction and sintering in one step. Other techniques that combine the two steps are hot pressing and spark sintering.
Hot Pressing The setup in uniaxial hot pressing is very similar to conventional PM pressing, except that heat is applied during compaction. The resulting product is generally dense, strong, hard, and dimensionally accurate.

## Slide 2
Despite these advantages, the process
presents certain technical problems that limit its adoption. Principal among these are:
(1) selecting a suitable mold material that can withstand the high sintering temperatures;
(2) longer production cycle required to accomplish sintering; and
(3) heating and maintaining atmospheric control in the process. Hot pressing has found some application in the production of sintered carbide products using graphite molds.

## Slide 3
Spark Sintering An alternative approach that combines pressing and sintering but overcomes some of the problems in hot pressing is spark sintering. The process consists of two basic steps:
(1) powder or a green compacted preform is placed in a die; and
(2) upper and lower punches, which also serve as electrodes, compress the part and simultaneously apply a high-energy electrical current that burns off surface contaminants and sinters the powders, forming a dense, solid part in about 15 seconds. The process has been applied to a variety of metals.

## Slide 4: Liquid Phase Sintering
Conventional sintering is solid-state sintering; the metal is sintered at a temperature below its melting point.
In systems involving a mixture of two powder metals, in which there is a difference in melting temperature between the metals, an alternative type of sintering is used, called liquid phase sintering.
16.5

## Slide 5
In this process, the two powders are initially mixed, and then heated to a temperature that is high enough to melt the lower melting- point metal but not the other.
The melted metal thoroughly wets the solid particles, creating a dense structure with strong bonding between the metals upon solidification.

## Slide 6
Depending on the metals involved, prolonged heating may result in alloying of the metals by gradually dissolving the solid particles into the liquid melt and/or diffusion of the liquid metal into the solid.
In either case, the resulting product is fully densified (no pores) and strong.
Examples of systems that involve liquid phase sintering include Fe–Cu, W–Cu, and Cu–Co.