## Slide 1
1
Diyala University
Collage of Engineering
Computer Engineering
Department
Euler Path
Lecture Five
In The Name of God

## Slide 2
The sequence of signals on the path (in this example: A, B, C) is the signal ordering for the inputs to be used in stick diagram.
PUN and PDN Euler paths should be consistent (same sequence).
If we can define a Euler path, then we can generate a layout with no diffusion breaks.
Referring to the stick diagram on the right in previous slide (redrawn here):
For PDN, we begin with node i, then we meet signal A (i.e. polysilicon wire), then we meet node GND, then we meet signal B (i.e. polysilicon wire), then we meet node i again (hence both nodes are connected together using metal1 layer), then we meet signal C (i.e. polysilicon wire), then we meet node X.
For PUN, we begin with node VDD, then we meet signal A (i.e. polysilicon wire), then we meet node j, then we meet signal B (i.e. polysilicon wire), then we meet node X (this node is connected to the previous X node using metal1 layer), then we meet signal C (i.e. polysilicon wire), then we meet node VDD again.
A
B
C
VDD
X
Mr. AHMED K. JAMEIL
GND

## Slide 3
Examples of consistent Euler path: ABDC, BDCA.
Examples of bad input ordering: DACB, BCAD.
Mr. AHMED K. JAMEIL

## Slide 4
Since no consistent Euler path exists for y = a + bc+ de, it is impossible to draw a single strip of n-diffusion and p-diffusion, with the same polysilicon ordering for both NMOS and PMOS. The best we can do is to have a single strip for n-diffusion and two strips of p-diffusions.
Exercise: Draw a compact stick diagram for y.
Mr. AHMED K. JAMEIL

## Slide 5
VTC characteristics are dependent upon the gate inputs (so the noise margins are also data dependent!)
Case 1 – both transistors in the PUN are on simultaneously (A = B = 0), representing a strong pull-up, i.e. large Wp. Referring to Inverter transparencies pp. 17, 19, and 21, which say that VM increases if pull-up current is bigger, the VTC is located to the right.
Cases 2 & 3 - only one of the pull-up devices is on. So the VTC is shifted left as a result of the weaker PUN.
There is a small difference between Cases 2 and 3, which can be attributed to the body effect on M2. Since M1 is “easier” to turn on (in other words, it can conduct relatively more current), VTC associated with it is on extreme left.
Mr. AHMED K. JAMEIL

## Slide 6
Note capacitance on the internal node – due to the source and drain diffusion capacitances and overlap and channel capacitances of the series transistors.
Mr. AHMED K. JAMEIL

## Slide 7
Mr. AHMED K. JAMEIL

## Slide 8
Reason for difference in the last two delays is due to internal node capacitance of the pull-down stack. When A transitions from 1 → 0, the pull- up only has to charge CL; when A = 1 and B transitions, pull-up has to charge up both CL and Cint.
For output high-to-low transitions (first three cases) delay depends on state of Cint. Delay is worst when internal node is charged up to VDD – VT2 (refer circuit on p. 15).
Conclusion: Estimates of delay can be fairly complex – have to consider internal node capacitances and the input data patterns.
Mr. AHMED K. JAMEIL

## Slide 9
Also note structure of pull-up and pull-down. The circuit is designed as above to minimize diffusion cap at output (only one PMOS drain is connected to output).
Very slow circuit if D PMOS is moved up, and B & C NMOS also moved up. In this case we have at the output node
for pull-up: drain capacitances of A & C transistors
for pull-down: drain capacitances of D, B & C transistors
Mr. AHMED K. JAMEIL

## Slide 10
Mr. AHMED K. JAMEIL

## Slide 11
Mr. AHMED K. JAMEIL

## Slide 12
The VeCAD (VLSI – eCAD) from FKE, UTM, MALAYSIA, 2012
2. Jimmie J. Cathey, Ph.D, Theory and Problems of Electronic Devices and Circuits, 2nd Edition, 2002.
3. J. M. Rabaey, A. Chandrakasan and B. Nikolic, Digital Integrated Circuits: A Design Perspective. 2nd ed. Upper Saddle River, NJ: Pearson Education, Inc., 2003.
4. S-M. Kang and Y. Leblebici, CMOS Digital Integrated Circuits. 3rd ed. Singapore: McGraw-Hill,
2005.
References: