## Slide 1
1
Diyala University
Collage of Engineering
Computer Engineering
Department
Delay Definitions
Lecture Nine
In The Name of God

## Slide 2
Delay is a function of fan-out. Larger fan-out means bigger capacitance at inverter output due to gate capacitances.

## Slide 3
The floating gate-drain capacitor can be replaced by a capacitance-to-ground that is accomplished by taking the so-called Miller effect into account.
During a low-high or high-low transition, the terminals of the gate-drain capacitor are moving in opposite directions. The voltage change over the floating capacitor is hence twice the actual output voltage swing.

## Slide 4
Vout
CL
Vout2
Vin
CG4
M
2
M4
CDB2
Vout
Cw
Vout2
V
in
CGD12
M1
CDB1
M
3
CG3
CG3 and CG4 are called extrinsic or fanout capacitances

## Slide 5
Cap parameters (see MOS Transistor note p. 37):
Overlap capacitance
COn = 0.31 fF/um; COp = 0.27 fF/um
Bottom junction capacitance
Cj0n = 2 fF/um2; Cj0p = 1.9 fF/um2
Side-wall junction capacitance
Cjsw0n = 0.28 fF/um; Cjsw0p = 0.22 fF/um
Gate capacitance
Cox = 6 fF/um2

## Slide 6
CGD1 and CGD2 doesn’t include channel cap because transistors are assumed either cut-off or pinched off.
CG3 and CG4 doesn’t include CGD3 and CGD4.
Bold parameters (Wn, Wp, ADn, PDn, ADp, PDp, Ln, Lp) show values that the designer has control over!
Notice that the load capacitance is almost evenly split between its two major components: the intrinsic capacitance (italic) composed of the diffusion and overlap capacitances and the extrinsic capacitance (CG3, CG4) and wiring capacitance (CW) contributed by the connecting gate and wire.

## Slide 7
Often it is desirable to have identical propagation delays for both rising and falling inputs. This condition can be achieved by making the on-resistance of the NMOS and PMOS approximately equal. This is the SAME condition as that for a symmetrical VTC.

## Slide 8
Reqn
= 8.67 k and
Reqp
= 6.89 k in this case. See MOS Transistor
transparency, p. 24 for normalized (W/L = 1) Req values.
The top time is from calculation using equation in p. 28 while the bottom time is simulation.
Note overshoots on simulated output signals. Caused by the gate-drain capacitances of the inverter transistors which couple the steep voltage step at the input node directly to the output before the transistors can even start to react to the changes at the inputs.
These overshoots have a negative effect on gate performance and explain why the simulated delays are larger than the estimations.

## Slide 9
Refer text section 5.4.2 for Reqn equation. NMOS is assumed to be in velocity saturation. The formula is
3 V DD 
7
9

 V DD 

Reqn 
1 
4 I DSAT 
Ignoring  term,
 3
V DD
Req n
4 I DS AT
If the supply voltage is high enough so that VDD >> VTn + VDSATn/2, the delay becomes virtually independent of the supply voltage! If VDD >> VTn + VDSATn/2, IDSATn = (W/L)nk’nVDSATn(VDD – VTn – VDSATn/2)  (W/L)nk’nVDSATnVDD.
Lowering VDD slows down the gate.

## Slide 10
Self-loading is when the intrinsic capacitance (diffusion capacitance) starts to dominate the extrinsic load formed by wiring and fanout.
Increasing VDD has reliability concerns - oxide breakdown, hot-electron effects
- that enforce firm upper bounds on the supply voltage in deep submicron
processes.

## Slide 11
The VeCAD (VLSI – eCAD) from FKE, UTM, MALAYSIA, 2012
2. Jimmie J. Cathey, Ph.D, Theory and Problems of Electronic Devices and Circuits, 2nd Edition, 2002.
3. J. M. Rabaey, A. Chandrakasan and B. Nikolic, Digital Integrated Circuits: A Design Perspective. 2nd ed. Upper Saddle River, NJ: Pearson Education, Inc., 2003.
4. S-M. Kang and Y. Leblebici, CMOS Digital Integrated Circuits. 3rd ed. Singapore: McGraw-Hill,
2005.
References: