## Slide 1
Multiple Choice Questions on 8086 Microprocessor
A microprocessor is a chip integrating all the functions of a CPU of a computer.
  multiple B. single C. double D. triple ANSWER: B
Microprocessor is a/an circuit that functions as the CPU of the compute
  electronic B. mechanic C. integrating D. processing ANSWER: A
Microprocessor is the of the computer and it perform all the computational tasks
  main B. heart C. important D. simple ANSWER: B
The purpose of the microprocessor is to control
  memory B. switches C. processing D. tasks ANSWER: A
The first digital electronic computer was built in the year
A. 1950 B. 1960 C. 1940 D. 1930 ANSWER: C
In 1960's texas institute invented
  integrated circuits B. microprocessor C. vacuum tubes D. transistors ANSWER: A
The intel 8086 microprocessor is a processor
  8 bit B. 16 bit C. 32 bit D. 4 bit ANSWER: B
The microprocessor can read/write 16 bit data from or to
  memory B. I /O device C. processor D. register ANSWER: A
In 8086 microprocessor , the address bus is bit wide
  12 bit B. 10 bit C. 16 bit D. 20 bit ANSWER: D
The work of EU is
  encoding B. decoding C. processing D. calculations ANSWER: B
The 16 bit flag of 8086 microprocessor is responsible to indicate
A. the condition of result of ALU operation
C. the result of addition ANSWER: A
12. The CF is known as
B. the condition of memory
D. the result of subtraction
A. carry flag B. condition flag
.ANSWER: A
C. common flag
D. single flag
13. The SF is called as
A. service flag B. sign flag ANSWER: B
C. single flag
D. condition flag
14. The OF is called as
A. overflow flag B. overdue flag ANSWER: A
C. one flag
D. over flag

## Slide 2
15. The IF is called as
A. initial flag B. indicate flag C. interrupt flag ANSWER: C
D. inter flag
16. The register AX is formed by grouping
A. AH & AL B. BH & BL C. CH & CL ANSWER: A
D. DH & DL
17. The SP is indicated by
A. single pointer B. stack pointer C. source pointer ANSWER: B
D. destination pointer
18. The BP is indicated by
A. base pointer B. binary pointer C. bit pointer ANSWER: A
D. digital pointer
19. The SS is called as
A. single stack B. stack segment C. sequence stack ANSWER: B
.D. random stack
20. The index register are used to hold
A. memory register B. offset address C. segment memory ANSWER: A
D. offset memory
The BIU contains FIFO register of size bytes
A. 8 B. 6 C. 4 D. 12 ANSWER: B
The BIU prefetches the instruction from memory and store them in
  queue B. register C. memory D. stack ANSWER: A
The 1 MB byte of memory can be divided into segment
  1 Kbyte B. 64 Kbyte C. 33 Kbyte D. 34 Kbyte ANSWER: B
The DS is called as
  data segment B. digital segment C. divide segment D. decode segment ANSWER: A
The CS register stores instruction in code segment
  stream B. path C. codes D. stream line ANSWER: C
The IP is bits in length
  8 bits B. 4 bits C. 16 bits D. 32 bits ANSWER: C
The push source copies a word from source to
  stack B. memory C. register D. destination ANSWER: A
LDs copies to consecutive words from memory to register and
  ES B. DS C. SS D. CS ANSWER: B
INC destination increments the content of destination by A. 1 B. 2 C. 30 D. 41
ANSWER: A

## Slide 3
IMUL source is a signed
  multiplication B. addition ANSWER: A
C. subtraction
D. division
31. destination inverts each bit of destination
A. NOT B. NOR C. AND ANSWER: A
D. OR
The JS is called as
  jump the signed bit
C. jump simple bit ANSWER: A
B. jump single bit
D. jump signal it
Instruction providing both segment base and offset address are called
  below type .B. far type C. low type D. high type ANSWER: B
The conditional branch instruction specify for branching
  conditions B. instruction C. address D. memory ANSWER: A
The microprocessor determines whether the specified condition exists or not by testing the
  carry flag B. conditional flag C. common flag D. sign flag ANSWER: B
The LES copies to words from memory to register and
  DS B. CS C. ES D. DS ANSWER: C
The translates a byte from one code to another code
  XLAT B. XCHNG C. POP D. PUSH ANSWER: A
The contains an offset instead of actual address
  SP B. IP C. ES D. SS ANSWER: B
The 8086 fetches instruction one after another from of memory
  code segment B. IP C. ES D. SS ANSWER: A
The BIU contains FIFO register of size 6 bytes called .
  queue B. stack C. segment D. register ANSWER: A
The is required to synchronize the internal operands in the processor CLK Signal
  UR Signal B. Vcc C. AIE D. Ground ANSWER: A
The pin of minimum mode AD0-AD15 has address
  16 bit B. 20 bit C. 32 bit D. 4 bit ANSWER: B
The pin of minimum mode AD0- AD15 has _ data bus
  4 bit B. 20 bit C. 16 bit D. 32 bit ANSWER: C
The address bits are sent out on lines through

## Slide 4
A. A16-19 B. A0-17 ANSWER: A
C. D0-D17
D. C0-C17
is used to write into memory
  RD B. WR C. RD / WR D. CLK ANSWER: B
The functions of Pins from 24 to 31 depend on the mode in which is operating A. 8085 B. 8086 C. 80835 D. 80845
ANSWER: B
The RD, WR, M/IO is the heart of control for a mode
  minimum B. maximum C. compatibility mode D. control mode ANSWER: A
In a minimum mode there is a on the system bus
  single B. double C. multiple D. triple ANSWER: A
If MN/MX is low the 8086 operates in mode
  Minimum B. Maximum C. both (A) and (B) D. medium ANSWER: B
In max mode, control bus signal So,S1 and S2 are sent out in form
  decoded B. encoded C. shared D. unshared ANSWER: B
The bus controller device decodes the signals to produce the control bus signal
  internal B. data C. external D. address ANSWER: C
A Instruction at the end of interrupt service program takes the execution back to the interrupted program
  forward B. return C. data D. line ANSWER: B
The main concerns of the are to define a flexible set of commands
A. memory interface
C. both (A) and (B)
.ANSWER: A
B. peripheral interface
D. control interface
Primary function of memory interfacing is that the should be able to read from and write into register
  multiprocessor B. microprocessor C. dual Processor D. coprocessor ANSWER: B
To perform any operations, the Mp should identify the
  register B. memory C. interface D. system ANSWER: A
The Microprocessor places address on the address bus
  4 bit B. 8 bit C. 16 bit D. 32 bit ANSWER: C
The Microprocessor places 16 bit address on the add lines from that address by register should be selected
  address B. one C. two D. three ANSWER: B

## Slide 5
The of the memory chip will identify and select the register for the EPROM
  internal decoder B. external decoder C. address decoder D. data decoder ANSWER: A
Microprocessor provides signal like to indicate the read operatio
  LOW B. MCMW C. MCMR D. MCMWR ANSWER: C
To interface memory with the microprocessor, connect register the lines of the address bus must be added to address lines of the chip.
  single B. memory C. multiple D. triple
ANSWER: B
The remaining address line of bus is decoded to generate chip select signal
  data B. address C. control bus D. both (a) and (b) ANSWER: B
signal is generated by combining RD and WR signals with IO/M
A. control B. memory C. register D. system ANSWER: A
63. Memory is an integral part of a system
A. supercomputer
C. mini computer ANSWER: B
B. microcomputer
D. mainframe computer
has certain signal requirements write into and read from its registers
  memory B. register C. both (a) and (b) D. control ANSWER: A
An is used to fetch one address
  internal decoder B. external decoder C. encoder D. register ANSWER: A
The primary function of the is to accept data from I/P devices
  multiprocessor B. microprocessor C. peripherals D. interfaces ANSWER: B
signal prevent the microprocessor from reading the same data more than one
  pipelining B. handshaking C. controlling D. signaling ANSWER: B
Bits in IRR interrupt are
  reset B. set C. stop D. start ANSWER: B
generate interrupt signal to microprocessor and receive acknowledge
A. priority resolver
C. interrupt request register ANSWER: B
B. control logic
D. interrupt register
70. The pin is used to select direct command word
A. A0 B. D7-D6 C. A12 ANSWER: A
D. AD7-AD6
71. The is used to connect more microprocessor
A. peripheral device B. cascade C. I/O devices ANSWER: B
D. control unit

## Slide 6
72. CS connect the output of
A. encoder B. decoder ANSWER: B
C. slave program
D. buffer
73. In which year, 8086 was introduced?
A. 1978 B. 1979 C. 1977 ANSWER: A
D. 1981
Expansion for HMOS technology_
  high level mode oxygen semiconductor
  high level metal oxygen semiconductor
  high performance medium oxide semiconductor
  high performance metal oxide semiconductor ANSWER: D
8086 and 8088 contains transistors
A. 29000 B. 24000 C. 34000 ANSWER: A
D. 54000
ALE stands for
  address latch enable
C. address leak enable ANSWER: A
77. What is DEN?
B. address level enable
D. address leak extension
A. direct enable B. data entered C. data enable ANSWER: C
D. data encoding
In 8086, Example for Non maskable interrupts are .
  TRAP B. RST6.5 C. INTR D. RST6.6 ANSWER: A
In 8086 the overflow flag is set when .
  the sum is more than 16 bits.
  signed numbers go out of their range after an arithmetic operation.
  carry and sign flags are set.
  subtraction ANSWER: B
In 8086 microprocessor the following has the highest priority among all type interrupts?
  NMI B. DIV 0 C. TYPE 255 D. OVER FLOW ANSWER: A
In 8086 microprocessor one of the following statements is not true?
A. coprocessor is interfaced in max mode.
C. I /O can be interfaced in max / min mode. ANSWER: B
82. Address line for TRAP is?
B. coprocessor is interfaced in min mode.
D. supports pipelining
A. 0023H B. 0024H ANSWER: B
C. 0033H
D. 0099H
83. Access time is faster for .
A. ROM B. SRAM ANSWER: B
C. DRAM
D. ERAM

## Slide 7
84. The First Microprocessor was .
A. Intel 4004 B. 8080 ANSWER: A
C. 8085
D. 4008
Status register is also called as .
  accumulator B. stack C. counter D. flags ANSWER: D
Which of the following is not a basic element within the microprocessor?
A. Microcontroller
C. Register array Ans.: A
B. Arithmetic logic unit (ALU)
D. Control unit
87. Which method bypasses the CPU for certain types of data transfer?
A. Software interrupts
C. Polled I/O Ans.: D
Which bus is bidirectional?
  Address bus
C. Data bus Ans.: C
B. Interrupt-driven I/O
D. Direct memory access (DMA)
B. Control bus
D. None of the above
89. The first microprocessor had a(n) .
A. 1 – bit data bus
C. 4 – bit data bus Ans.: C
B. 2 – bit data bus
D. 8 – bit data bus
90. Which microprocessor has multiplexed data and address lines?
A. 8086
Ans.: A
Which is not an operand?
  Variable Ans.: D
B. 80286 C. 80386
D. Pentium
B. Register
C. Memory location D. Assembler
Which is not part of the execution unit (EU)?
  Arithmetic logic unit (ALU)
C. General registers Ans.: B
A 20-bit address bus can locate .
  1,048,576 locations
C. 4,194,304 locations Ans.: A
B. Clock
D. Flags
B. 2,097,152 locations
D. 8,388,608 locations
94. Which of the following is not an arithmetic instruction?
A. INC (increment)
C. DEC (decrement) Ans.: D
B. CMP (compare)
D. ROL (rotate left)

## Slide 8
95. During a read operation the CPU fetches _.
A. a program instruction
C. data itself Ans.: D
B. another address
D. all of the above
96. Which of the following is not an 8086/8088 general-purpose register?
A. Code segment (CS)
C. Stack segment (SS) Ans.: D
B. Data segment (DS)
D. Address segment (AS)
A 20-bit address bus allows access to a memory of capacity
  1 MB B. 2 MB C. 4 MB Ans.: A
D. 8 MB
98. Which microprocessor accepts the program written for 8086 without any changes?
A. 8085 B. 8086 C. 8087
Ans.: D
99. Which group of instructions do not affect the flags?
D. 8088
A. Arithmetic operations
C. Data transfer operations Ans.: C
The result of MOV AL, 65 is to store
  store 0100 0010 in AL
C. store 40H in AL Ans.: D
B. Logic operations
D. Branch operations
B. store 42H in AL
D. store 0100 0001 in AL