## Slide 1
8086 Microprocessor
Assistant lecturer: Abdullah Thaier Abdalsatir
Diyala university
College of engineering
Department of computer engineering
Second stage

## Slide 2
41
8086
Microprocessor
Addressing Modes: Memory Access
Segment Register (16 bits)
0 0 0
0
Physical Address (20 Bits)
Adder
Offset Value (16 bits)

## Slide 3
42
8086
Microprocessor
Addressing Modes : Memory Access
20 Address lines  8086 can address up to
2
20
= 1M bytes of memory
However, the largest register is only 16 bits
Physical Address will have to be calculated
Physical Address: Actual address of a byte in
memory. i.e. the value which goes out onto the
address bus.
Memory Address represented in the form –
Seg : Offset
(Eg - 89AB:F012)
Each time the processor wants to access
memory, it takes the contents of a segment
register, shifts it one hexadecimal place to the
left (same as multiplying by 1610), then add the
required offset to form the 20- bit address
89AB : F012  89AB 
89AB0 (Paragraph to byte  89AB x 10 = 89AB0) F012 
0F012
+ -------
(Offset is already in byte unit)
98AC2 (The absolute address)
16 bytes of
contiguous memory

## Slide 4
43
8086
Microprocessor
Addressing Modes : Memory Access
To access memory we use these four registers:
SI, DI, BP
BX,
Combining these registers inside [ ] symbols, we
can get different memory locations (Effective
Address, EA)
Supported combinations:
[BX + SI]
[BX + DI]
[BP + SI]
[BP + DI]
[SI]
[DI]
d16 (variable offset only) [BX]
[BX + SI + d8] [BX + DI + d8] [BP +
SI + d8] [BP + DI + d8]
[SI + d8]
[DI + d8]
[BP + d8]
[BX + d8]
[BX + SI + d16]
[BX + DI + d16]
[BP + SI + d16] [BP
+ DI + d16]
[SI + d16] [DI + d16] [BP + d16]
[BX + d16]
BX
BP
SI
DI
+ disp

## Slide 5
44
8086
Microprocessor
1. Register Addressing
2. Immediate Addressing
Addressing Modes
Group II : Addressing modes
for memory data
4. Register Indirect Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
Here, the effective address of the memory location
at which the data operand is stored is given in the
instruction.
The effective address
is just
a
16
-
bit number
written directly in the instruction.
Example:
The square brackets around the 1354H denotes the
contents of the memory location. When executed,
this instruction will copy the contents of the
memory location into BX register.
This addressing mode is called direct because the
displacement of the operand from the segment
base is specified directly in the instruction.
MOV BX, [1354H]
MOV BL, [0400H]
3. Direct Addressing

## Slide 6
(CH)

(MA +1)
45
8086
Microprocessor
Addressing Modes
Group II : Addressing modes
for memory data
1. Register Addressing
2.
Immediate Addressing
3. Direct Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In Register indirect addressing, name of the
register which holds the effective address (EA) will
be specified in the instruction.
Registers used to hold EA are any of the following
registers:
BX, BP, DI and SI.
Content of the DS register is used for base
address calculation.
Example:
MOV CX, [BX]
Operations:
EA = (BX)
BA = (DS) x 1610
MA = BA + EA
(CX)  (MA) or,
(CL)  (MA)
Note : Register/ memory
enclosed in brackets refer
to
content
memory
of
register/
4. Register Indirect Addressing

## Slide 7
8086
Microprocessor
Addressing Modes
Group II : Addressing modes
for memory data
1. Register Addressing
2.
Immediate Addressing
3. Direct Addressing
4. Register Indirect Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In Based Addressing, BX or BP is used to hold the
base value for effective address and a signed 8-bit
or unsigned 16-bit displacement will be specified in
the instruction.
In case of 8-bit displacement, it is sign extended
to 16-bit before adding to the base value.
When BX holds the base value of EA, 20-bit
physical address is calculated from BX and DS.
When BP holds the base value of EA, BP and SS is
used.
Example:
MOV AX, [BX + 08H]
Operations:
0008H  08H (Sign extended) EA = (BX) +
0008H
BA = (DS) x 1610
MA = BA + EA
(AX)  (MA)
or,
(AL)  (MA)
(AH)  (MA + 1)
5. Based Addressing
46

## Slide 8
47
8086
Microprocessor
Addressing Modes
Group II : Addressing modes
for memory data
1. Register Addressing
2.
Immediate Addressing
3. Direct Addressing
4. Register Indirect Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
SI or DI register is used to hold an index value for
memory data and a signed 8-bit or unsigned 16- bit
displacement will be specified in the instruction.
Displacement is added to the index value in SI or
DI register to obtain the EA.
In case of 8-bit displacement, it is sign extended
to 16-bit before adding to the base value.
Example:
MOV CX, [SI + 0A2H]
Operations:
FFA2H  A2H (Sign extended)
EA = (SI) + FFA2H
BA = (DS) x 1610
MA = BA + EA
(CX)  (MA) or,
(CL)  (MA)
(CH)  (MA + 1)

## Slide 9
48
8086
Microprocessor
Addressing Modes
Group II : Addressing modes
for memory data
1. Register Addressing
2. Direct Addressing
3. Register Indirect Addressing
4. Based Addressing
5. Indexed Addressing
8. String Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
Immediate Addressing In Based Index Addressing,
the effective address is computed from the sum of
a base register (BX
or BP), an index register (SI or DI) and a
displacement
Example: MOV DX, [BX + SI + 0AH]
Operations:
000AH  0AH (Sign extended)
EA = (BX) + (SI) + 000AH
BA = (DS) x 1610
MA = BA + EA
(DX)  (MA) or,
(DL)  (MA)
(DH)  (MA + 1)
7. Based Index Addressing

## Slide 10
Note : Effective address of
the Extra segment register
8086
Microprocessor
Addressing Modes
Group II : Addressing modes
for memory data
1. Register Addressing
2.
Immediate Addressing
3. Direct Addressing
4. Register Indirect Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
Employed in string operations to operate on string
data.
The effective
address (EA)
of
source data is stored
in SI register and the EA of destination is stored in
DI register.
Segment register for calculating base address of
source data is DS and that of the destination data
is ES
Example: MOVS BYTE
Operations:
Calculation of source memory location:
EA = (SI)
BA = (DS) x 1610
MA = BA + EA
Calculation of destination memory location:
EAE = (DI)
BAE = (ES) x 1610
MAE = BAE + EAE
(MAE)  (MA)
If DF = 1, then (SI)  (SI) – 1 and (DI) = (DI) - 1
If DF = 0, then (SI)  (SI) +1 and (DI) = (DI) + 1
49
8. String Addressing

## Slide 11
In indirect port addressing mode, the instruction
will specify the name of the register which holds
the port address. In 8086, the 16-bit port address
is stored in the DX register.
Example: OUT [DX], AX
Operations: PORTaddr = (DX)
(PORT)  (AX)
Content of AX is moved to port
whose address is specified by DX
register.
8086
Microprocessor
Addressing Modes
Group III : Addressing
modes for I/O ports
1. Register Addressing
2.
Immediate Addressing
3. Direct Addressing
4. Register Indirect Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
These addressing modes are
used to access data
from standard I/O mapped devices
or
ports.
In direct port addressing mode, an 8-bit port
address is directly specified in the instruction.
Example: IN AL, [09H]
Operations: PORTaddr = 09H
(AL)  (PORT)
Content of port with address 09H is
moved to AL register
11. Relative Addressing
12. Implied Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
50