## Slide 1
8086 Microprocessor
Assistant lecturer: Abdullah Thaier Abdalsatir
Diyala university
College of engineering
Department of computer engineering
Second stage

## Slide 2
51
8086
Microprocessor
1. Register Addressing
2. Immediate Addressing
Addressing Modes
3. Direct Addressing
4. Register Indirect Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
9. Direct I/O port Addressing
10. Indirect I/O port Addressing
12.Implied Addressing
IN this addressing mode, the effective address of
a program instruction is s p e c i f i e d relative to
Instruction Pointer (IP)by an 8-bit signed
displacement.
Example:JZ0AH
Operations:
000AH  0AH (sign extend)
If ZF =1then
EA = (IP) + 000AH
BA = (CS) x 1610
MA = BA + EA
If ZF = 1, then the program control jumps to new address
calculated above.
If ZF = 0, then next instruction of the program is
executed.
11. Relative Addressing

## Slide 3
52
8086
Microprocessor
1. Register Addressing
2. Immediate Addressing
3. Direct Addressing
Addressing Modes
Group IV: Implied
Addressing mode
4. Register Indirect Addressing
5. Based Addressing
6. Indexed Addressing
7. Based Index Addressing
8. String Addressing
9.
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
Instructions using this mode have no
operands. The instruction itself will specify
the data to be
operated by
the
instruction.
Example: CLC
This clears the carry flag to zero.
12. Relative Addressing

## Slide 4
53
8086
Microprocessor
Instruction Set
8086 supports 6 types of instructions.
1. Data Transfer Instructions
2. Arithmetic Instructions
3. Logical Instructions
4. String manipulation Instructions
5. Process Control Instructions
6. Control Transfer Instructions

## Slide 5
54
8086
Microprocessor
Instruction Set
1. Data Transfer Instructions
Generally involve two operands: Source operand and
Destination operand of the same size.
Source: Register or a memory location or an immediate data
Destination : Register or a memory location.
The size should be a either a byte or a word.
A 8-bit data can only be moved to 8-bit register/ memory
and a 16-bit data can be moved to 16-bit register/ memory.
Instructions that are used to transfer data/ address in to
registers, memory locations and I/O ports.

## Slide 6
55
8086
Microprocessor
Instruction Set
1. Data Transfer Instructions
Mnemonics: MOV, XCHG, PUSH, POP, IN, OUT …
MOV reg2/ mem, reg1/ mem
MOV reg2, reg1
MOV mem, reg1
MOV reg2, mem
(reg2)  (reg1)
(mem)  (reg1)
(reg2)  (mem)
MOV reg/ mem, data
MOV reg, data
MOV mem, data
(reg)  data
(mem)  data
XCHG reg2/ mem, reg1
XCHG reg2, reg1
XCHG mem, reg1
(reg2)  (reg1)
(mem)  (reg1)

## Slide 7
56
8086
Microprocessor
Instruction Set
1. Data Transfer Instructions
Mnemonics: MOV, XCHG, PUSH, POP, IN, OUT …
PUSH reg16/ mem
PUSH reg16
PUSH mem
(SP)  (SP) – 2
MA S = (SS) x 1610 + SP
(MA S ; MA S + 1)  (reg16)
(SP)  (SP) – 2
MA S = (SS) x 1610 + SP
(MA S ; MA S + 1)  (mem)
POP reg16/ mem
POP reg16
POP mem
MA S = (SS) x 1610 + SP
(reg16)  (MA S ; MA S + 1)
(SP)  (SP) + 2
MA S = (SS) x 1610 + SP
(mem)  (MA S ; MA S + 1)
(SP)  (SP) + 2

## Slide 8
57
8086
Microprocessor
Instruction Set
1. Data Transfer Instructions
Mnemonics: MOV, XCHG, PUSH, POP, IN, OUT …
IN A, [DX]
IN AL, [DX]
IN AX, [DX]
PORTaddr = (DX)
(AL)  (PORT)
PORTaddr = (DX)
(AX)  (PORT)
IN A, addr8
IN AL, addr8
IN AX, addr8
(AL)  (addr8)
(AX)  (addr8)
OUT [DX], A
OUT [DX], AL
OUT [DX], AX
PORTaddr = (DX)
(PORT)  (AL)
PORTaddr = (DX)
(PORT)  (AX)
OUT addr8, A
OUT addr8, AL
OUT addr8, AX
(addr8)  (AL)
(addr8)  (AX)

## Slide 9
58
8086
Microprocessor
Instruction Set
2. Arithmetic Instructions
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
ADD reg2/ mem, reg1/mem
ADC reg2, reg1
ADC reg2, mem
ADC mem, reg1
(reg2)  (reg1) + (reg2)
(reg2)  (reg2) + (mem)
(mem)  (mem)+(reg1)
ADD reg/mem, data
ADD reg, data
ADD mem, data
(reg)  (reg)+
data
(mem)  (mem)+data
ADD A, data
ADD AL, data8
ADD AX, data16
(AL)  (AL) + data8
(AX)  (AX) +data16

## Slide 10
59
8086
Microprocessor
Instruction Set
2. Arithmetic Instructions
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
ADC reg2/ mem, reg1/mem
ADC reg2, reg1
ADC reg2, mem
ADC mem, reg1
(reg2)  (reg1) + (reg2)+CF
(reg2)  (reg2) + (mem)+CF
(mem)  (mem)+(reg1)+CF
ADC reg/mem, data
ADC reg, data
ADC mem, data
(reg)  (reg)+ data+CF
(mem)  (mem)+data+CF
ADDC A, data
ADD AL, data8
ADD AX, data16
(AL)  (AL) + data8+CF
(AX)  (AX) +data16+CF

## Slide 11
60
8086
Microprocessor
Instruction Set
2. Arithmetic Instructions
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
SUB reg2/ mem, reg1/mem
SUB reg2, reg1
SUB reg2, mem
SUB mem, reg1
(reg2)  (reg1) -
(reg2)
(reg2)  (reg2) -
(mem)
(mem)  (mem) -
(reg1)
SUB reg/mem, data
SUB reg, data
SUB mem, data
(reg)  (reg) -
data
(mem)  (mem) - data
SUB A, data
SUB AL, data8
SUB AX, data16
(AL)  (AL) - data8
(AX)  (AX) - data16