## Slide 1
8086 Microprocessor
Assistant lecturer: Abdullah Thaier Abdalsatir
Diyala university
College of engineering
Department of computer engineering
Second stage

## Slide 2
81
8086
Microprocessor
Instruction Set
4. String Manipulation Instructions
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
Scan (compare) a string byte or word with accumulator
SCAS
SCASB
SCASW
MAE = (ES) x 1610 + (DI)
Modify flags  (AL) -
(MAE)
If (AL) > (MAE), then CF = 0; ZF = 0; SF = 0
If (AL) < (MAE), then CF = 1; ZF = 0; SF = 1
If (AL) = (MAE), then CF = 0; ZF = 1; SF = 0
If DF = 0, then (DI)  (DI) + 1
If DF = 1, then (DI)  (DI) –
1
MAE = (ES) x 1610 + (DI)
Modify flags  (AL) -
(MAE)
If (AX) > (MAE ; MAE + 1), then CF = 0; ZF = 0; SF = 0
If (AX) < (MAE ; MAE + 1), then CF = 1; ZF = 0; SF = 1
If (AX) = (MAE ; MAE + 1), then CF = 0; ZF = 1; SF = 0
If DF = 0, then (DI)  (DI) + 2
If DF = 1, then (DI)  (DI) –
2

## Slide 3
82
8086
Microprocessor
Instruction Set
4. String Manipulation Instructions
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
Load string byte in to AL or string word in to AX
LODS
LODSB
LODSW
MA = (DS) x 1610 + (SI)
(AL)  (MA)
If DF = 0, then (SI)  (SI) +
1
If DF = 1, then (SI)  (SI) –
1
MA = (DS) x 1610 + (SI)
(AX)  (MA ; MA + 1)
If DF = 0, then (SI)  (SI) +
2
If DF = 1, then (SI)  (SI) –
2

## Slide 4
83
8086
Microprocessor
Instruction Set
4. String Manipulation Instructions
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
Store byte from AL or word from AX in to string
STOS
STOSB
STOSW
MAE = (ES) x 1610 + (DI)
(MAE)  (AL)
If DF = 0, then (DI)  (DI) +
1
If DF = 1, then (DI)  (DI) –
1
MAE = (ES) x 1610 + (DI)
(MAE ; MAE + 1 )  (AX)
If DF = 0, then (DI)  (DI) +
2
If DF = 1, then (DI)  (DI) –
2

## Slide 5
4
8086
Microprocessor
Instruction Set
5. Processor Control Instructions
Mnemonics
Explanation
STC
Set CF  1
CLC
Clear CF  0
CMC
Complement carry CF  CF
/
STD
Set direction flag DF  1
CLD
Clear direction flag DF  0
STI
Set interrupt enable flag IF  1
CLI
Clear interrupt enable flag IF  0
NOP
No operation
HLT
Halt after interrupt is set
WAIT
Wait for TEST pin active
ESC opcode mem/ reg
Used to pass instruction to a coprocessor
which shares the address and data bus
with the 8086
LOCK
Lock bus during next instruction
8

## Slide 6
85
8086
Microprocessor
Instruction Set
6. Control Transfer Instructions
Transfer the control to a specific destination or target instruction
Do not affect flags
 8086 Unconditional transfers
Mnemonics
Explanation
CALL reg/ mem/ disp16
Call subroutine
RET
Return from subroutine
JMP reg/ mem/ disp8/ disp16
Unconditional jump

## Slide 7
86
8086
Microprocessor
Instruction Set
6. Control Transfer Instructions
 8086 signed conditional
branch instructions
 8086 unsigned
conditional
branch instructions
Checks flags
If conditions are true, the program control is
transferred to the new memory location in the same
segment by modifying the content of IP

## Slide 8
87
8086
Microprocessor
Instruction Set
6. Control Transfer Instructions
 8086 signed
conditionals
branch instructions

8086 unsigned conditional
branch instructions
Name
Alternate name
JE disp8
Jump if equal
JZ disp8
Jump if result is 0
JNE disp8
Jump if not equal
JNZ disp8
Jump if not zero
JG disp8
Jump if greater
JNLE disp8
Jump if not less or
equal
JGE disp8
Jump if greater
than or equal
JNL disp8
Jump if not less
JL disp8
Jump if less than
JNGE disp8
Jump if not
greater than or
equal
JLE disp8
Jump if less than
or equal
JNG disp8
Jump if not
greater
Name
Alternate name
JE disp8
Jump if equal
JZ disp8
Jump if result is 0
JNE disp8
Jump if not equal
JNZ disp8
Jump if not zero
JA disp8
Jump if above
JNBE disp8
Jump if not below
or equal
JAE disp8
Jump if above or
equal
JNB disp8
Jump if not below
JB disp8
Jump if below
JNAE disp8
Jump if not above
or equal
JBE disp8
Jump if below or
equal
JNA disp8
Jump if not above

## Slide 9
88
8086
Microprocessor
Instruction Set
6. Control Transfer Instructions
 8086 conditional branch instructions affecting individual flags
Mnemonics
Explanation
JC disp8
Jump if CF = 1
JNC disp8
Jump if CF = 0
JP disp8
Jump if PF = 1
JNP disp8
Jump if PF = 0
JO disp8
Jump if OF = 1
JNO disp8
Jump if OF = 0
JS disp8
Jump if SF = 1
JNS disp8
Jump if SF = 0
JZ disp8
Jump if result is zero, i.e, Z = 1
JNZ disp8
Jump if result is not zero, i.e, Z = 1