## Slide 1
Regulation
2018
Branch
Computer engineering
Year & Semester
: II Year / I Semester
MICROPROCESSOR AND MICROCONTROLLER LABORATORY
LAB MANUAL
Diyala university
College of engineering
Department of computer engineering
Assistant lecturer: Abdullah Thaier Abdalsatir

## Slide 2
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
2
ANNA UNIVERSITY CHENNAI
Regulation 2013
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY SYLLABUS
LIST OF EXPERIMENTS:
8086 Programs using kits and MASM
Basic arithmetic and Logical operations
Move a data block without overlap
Code conversion, decimal arithmetic and Matrix operations.
Floating point operations, string manipulations, sorting and searching
Password checking, Print RAM size and system date
Counters and Time Delay
Peripherals and Interfacing Experiments
Traffic light control
Stepper motor control
Digital clock
Key board and Display 11.Printer status
Serial interface and Parallel interface
A/D and D/A interface and Waveform Generation 8051.
Experiments using kits and MASM
Basic arithmetic and Logical operations
15. Square and Cube program, Find 2’s complement of a number
16. Unpacked BCD to ASCII
TOTAL: 45 PERIODS

## Slide 3
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
3
INTRODUCTION TO MICROPROCESSORS & MICROCONTROLLERS:
Microprocessor and controller is digital and programmable device with highly reliable and secured modern architecture. Building blocks of the Digital computer CPU functions Memory types Input / Output Devices Stored program concept History of Microprocessors.
Intel 8085 microprocessor:
Internal architecture, Hardware description, Interrupts and interrupts servicing and Interfacing the memory. Assembly Language Programming: 8085- Addressing modes & Instruction set, Flow charts, Assembly language programming and assembler directives, Linker and its operation, Programming examples.
Interfacing the input / output devices:
8255 Programmable Peripheral Interface, i8253 Programmable Interval Timer, 8251 Universal Synchronous /Asynchronous Receiver Transmitter, 8259 Programmable Interrupt Controller and i8279 Programmable Keyboard / Display interface device.
Interfacing the data converters:
Digital-to-Analog Converters, Interfacing DAC with 8086 microprocessor, Analog-to-Digital Converters Interfacing ADC with 8086.
Microprocessors:
Intel 8086 family microprocessors, Programming model, Memory paging, Virtual memory concept, advanced features of 80386/486/Pentium Processors.
Microcontroller:
Introduction to Microcontrollers, Intel-8051: description, Memory organization, Addressing Modes.
Architecture,
Hardware
Programming the i8051:
Instruction set, Assembly language programming, Interrupt structure and interrupt priorities, Interfacing with external devices and Programming.

## Slide 4
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
4
INDEX
EX. NO | DATE | NAME OF THE EXPERIMENT | STAFF SIGN | REMARKS
1 |  | BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR 16 BIT ADDITION |  | 
2 |  | BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR 16 BIT SUBTRACTION |  | 
3 |  | BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR 16 BIT MULTIPLICATION |  | 
4 |  | BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR 16 BIT DIVISION: |  | 
5 |  | MOVE A DATA BLOCK WITHOUT OVERLAP |  | 
6 |  | CODE CONVERSION, DECIMAL ARITHMETIC AND MATRIX OPERATIONS.CODE CONVERSIONS – DECIMAL TO HEXADECIMAL |  | 
7 |  | CODE CONVERSION –HEXADECIMAL TO DECIMAL |  | 
8 |  | FLOATING POINT OPERATIONS- STRING MANIPULATI SORTING AND SEARCHING,COPYING A STRING |  | 
9 |  | ASCENDING & DESCENDING |  | 
10 |  | LARGEST& SMALLEST |  | 
11 |  | PASSWORD CHECKING, PRINT RAM SIZE AND SYSTEM |  | 
12 |  | COUNTERS AND TIME DELAY |  | 
13 |  | TRAFFIC LIGHT CONTROL |  | 
14 |  | STEPPER MOTOR INTERFACING |  | 
15 |  | DIGITAL CLOCK |  | 

## Slide 5
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
5
EX. NO | DATE | NAME OF THE EXPERIMENT | STAFF SIGN | REMARKS
16 |  | INTERFACING PRGRAMMABLE KEYBOARD ANDDISPLAY CONTROLLER- 8279 |  | 
17 |  | PRINTER STATUS |  | 
18 |  | A/D AND D/A INTERFACE AND WAVEFORM GENERATION-ADC |  | 
19 |  | INTERFACING DIGITAL – TO – ANALOG CONVERTE |  | 
20 |  | BASIC ARITHMETIC AND LOGICAL OPERATIONS 8 BIT ADDITION |  | 
21 |  | 8 BIT SUBTRACTION |  | 
22 |  | 8 BIT MULTIPLICATION |  | 
23 |  | 8 BIT DIVISION |  | 
24 |  | SQUARE AND CUBE PROGRAM, FIND 2’S COMPLEMENT OF A NUMBER |  | 
25 |  | UNPACKED BCD TO ASCII |  | 

## Slide 6
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
6
EX. NO: 01 DATE :
BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR -16 BIT ADDITION
AIM:
To write an assembly language program to perform addition two 16 bit numbers by an 8 bit number using 8086.
APPARATUS REQUIRED:
ALGORITHM:
bit addition
  Get the first number is specific address.
  Add the second number to the first number.
  Add the two values.
  Store the sum and carry.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIR | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 7
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
7
FLOECHART: ADDITION:
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING

## Slide 8
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
8
PROGRAM FOR ADDITION;
OUTPUT FOR ADDITION:
RESULT:
Thus assembly language programs to perform addition two 16 bit numbers by an 8 bit number using 8086 Performed and the result is stored.
ADDRESS | OPCODE | LABEL | MNEMONICS | COMMENT
1000 |  |  | MOV CX,0000H | Initialize counter CX
1003 |  |  | MOV AX,[1200] | Get the first data in AX register.
1006 |  |  | MOV BX, [1202] | Get the second data in BX register.
100A |  |  | ADD AX,BX | Add the contents of both the register AX & BX
100C |  |  | JNC L1 | Check for carry
100E |  |  | INC CX | If carry exists, increment the CX
100F |  | LI | L1 : MOV [1206],CX | Store the carry
1013 |  |  | MOV [1204], AX | Store the sum
1016 |  | INT-3 | HLT | Stop the program
INPUT | ADDRESS | DATA
 | 1200 1201 1202 1203 | 
OUTPUT | 1204 1205 | 

## Slide 9
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
9
EX. NO: 02 DATE :
BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR - 16 BIT SUBTRACTION
AIM:
To write an assembly language program to perform subtraction two 16 bit numbers by an 8 bit number using 8086.
APPARATUS REQUIRED:
ALGORITHM:
bit SUBTRACTION:
  Initialize the MSBs of difference to 0
  Get the first number
  Subtract the second number from the first number.
  If there is any borrow, increment MSBs of difference by 1.
  Store LSBs of difference.
  Store MSBs of difference.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIR | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 10
VVIT
DEPARTMENT OF ELEC1RONICS AND CO:MMUNICA TION ENGINEERING
CS6412- :MICROPROCESSOR AND :MICROCONTROLLER LABORATORY
10
FLOECHART: SUBTRACTION:
START
IF THERE IS ANY BORROW
YES
..
•
....
+
STOP
STEP UP COUNTER FOR CAR RY | 
GET FIRST DATA | 
ADD SECOND OPERAND FROM MEMORY | 
 |  | INCREMENT COUNT
NO |  | 
 | r | 
STORE THE DIFFERENCE |  | 
STORE THE BORROW |  | 

## Slide 11
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
11
PROGRAM FOR SUBTRACTION:
OUTPUT FOR ADDITION:
RESULT:
Thus assembly language programs to perform subtraction two 16 bit numbers by an 8 bit number using 8086 Performed and the result is stored.
ADDRESS | OPCODE | LABEL | MNEMONICS | COMMENT
1000 |  |  | MOV CX,0000H | Initialize counter CX
1003 |  |  | MOV AX,[1300] | Get the first data in AX register
1006 |  |  | MOV BX, [1302] | Get the second data in BX register.
100A |  |  | SUB AX,BX | Subtract the contents of both the register AX & BX
100C |  |  | JNC A | Check the Borrow.
100E |  |  | INC CX | If carry exists, increment the CX
100F |  | LI | MOV [1306],CX | Store the Borrow.
1013 |  |  | MOV [1304], AX | Store the difference.
1016 |  | INT-3 | HLT | Stop the program
INPUT | ADDRESS | DATA
 | 1300 1301 1302 1303 | 
OUTPUT | 1304 1305 | 

## Slide 12
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
12
EX. NO: 03 DATE :
BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR - 16 BIT MULTIPLICATION
AIM:
To write an assembly language program to perform Multiplication two 16 bit numbers by an 8 bit number using 8086.
APPARATUS REQUIRED:
ALGORITHM:
bit MULTIPLICATION
Multiplication of 16-bit numbers:
  Get the multiplier.
  Get the multiplicand
  Initialize the product to 0.
  Product = product + multiplicand
  Decrement the multiplier by 1.
  If multiplicand is not equal to 0, repeat from step (d) otherwise store the product.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIR | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 13
VVIT
DEPARTMENT OF ELEC1RONICS AND CO:MMUNICA TION ENGINEERING
CS6412- :MICROPROCESSOR AND :MICROCONTROLLER LABORATORY
13
FLOECHART: MULTIPLICATION:
START
GET THE MULTIPLICAND
REGISTER=OO
YES
STOP
REGISTER =REGJSTER MULTIPLICANT |  |  | 
 | MULTIPLIER - 1 |  | 
 | STORE THE RESULT | 

## Slide 14
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
14
PROGRAM FOR MULTIPLICATION:
MULTIPLICATION OUTPUT:
RESULT:
Thus assembly language programs to perform multiplication two 16 bit numbers by an 8 bit number using 8086 Performed and the result is stored.
ADDRESS | OPCODE | LABEL | MNEMONICS | COMMENT
1000 |  |  | MOV AX,1234H | Get the first data in AX register.
1003 |  |  | MOV BX,[1300] | Get the second data in BX register.
1006 |  |  | MUL BX | Multiply AX & BX data
1008 |  |  | INT 3 | Break point.
INPUT |  | 
OUTPUT |  | 

## Slide 15
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
15
EX. NO: 04 DATE :
BASIC ARITHMETIC AND LOGICAL OPERATIONS USING 8086 MICROPROCESSOR - 16 BIT DIVISION:
AIM:
To write an assembly language program to perform division two 16 bit numbers by an 8 bit number using 8086.
APPARATUS REQUIRED:
ALGORITHM:
bit division
Division of 16-bit numbers:
  Get the dividend and divisor.
  Initialize the quotient to 0.
  Dividend = dividend–divisor
  If the divisor is greater, store the quotient
  Go to step 3
  If dividend is greater, quotient = quotient+ repeat from step 4.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIT | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 16
CS6412- :MICROPROCESSOR AND :MICROCONTROLLER LABORATORY
VVIT
DEPARTMENT OF ELEC1RONICS AND CO:MMUNICA TION ENGINEERING
FLOECHART: DIVISION:
START
LOAD DIVlSIOl 2 DIVIDED
QU TlENT = O
DIVIDENT = DTVTDENT- DIVI OR
Q ATTE T Q
TTENT+ 1
TOREQ ATIE TSTOREREMJ _ DER =
DIVIDENT NO CARRY
THERE Ul..T
STOP
16

## Slide 17
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
17
PROGRAM FOR DIVISION:
OUTPUT FOR DIVISION:
RESULT:
Thus assembly language programs to perform division two 16 bit numbers by an 8 bit number using 8086 Performed and the result is stored.
ADDRESS | OPCODE | LABEL | MNEMONICS | COMMENT
1000 |  |  | MOV AX,[1200] | Get the first data in AX register,
1003 |  |  | MOV DX,[1202] | Get the second data in DX register.
1007 |  |  | MOV BX,[1204] | Move the higher order data.
100D |  |  | MOV [1206],AX | Move ax register into address
100B |  |  | DIV DX | Divide the dividend by divisor
1010 |  |  | MOV AX,BX | Copy the lower order data
1012 |  |  | MOV [1208],AX | Store the higher order data.
1015 |  |  | INT 3 | Stop the program.
INPUT | AX= | DX=
OUTPUT | AX= | DX=

## Slide 18
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
18
EX. NO: 05 DATE :
MOVE A DATA BLOCK WITHOUT OVERLAP
AIM:
To move a data block without overlap
APPARATUS REQUIRED:
ALGORITHM:
Initialize the memory location to the data pointer.
Increment B register.
Increment accumulator by 1 and adjust it to decimal every time.
Compare the given decimal number with accumulator value.
When both match, the equivalent hexadecimal value is in B register.
Store the resultant in memory location.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIR | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 19
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
19
PROGRAM:
OUTPUT:
RESULT:
Thus the output for the Move a data block without overlap was executed successfully.
ADDRESS | OPCODES | PROGRAM | COMMENTS
1000 |  | MOV CL, 05 | Get the Data range
1002 |  | MOV SI, 1400 | Get the first data.
1005 |  | MOV DI, 1450 | Get the second data.
1008 |  | LD DSB | Store the lower order product
1009 |  | MOV [DI], AL | Store the result
100B |  | INC DI | Increment the pointer.
100C |  | DEC 1008 | Counter 0
1010 |  | INT 3 | Break point
INPUT |  | OUTPUT | 
1400 |  | 1450 | 
1401 |  | 1451 | 
1402 |  | 1452 | 
1403 |  | 1453 | 
1404 |  | 1454 | 

## Slide 20
VVIT
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
20
EX. NO: 06 DATE :
CODE CONVERSION, DECIMAL ARITHMETIC AND MATRIX OPERATIONS.
Code Conversions –Decimal to Hexadecimal:
AIM:
To convert a given decimal number to hexadecimal.
ALGORITHM:
Initialize the memory location to the data pointer.
Increment B register.
Increment accumulator by 1 and adjust it to decimal every time.
Compare the given decimal number with accumulator value.
When both match, the equivalent hexadecimal value is in B register.
Store the resultant in memory location.

## Slide 21
CS6412- :MICROPROCESSOR AND :MICROCONTROLLER LABORATORY
21
FLOWCHART:
GET DECIMAL DATA IN AL REG ISTER
MOVEALto AH
A D AHWlTR OF
MOVEAHtoBL
OALWlTHFO
10VE A CO . TVALOE 04 to CC
VVIT
DEPARTMENT OF ELEC1RONICS AND CO:MMUNICA TION ENGINEERING
ROTATA THE CO NT OF AL REC. FOUR TI ME
LOAD THE AL REC.M LTIPLEOA to BH REC.
MULTTPLE AL WTTH BH THE PROD UCT AL
ADD UNJT(BL) PRODUCT ALTO GO AH REG.HEXA
DECIMAL DATAl. AL REC.

## Slide 22
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
22
PROGRAM:
OUTPUT:[DECIMAL TO HEXADECIMAL]
RESULT:
Thus the output for the code conversions –decimal to hex was executed successfully.
ADDRESS | OPCODE | LABEL | MNEMONICS | COMMENDS
1000 |  |  | MOV AL, [1100] | Move data block AL
1003 |  |  | MOV AH, AL | Move data lower to higher
1005 |  |  | MOV AH, OF | Move data OF into AH
1008 |  |  | MOV BL, AH | Move data BL into AH
100A |  |  | AND AL, FO | AND the data AL to FO
100C |  |  | MOV CL, 04 | Move data 04 to CL block
100E |  |  | ROR AL, CL | Rotate functions CL and AL
1010 |  |  | MOV BH, OA | Move data OA into BH
1012 |  |  | MUL BH | Multiply BH
1014 |  |  | ADD AL, BL | ADD the data AL And BL
1016 |  |  | MOV [2000], AL | Move the store data
1019 |  |  | INT-3 | Halt program
DATA | ADRESS | DATA
INPUT |  | 
OUTPUT |  | 

## Slide 23
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
23
EX. NO: 07 DATE :
CODE CONVERSION –HEXADECIMAL TO DECIMAL
AIM:
To convert a given hexadecimal number to decimal.
ALGORITHM:
Initialize the memory location to the data pointer.
Increment B register.
Increment accumulator by 1 and adjust it to decimal every time.
Compare the given hexadecimal number with B register value.
When both match, the equivalent decimal value is in A register.
Store the resultant in memory location.

## Slide 24
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
24
PROGRAM;
ADDRESS | OPCODE | LABEL | MNEMONICS | COMMENTS
1000 |  |  | MOV AL, [1100] | Move date to AL REG
1003 |  |  | MOV DX, AL | Move data AL TO DX
1006 |  | HUND | MOV AL, 64 | Move data to AX REG
1008 |  |  | JC TEN | Jump carry
100A |  |  | SUB AL, 64 | Subtract data
100C |  |  | INC DL | Increment DL
100E |  |  | JUP HUND | JUMP label data
1010 |  | TEN | CMP AL, OA | Compare register
1012 |  |  | JC UNIT | Jump carry
1014 |  |  | SUB AL,OA | Subtract data
1016 |  |  | INC DH | Increment DH
1018 |  |  | JC TEN | JUMP carry
101A |  | UNIT | MOV [200],DL | Move data to DL
101E |  |  | MOV [200],DH | Move data to DH
1022 |  |  | MOV [200],AL | Move data to AL
1025 |  |  | MOV [200],AH | Move data to AH
1027 |  |  | HLT | Stop the program

## Slide 25
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
25
OUTPUT:[ HEXADECIMAL NUMBER TO DECIMAL]:
RESULT:
Thus the output for the addition code conversions –decimal to hex was executed successfully.
 | INPUT | OUTPUT
MEMORY |  | 
DATA |  | 

## Slide 26
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
26
EX. NO: 08 DATE :
FLOATING POINT OPERATIONS- STRING MANIPULATIONS, SORTING AND SEARCHING
Copying a String:
AIM:
To move a string of length FF from source to destination.
ALGORITHM:
Initialize the data segment .(DS)
Initialize the extra data segment .(ES)
Initialize the start of string in the DS. (SI)
Initialize the start of string in the ES. (DI)
Move the length of the string (FF) in CX register.
Move the byte from DS TO ES, till CX=0.

## Slide 27
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
27
FLOECHART:
START
+
lNlTIALlZETHE POINTER TO MEMORYWHRE DATA TO BE TRANSFERED
lr
LOAD THE AL REG.WITH DATA FROM MEMORY
JNJTIALJZE DATA SESTINATION POINTER TO MEMORY WHERE DATA TO BE STORED
STORE DATE FROM AL REG.
STOP

## Slide 28
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
28
PROGRAM:
OUTPUT : [ COPYING A STRING]:
RESULT:
Thus a string of a particular length is moved from source segment to destination segment.
ADDRESS | OPCODES | PROGRAM |  | COMMENTS
1000 |  | MOV | SI,1200H | Initialize destination address
1003 |  | MOV | DI,1300H | Initialize starting address.
1006 |  | MOV | CX,0006H | Initialize array size
1008 |  | CLD |  | Clear direction flag
100A |  | REP | MOVSB | Copy the contents of source into destination until count reaches zero
100C |  | HLT |  | Stop
INPUT |  | OUTPUT | 
1400 |  | 1450 | 
1401 |  | 1451 | 
1402 |  | 1452 | 
1403 |  | 1453 | 
1404 |  | 1454 | 

## Slide 29
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
29
EX. NO: 09 DATE :
ASCENDING & DESCENDING
AIM:
To write an Assembly Language Program (ALP) to sort a given array in ascending and descending order.
APPARATUS REQUIRED:
PROBLEM STATEMENT:
An array of length 10 is given from the location. Sort it into descending and ascending order and store the result.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIR | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 30
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
30
ALGORITHM:
Sorting in ascending order:
Load the array count in two registers C1 and C2.
Get the first two numbers.
Compare the numbers and exchange if necessary so that the two numbers are in ascending order.
Decrement C2.
Get the third number from the array and repeat the process until C2 is 0.
Decrement C1 and repeat the process until C1 is 0.
Sorting in descending order:
Load the array count in two registers C1 and C2.
Get the first two numbers.
Compare the numbers and exchange if necessary so that the two numbers are in descending order.
Decrement C2.
Get the third number from the array and repeat the process until C2 is 0.
Decrement C1 and repeat the process until C1 is 0.

## Slide 31
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
31
FLOECHART: [ASCENDING]:
ST.4JU
'f
GET THE FIRST DATA TO COMPARE WITH THE SECOND DATA
YES
_..
IF SECOND DATA IN ASCENDIJiG
ORDER
NO
..
•
DO ABOVE COMPARITION AS MANY TIME AS THE COUNT
FINALLY THE ARRAY IS ASCENDING ORDER
(
STOP
)
NO SWAP | 
SWAPTHEDATABY ASCEND1"1G ORDER | 
 | COMPARE THE OTHER DATA TYPE UPTOCOUNT | 

## Slide 32
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
32
FLOWCHART :[DECENDING]:
START
'
GET THE FIRST DATA TO COl\iPARE WITH THE SECOND DATA
YES
NO
IF SECOND DATA IN DESCENDING
ORDER
..
NO SWAP
'
COMPARE THE OTHER DATA TYPE UPTOCOUNT
•
DO ABOVE COMPARITION AS MANY TIME AS THE COUNT
FINALLY THE ARRAY IS ASCENDING ORDER
(
STOP
)
SWAPTHEDATABY DESCENDING ORDER | 

## Slide 33
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
33
PROGRAM FOR ASCENDING ORDER:
ADDRESS | OPCODES | PROGRAM | COMMENTS
1000 |  | MOV SI,1200H | Initialize memory location for array size
1002 |  | MOV CL,[SI] | Number of comparisons in CL
1004 |  | L4 : MOVSI,1200H | Initialize memory location for array size
1006 |  | MOV DL,[SI] | Get the count in DL
1007 |  | INC SI | Go to next memory location
1009 |  | MOV AL,[SI] | Get the first data in AL
100B |  | L3 : INC SI | Go to next memory location
100E |  | MOV BL,[SI] | Get the second data in BL
1010 |  | CMP AL,BL | Compare two data’s
1012 |  | JNB L1 | If AL < BL go to L1
1014 |  | DEC SI | Else, Decrement the memory location
1016 |  | MOV [SI],AL | Store the smallest data
1018 |  | MOV AL,BL | Get the next data AL
1019 |  | JMP L2 | Jump to L2
101A |  | L1 : DEC SI | Decrement the memory location
101C |  | MOV [SI],BL | Store the greatest data in memory location
101E |  | L2 : INC SI | Go to next memory location
1020 |  | DEC DL | Decrement the count
1022 |  | JNZ L3 | Jump to L3, if the count is not reached
1024 |  | MOV [SI],AL | Store data in memory location
1026 |  | DEC CL | Decrement the count
1028 |  | JNZ L4 | Jump to L4, if the count is not reached zero
1029 |  | HLT | Stop

## Slide 34
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
34
PROGRAM FOR DESCENDING ORDER:
ADDRESS | OPCODES | PROGRAM | COMMENTS
1000 |  | MOV SI,1200H | Initialize memory location for array size
1002 |  | MOV CL,[SI] | Number of comparisons in CL
1004 |  | L4 : MOVSI,1200H | Initialize memory location for array size
1006 |  | MOV DL,[SI] | Get the count in DL
1007 |  | INC SI | Go to next memory location
1009 |  | MOV AL,[SI] | Get the first data in AL
100B |  | L3 : INC SI | Go to next memory location

## Slide 35
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
35
OUTPUT FOR ASCENDING:
OUTPUT FOR DESCENDING ORDER:
RESULT:
Thus given array of numbers are sorted in ascending & descending order.
 | DATA |  |  |  |  | 
INPUT |  |  |  |  |  | 
OUTPUT |  |  |  |  |  | 
 | DATA |  |  |  |  | 
INPUT |  |  |  |  |  | 
OUTPUT |  |  |  |  |  | 

## Slide 36
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
36
EX. NO: 10 DATE :
LARGEST& SMALLEST
AIM:
To write an Assembly Language Program(ALP) to find the largest and smallest number in a given array.
APPARATUS REQUIRED:
PROBLEM STATEMENT:
An array of length 5 is given from the location. Find the largest and smallest number and store the result.
S.NO | ITEM | SPECIFICATION | QUANTITY
1. | MICROPROCESSOR KIR | 8086 KIT | 1
2. | POWER SUPPLY | + 5 V DC | 1
3. | KEY BOARD | - | 1

## Slide 37
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
37
ALGORITHM:
(i) Finding largest number:
Load the array count in a register C1.
Get the first two numbers.
Compare the numbers and exchange if the number is small.
Get the third number from the array and repeat the process until C1 is 0.
(ii) Finding smallest number:
Load the array count in a register C1.
Get the first two numbers.
Compare the numbers and exchange if the number is large.
Get the third number from the array and repeat the process until C1 is 0.

## Slide 38
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
38
FLOECHART: [LARGEST]
(sTART
+
•
11;'
NO
COllNT IS NOT '0'
TillN CONTINUE FROJ\>I
THESTEPl
YES
(
STOP
TAKE THHE FIRST UMHER OF ARRAY | 
COMPARE WlTHTillNEXTNUMBER |  |  | 
TAKJ;: THE BIGGEST OF THE TWO NUMBER |  |  | 
 | DECREMENT COUNT |  | 
STORE THE RESULT |  |  | 

## Slide 39
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
39
FLOECHART:[SMALLEST]

## Slide 40
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
40
PROGRAM FOR FINDING LARGEST NUMBER:
ADDRESS | OPCODES | PROGRAM | COMMENDS
1000 |  | MOV SI,1200H | Initialize array size
1002 |  | MOV CL,[SI] | Initialize the count
1004 |  | INC SI | Go to next memory location
1006 |  | MOV AL,[SI] | Move the first data in AL
1007 |  | DEC CL | Reduce the count
1009 |  | L2 : INC SI | Move the SI pointer to next data
100B |  | CMP AL,[SI] | Compare two data’s
100E |  | JNB L1 | If AL > [SI] then go to L1 ( no swap)
1010 |  | MOV AL,[SI] | Else move the large number to AL
1012 |  | L1 : DEC CL | Decrement the count
1014 |  | JNZ L2 | If count is not zero go to L2
1016 |  | MOV DI,1300H | Initialize DI with 1300H
1018 |  | MOV [DI],AL | Else store the biggest number in 1300 location
1010 |  | HLT | Stop

## Slide 41
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
41
PROGRAM FOR FINDING SMALLEST NUMBER:
ADDRESS | OPCODES | PROGRAM | COMMENDS
1000 |  | MOV SI,1200H | Initialize array size
1002 |  | MOV CL,[SI] | Initialize the count
1004 |  | INC SI | Go to next memory location
1006 |  | MOV AL,[SI] | Move the first data in AL
1007 |  | DEC CL | Reduce the count
1009 |  | L2 : INC SI | Move the SI pointer to next data
100B |  | CMP AL,[SI] | Compare two data’s
100E |  | JB L1 | If AL < [SI] then go to L1 ( no swap)
1010 |  | MOV AL,[SI] | Else move the large number to AL
1012 |  | L1 : DEC CL | Decrement the count
1014 |  | JNZ L2 | If count is not zero go to L2
1016 |  | MOV DI,1300H | Initialize DI with 1300H
1018 |  | MOV [DI],AL | Else store the biggest number in 1300 location
1010 |  | HLT | Stop

## Slide 42
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
42
OUTPUT FOR LARGESTNUMBER:
OUTPUT FOR SMALLEST NUMBER:
RESULT:
Thus largest and smallest number is found in a given array.
 | DATA |  |  |  |  | 
INPUT |  |  |  |  |  | 
OUTPUT |  |  |  |  |  | 
 | DATA |  |  |  |  | 
INPUT |  |  |  |  |  | 
OUTPUT |  |  |  |  |  | 

## Slide 43
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
43
EX. NO: 11 DATE :
PASSWORD CHECKING
AIM:
To write an Assembly Language Program (ALP) for performing the Arithmetic operation of two byte numbers
APPARATUS REQUIRED:
PROGRAM:
; PASSWORD IS MASM1234 DATA SEGMENT
PASSWORD DB 'MASM1234' LEN EQU ($-PASSWORD)
MSG1 DB 10, 13,'ENTER YOUR PASSWORD: $'
MSG2 DB 10, 13,' WELCOME TO ELECTRONICS WORLD!!$' MSG3 DB 10, 13,'INCORRECT PASSWORD!$'
NEW DB 10, 13,'$'
INST DB 10 DUP (0) DATA ENDS
CODE SEGMENT
SL .No | ITEM | SPECIFICATION | QUANTITY
1. | Microprocessor kit | 8086 kit | 1
2. | Power Supply | +5 V dc | 1

## Slide 44
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
44
ASSUME CS: CODE, DS: DATA START:
MOV AX, DATA MOV DS, AX
LEA DX, MSG1 MOV AH, 09H INT 21H
MOV SI, 00 UP1:
MOV AH, 08H INT 21H
CMP AL, 0DH JE DOWN
MOV [INST+SI], AL MOV DL,'*'
MOV AH, 02H
INT 21H INC SI JMP UP1 DOWN:
MOV BX, 00 MOV CX, LEN CHECK:
MOV AL,[INST+BX]
MOV DL,[PASSWORD+BX] CMP AL, DL
JNE FAIL

## Slide 45
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
45
INC BX LOOP CHECK
LEA DX, MSG2 MOV AH, 09H
INT 21H
JMP FINISH FAIL:
LEA DX, MSG3 MOV AH, 009H INT 21H FINISH:
INT 3 CODE ENDS END START END
RESULT:
Thus the output for the Password checking, Print RAM size and system date was executed successfully

## Slide 46
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
46
EX.NO: 12 DATE :
COUNTERS AND TIME DELAY
AIM:
To write an assembly language program in 8086 to Counters and Time Delay
APPARATUS REQUIRED:
PROGRAM:
.MODEL SMALL
.DATA
MSGIN DB 'Enter delay duration (0-50): $' MSG1 DB 'This is Microprocessor! $' DELAYTIME DW 0000H
.CODE
MOV DX,@DATA MOV DS, DX LEA DX, MSGIN MOV AH, 09H INT 21H
IN1:
SL .No | ITEM | SPECIFICATION | QUANTITY
1. | Microprocessor kit | 8086 kit | 1
2. | Power Supply | +5 V dc | 1

## Slide 47
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
47
MOV AH, 01H INT 21H
CMP AL, 0DH JE NXT
SUB AL, 30H MOV DL, AL MOV AX, BX MOV CL, 0AH MUL CL
MOV BX, AX AND DX, 00FFH ADD BX, DX
MOV DELAYTIME, BX LOOP IN1
NXT:
MOV CX, DELAYTIME MOV DL, 10
MOV AH, 02H INT 21H
LEA SI, MSG1
;
LP:
MOV DL,[SI] CMP DL,'$' JE NXT2
MOV AH, 02H INT 21H
ADD SI, 1 POP DX
PUSH DX
MOV DI, DELAYTIME MOV AH, 0
INT 1Ah MOV BX, DX
Delay: MOV AH, 0 INT 1Ah

## Slide 48
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
48
SUB DX, BX CMP DI, DX
JA Delay LOOP LP
NXT2:
MOV AH, 4CH INT 21H
END
RESULT:
Thus the output for the Counters and Time Delay was executed successfully

## Slide 49
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
49
EXP.NO: 13 DATE :
TRAFFIC LIGHT CONTROL
AIM:
To write an assembly language program in 8086 to Traffic light control
APPARATUS REQUIRED:
PROGRAM;
Log into System.
Select control type.
If Automatic mode select then go to step 4th else go to step 8.
If Automatic control activated.
Assign time period for green, yellow signal.
If emergency vehicle is over then go to step 4.
If rally come then go to step 8.
Manual control activated.
Assign time period for green, yellow signal according to that particular road.
If emergency over then go to step 4.
SL .No | ITEM | SPECIFICATION | QUANTITY
1. | Microprocessor kit | 8086 kit | 1
2. | Power Supply | +5 V dc | 1

## Slide 50
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
50
MODEL GRAPH FOR TRAFFIC LIGHT CONTROL:

## Slide 51
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
51
ASSEMBLY LANGUAGE PROGRAM FOR TRAFFIC LIGHT CONTROL:

ADDRESS | OPCODE | LABEL | MNEMONICS
1000 |  |  | MVI A,80
1002 |  |  | OUT CWR
1004 |  | REPEAT | MVI E, 03
1006 |  |  | LXI H, C100
1007 |  | NEXTSTAT | MOV A, M
1009 |  |  | OUT PORRTA
100B |  |  | INX H
100E |  |  | MOV A, M
1010 |  |  | OUT PORTB
1012 |  |  | INX H
1014 |  |  | MOV A,M
1016 |  |  | OUT PORT C
1018 |  |  | CALL DELAY
1019 |  |  | INX H
101A |  |  | DCR E
101C |  |  | JNZ NEXTSTAT
101E |  |  | JMP REPEAT
1022 |  | DELAY | LXI D, 3000
1024 |  | L2 | MVI C,FF
1026 |  | L1 | DCR C
1028 |  |  | JNZ L1
1029 |  |  | DCR D
1000 |  |  | MOV A, D
1002 |  |  | ORA E
1004 |  |  | JNZ L2
1006 |  |  | RET

## Slide 52
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
52
RESULT:
Thus the assembly language program for traffic light control is verified

## Slide 53
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
53
EX. NO: 14 DATE :
STEPPER MOTOR INTERFACING
AIM:
To write an assembly language program in 8086 to rotate the motor at different speeds.
APPARATUS REQUIRED:
PROBLEM STATEMENT:
Write a code for achieving a specific angle of rotation in a given time and particular number of rotations in a specific time.
THEORY:
A motor in which the rotor is able to assume only discrete stationary angular position is a stepper motor. The rotary motion occurs in a stepwise manner from one equilibrium position to the next. Two-phase scheme: Any two adjacent stator windings are energized. There are two magnetic fields active in quadrature and none of the rotor pole faces can be in direct alignment with the stator poles. A partial but symmetric alignment of the rotor poles is of course possible.
SL.NO | ITEM | SPECIFICATION | QUANTITY
1. | Microprocessor kit | 8086 | 1
2. | Power Supply | +5 V, dc,+12 V dc | 1
3. | Stepper Motor Interface board | - | 1
4. | Stepper Motor | - | 1

## Slide 54
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
54
ALGORITHM:
For running stepper motor clockwise and anticlockwise directions





Get the first data from the lookup table.
Initialize the counter and move data into accumulator. Drive the stepper motor circuitry and introduce delay
Decrement the counter is not zero repeat from step(iii)
Repeat the above procedure both for backward and forward directions.
SWITCHING SEQUENCE OF STEPPER MOTOR:
MEMORY LOCATION | A1 | A2 | B1 | B2 | HEX CODE
4500 | 1 | 0 | 0 | 0 | 09 H
4501 | 0 | 1 | 0 | 1 | 05 H
4502 | 0 | 1 | 1 | 0 | 06 H
4503 | 1 | 0 | 1 | 0 | 0A H

## Slide 55
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
55
FLOWCHART:
( ST.A.H:r)
INITIALIZE COUNTER FOR LOOK Ul' DATA
GETTifEFIRST DATA FROM THt:ACCUMULATOR
l
"'
MOVE DATA TO ACCUMULATOR
+
DRIVE THt: MOTOR DELAY
..
( DELAY 0
•
DECREI\11£NT THE COUNTER
u
NO
li=IJ
a:;s
STORE THE .Rt.:SULT
..I .
( STOP

## Slide 56
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
56
PROGRAM FOR STEPPER MOTOR CONTOL;
RESULT:
Thus the assembly language program for rotating stepper motor in both clockwise and anticlockwise directions is written and verified.
ADDRESS | OPCODE | PROGRAM | COMMENTS
1000 |  | START : MOV DI, 1200H | Initialize memory location to store the array of number
1002 |  | MOV CX, 0004H | Initialize array size
1004 |  | LOOP 1 : MOV AL,[DI] | Copy the first data in AL
1006 |  | OUT 0C0,AL | Send it through port address
1007 |  | MOV DX, 1010H | Introduce delay
1009 |  | L1 : DEC DX | Declare DX
100B |  | JNZ L1 | JUNP no zero
100E |  | INC DI | Increment DI
1010 |  | LOOP LOOP1 | Go to next memory location
1012 |  | JMP START | Loop until all the data’s have been sent Go to start location for continuous rotation
1014 |  | 1200 : 09,05,06,0A | Array of data’s

## Slide 57
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
57
EX. NO: 15 DATE :
DIGITAL CLOCK
AIM:
To display the digital clock specifically by displaying the hours, minutes and seconds using 8086 kits
APPARATUS REQUIRED:
PRELIMINARY SETTINGS:
Store time value in memory location 1500- Seconds
1501- Minutes
1502- Hours
S.NO | ITEM | SPECIFICATION
1 | Microprocessor kit | 8086
2 | Power Supply | 5V

## Slide 58
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
58
DIGITAL CLOCK PROGRAM:
MEMORY | OPCODE | LABEL | MNEMONICS
1000 |  | START | 
1000 |  |  | CALL CONVERT
1003 |  |  | CALL DISPLAY
1006 |  | DELAY | MOV AL, 0B0H
1009 |  |  | OUT 16H, AL
100B |  |  | MOV CL, 07H
100E |  | S2 | MOV AL, 88H
1011 |  |  | OUT 14H, AL
1013 |  |  | MOV AL, 80H
1016 |  |  | OUT 14H, AL
1018 |  | S1 | MOV AL, 80H
101B |  |  | OUT 16H, AL
101D |  |  | NOP
101E |  |  | NOP
101F |  |  | NOP
1020 |  |  | NOP
1021 |  |  | IN AL, 14H
1023 |  |  | MOV DL, AL
1025 |  |  | IN AL, 14H
1027 |  |  | OR AL,DL
1029 |  |  | JNZ S1
102B |  |  | DEC CL

## Slide 59
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
59
102D |  |  | JNZ S2
102F |  |  | MOV SI, 1500H
1033 |  |  | MOV AL.[SI]
1035 |  |  | INC AL
1037 |  |  | MOV [SI],AL
1039 |  |  | CMP AL, 3CH
103C |  |  | JNZ START
103E |  |  | MOV AL, 00H
1041 |  |  | MOV[SI], AL
1043 |  |  | INC AL
1044 |  |  | MOV [SI],AL
1046 |  |  | CMP AL,3CH
1048 |  |  | JNZ START
1041 |  |  | MOV AL, 0
104D |  |  | MOV AL, [SI]
104F |  |  | MOV AL, O
1052 |  |  | MOV [SI],AL
1054 |  |  | INC SI
1055 |  |  | MOV AL, [SI]
1057 |  |  | CMP AL, 18H
1059 |  |  | JNZ START
105B |  |  | MOV AL, 0
105E |  |  | MOV SI,AL
1060 |  |  | MOV AL,0
1063 |  |  | MOV [SI],AL

## Slide 60
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
60
1065 |  |  | JMP | START
1068 |  | DISPLAY | MOV | AH, 06H
106B |  |  | MOV | DX, 1600H
106F |  |  | MOV | CH, 01
1072 |  |  | MOV | CL , 01
1075 |  |  | INT | 5
1077 |  |  | RET | 
1078 | CONVERT |  | MOV | SI, 1500H
107C |  |  | MOV | BX, 1608H
1080 |  |  | MOV | AL, 24
1080 |  |  | MOV | [BX,] AL
SECONDS |  |  |  | 
1085 |  |  | MOV | AL, SI
1087 |  |  | MOV | AH, 0
108A |  |  | MOV | DH, 0AH
108D |  |  | DIV | DH
108F |  |  | ADD | AH, 30H
1092 |  |  | DEC | BX
1093 |  |  | MOV | [BX], AH
1095 |  |  | DEC | BX
1096 |  |  | ADD | AL, 30H
1098 |  |  | HLT | 

## Slide 61
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
61
RESULT;
Thus the digital clock program has been written and executed using 8086 microprocessor kit and the output of digital clock was displayed as [hours: minutes: seconds] successfully.

## Slide 62
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
62
EX. NO: 16 DATE :
INTERFACING PRGRAMMABLE KEYBOARD AND DISPLAY CONTROLLER- 8279
AIM :
To display the rolling message “HELP US “ in the display.
APPARATUS REQUIRED:
8086 Microprocessor kit, Power supply, interfacing board.
ALGORITHM :
Display of rolling message “HELP US “
Initialize the counter
Set 8279 for 8 digit character display, right entry
Set 8279 for clearing the display
Write the command to display
Load the character into accumulator and display it
Introduce the delay
Repeat from step 1.

## Slide 63
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
63
PROGRAM:
MEMORY LOCATION | OPCODES | PROGRAM | COMMENDS
1000 |  | START : MOV SI,1200H | Initialize array
1000 |  | MOV CX,000FH | Initialize array size
1003 |  | MOV AL,10 | Store the control word for display mode
1006 |  | OUT C2,AL | Send through output port
1009 |  | MOV AL,CC | Store the control word to clear display
100B |  | OUT C2,AL | Send through output port
100E |  | MOV AL,90 | Store the control word to write display
1011 |  | OUT C2,AL | Send through output port
1013 |  | L1 : MOV AL,[SI] | Get the first data
1016 |  | OUT C0,AL | Send through output port
1018 |  | CALL DELAY | Give delay
101B |  | INC SI | Go & get next data
101D |  | LOOP L1 | Loop until all the data’s have been taken
101E |  | JMP START | Go to starting location
101F |  | DELAY : MOV DX,0A0FFH | Store 16bit count value
1020 |  | LOOP1 : DEC DX | Decrement count value
1021 |  | JNZ LOOP1 | Loop until count values becomes zero
1023 |  | RET | Return to main program

## Slide 64
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
64
1. Display Mode Setup: Control word-10 H
0
0
0
1
0
0
0
0
DD-00- 8Bit character display left entry 01- 16Bit character display left entry
10- 8Bit character display right entry 11- 16Bit character display right entry
KKK- Key Board Mode 000-2Key lockout.
2.Clear Display: Control word-DC H
1
1
0
1
1
1
0
0
11
A0-3; B0-3 =F
1-Enables Clear display
0-Contents of RAM will be displayed
1-FIFO Status is cleared
1-Clear all bits (Combined effect of CD)
0 | 0 | 0 | D | D | K | K | K
1 | 1 | 0 | CD | CD |  | CD |  | CF | CA

## Slide 65
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
65
3. Write Display: Control word-90H
1
0
0
1
0
0
0
0
1
0
0
AI
A
A
A
A
Selects one of the 16 rows of display.
Auto increment = 1, the row address selected will be incremented after each of read and write operation of the display RAM.

## Slide 66
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
66
FLOWCHART:
(sTART)
SETUP POINTER
·
i
SE 8279 CLEARING DISPLAY
•
+
lN1TlALIZE THE COUNTER | 
SET 8279 CHARECTER DISPLAY | 
WRITE COMMAND DISPLAY |  |  | 
 | DELAY |  | 

## Slide 67
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
67
SEGMENT DEFINITION:
RESULT:
Thus the rolling message “HELP US” is displayed using 8279 interface kit.
DATA BUS | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
SEGMENTS | d | c | b | a | d | g | f | e

## Slide 68
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
68
EX. NO: 17 DATE :
PRINTER STATUS
AIM:
To determine the printer status.
APPARATUS REQUIRED:
PROGRAM:
XOR AX, AX
XOR BX, BX
; This divides my 3digit number my, hundredth digit
MOV AX, RES MOV BX, 100 DIV BX
; prints the hundredth digit
ADD AL, '0' MOV DL, AL
PUSH AX; save AX on the stack MOV AH, 02h
by 100 giving me
INT 21h
S.NO | ITEM | SPECIFICATION
1 | Microprocessor kit | 8086
2 | Power Supply | 5V

## Slide 69
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
69
POP AX; restore ax
; divides the remainder digit
by 10 giving
me my tens
MOV BX, 10
DIV BX
; prints my tens digit ADD AL, '0'
MOV DL, AL
PUSH AX; save AX on the stack
MOV AH, 02h INT 21h
POP AX; restore ax
; print my last remainder which ADD AH, '0'
MOV DL, AH MOV AH, 02h INT 21h
is my ones
RESULT:
Thus the output for the Move a data block without overlap was executed successfully.

## Slide 70
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
70
EX. NO: 18 DATE :
A/D AND D/A INTERFACE AND WAVEFORM GENERATION. ADC
AIM:
To write an assembly language program to convert an analog signal into a digital signal using an ADC interfacing.
APPARATUS REQUIRED:
THEORY:
An ADC usually has two additional control lines: the SOC input to tell the ADC when to start the conversion and the EOC output to announce when the conversion is complete.
ALGORITHM:
Select the channel and latch the address.
Send the start conversion pulse.
Read EOC signal.
If EOC = 1 continue else go to step (iii)
Read the digital output.
Store it in a memory location.
SL.NO | ITEM | SPECIFICATION | QUANTITY
1. | Microprocessor kit | 8086 | 1
2. | Power Supply | +5 V dc,+12 V dc | 1
3. | ADC Interface board | - | 1

## Slide 71
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
71
PROGRAM:
MEMORY LOCATION | OPCODES | PROGRAM |  |  | COMMENTS
1000 |  | MOV | AL,00 |  | Load accumulator with value for ALE high
1000 |  | OUT | 0C8H,AL |  | Send through output port
1003 |  | MOV | AL,08 |  | Load accumulator with value for ALE low
1006 |  | OUT | 0C8H,AL |  | Send through output port
1009 |  | MOV | AL,01 |  | Store the value to make SOC high in the accumulator
100B |  | OUT | 0D0H,AL |  | Send through output port
100E |  | MOV | AL,00 |  | Introduce delay
1011 |  | MOV AL,00 |  |  | 
1013 |  | MOV AL,00 |  |  | 
1016 |  | MOV AL,00 |  |  | 
1018 |  | OUT | 0D0H,AL |  | Store the value to make SOC low the accumulator
101B |  | L1 : IN AL, |  | 0D8H | Send through output port
101D |  | AND AL,01 |  |  | Read the EOC signal from port & check for end of conversion
101E |  | CMP AL,01 |  |  | 
101F |  | JNZ L1 |  |  | 

## Slide 72
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
72
1020 |  | IN AL,0C0H | from port again
1021 |  | MOV BX,1100 | Read data from port
1023 |  | MOV [BX],AL | Initialize the memory location to store data
1025 |  | HLT | Store the data and halt program

## Slide 73
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
FLOWCHART:
START
NO
STOP
73
SELECT THE CHANNEL AND .LENGTH | 
SEND THE START CONVERSION PULSE | 
 | YES
READ THE DIGITAL OUTPUT | 
STORE THE DIGITAL VALUE IN THE MEMORY LOCATION SPECIFIED |  |  | 

## Slide 74
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
74
OUTPUT:
RESULT:
Thus the ADC was interfaced with 8086 and the given analog inputs were converted into its digital equivalent.
ANALOG VOLTAGE | DIGITAL DATA ON LED DISPLAY | HEX CODE IN MEMORY LOCATION

## Slide 75
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
75
EX. NO: 19 DATE :
INTERFACING DIGITAL – TO – ANALOG CONVERTER
AIM:
To write an assembly language program for digital to analog conversion
To convert digital inputs into analog outputs & To generate different waveforms
APPARATUS REQUIRED:
PROBLEM STATEMENT:
The program is executed for various digital values and equivalent analog voltages are measured and also the waveforms are measured at the output ports using CRO.
THEORY:
Since DAC 0800 is an 8 bit DAC and the output voltage variation is between –5v and +5v. The output voltage varies in steps of 10/256 = 0.04 (approximately). The digital data input and the corresponding output voltages are presented in the table. The basic idea behind the generation of waveforms is the continuous generation of analog output of DAC. With 00 (Hex) as input to DAC2 the analog output is –5v. Similarly with FF H as input, the output is +5v. Outputting digital data 00 and FF at regular intervals, to DAC2, results in a square wave of amplitude 5v.Output digital data from 00 to FF in constant steps of 01 to DAC2. Repeat this sequence again and again. As a result a saw-tooth wave will be generated at DAC2 output. Output digital data from 00 to FF in constant steps of 01 to DAC2. Output digital data from FF to 00 in constant steps of 01 to DAC2.
SL.NO | ITEM | SPECIFICATION | QUANTITY
1. | Microprocessor kit | 8086 Vi Microsystems | 1
2. | Power Supply | +5 V, dc,+12 V dc | 1
3. | DAC Interface board | - | 1

## Slide 76
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
76
FLOECHART:
START
'
SEND THE DIGITAL VALUE TO ACCUMLATOR
TRANSFER THE ACCUMLATOR
'
READ THE CORRESPONDING ANALOG VALUE
STOP

## Slide 77
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
77
ALGORITHM:
Measurement of analog voltage:
Send the digital value of DAC.
Read the corresponding analog value of its output.
Waveform generation:
Square Waveform:
Send low value (00) to the DAC.
Introduce suitable delay.
Send high value to DAC.
Introduce delay.
Repeat the above procedure. Saw-tooth waveform:
Load low value (00) to accumulator.
Send this value to DAC.
Increment the accumulator.
Repeat step (ii) and (iii) until accumulator value reaches FF.
Repeat the above procedure from step 1. Triangular waveform:
(i)
(ii)
(iii)
Load the low value (00) in accumulator. Send this accumulator content to DAC. Increment the accumulator.
(iv) Repeat step 2 and 3 until the accumulator reaches FF, decrement the accumulator and send the accumulator contents to DAC.
MEASUREMENT OF ANALOG VOLTAGE:
PROGRAM | COMMENTS
MOV AL,7FH | Load digital value 00 in accumulator
OUT C0,AL | Send through output port
HLT | Stop

## Slide 78
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
78
PROGRAM TABLE: saw tooth wave
DIGITAL DATA | ANALOG VOLTAGE
PROGRAM | COMMENTS
L2: MOV AL,00H | Load 00 in accumulator
OUT C0,AL | Send through output port
CALL L1 | Give a delay
MOV AL,FFH | Load FF in accumulator
OUT C0,AL | Send through output port
CALL L1 | Give a delay
JMP L2 | Go to starting location
L3: MOV CX,05FFH | Load count value in CX register
L1: LOOP L3 | Decrement until it reaches zero
RET | Return to main program

## Slide 79
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
79
PROGRAM TABLE: Square Wave
PROGRAM TABLE: Triangular Wave
PROGRAM | COMMENTS
L2; OUT C0,AL | Load 00 in accumulator
CALL L1 | Send through output port
MOV AL,FFH | Give a delay
OUT C0,AL | Load FF in accumulator
CALL L1 | Send through output port
JMP L2 | Give a delay
L1 | Load 00 in accumulator
L3 | Send through output port
RET | return
PROGRAM |  | COMMENTS
L3 |  | Load 00 in accumulator
L1 |  | Send through output port
INC | AL | Increment contents of accumulator
JNZ | L1 | Send through output port until it reaches FF
MOV | AL,0FFH | Load FF in accumulator
L2 |  | Send through output port
DEC | AL | Decrement contents of accumulator
JNZ | L2 | Send through output port until it reaches 00
JMP | L3 | Go to starting location
L3 |  | Load 00 in accumulator

## Slide 80
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
80
WAVEFORM GENERATION:
RESULT
Thus the DAC was interfaced with 8085 and different waveforms have been generated.
WAVEFORMS | AMPLITUDE | TIMEPERIOD
Square Waveform |  | 
Saw-tooth waveform |  | 
Triangular waveform |  | 

## Slide 81
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
81
EX. NO: 20 DATE :
BASIC ARITHMETIC AND LOGICAL OPERATIONS 8 BIT ADDITION
AIM:
To write a program to add two 8-bit numbers using 8051 microcontroller.
ALGORITHM:
Clear Program Status Word.
Select Register bank by giving proper values to RS1 & RS0 of PSW.
Load accumulator A with any desired 8-bit data.
Load the register R 0 with the second 8- bit data.
Add these two 8-bit numbers.
Store the result.
Stop the program.

## Slide 82
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
82
FLOWCHART:
(sTART)
+
STOP
 | CLEARPSW |  | 
 |  |  | lr
SELECT REGISTER |  |  | 
 |  |  | lr
 |  | LOAD A REG. & Ro REG. WITH 8 BIT DATA | 
 | ADDA&Ro |  |  | 
 |  |  | lr | 
STORE THE SUM |  |  |  | 
 |  |  | lr | 

## Slide 83
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
83
PROGRAM:
OUTPUT:
RESULT:
Thus the 8051 ALP for addition of two 8 bit numbers is executed.
ADDRESS | LABEL | MNEMONIC | OPERAND | HEX CODE | COMMENTS
4100 |  | CLR | C | C3 | Clear CY Flag
4101 |  | MOV | A, data1 | 74,data1 | Get the data1 in Accumulator
4103 |  | ADDC | A, # data 2 | 24,data2 | Add the data1 with data2
4105 |  | MOV | DPTR, #4500H | 90,45,00 | Initialize the memory Location
4108 |  | MOVX | @ DPTR, A | F0 | Store the result in memory location
4109 | L1 | SJMP | L1 | 80,FE | Stop the program
INPUT |  | OUTPUT | 
MEMORY DATA |  | MEMORY DATA | 

## Slide 84
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
84
EX. NO: 21 DATE :
8 BIT SUBTRACTION
AIM:
To perform subtraction of two 8 bit data and store the result in memory.
ALGORITHM:
Clear the carry flag.
Initialize the register for borrow.
Get the first operand into the accumulator.
Subtract the second operand from the accumulator.
If a borrow results increment the carry register.
Store the result in memory.

## Slide 85
DEPARTMENT OF ELEC1RONICS AND CO:MMUNICA TION ENGINEERING
CS6412-l.\flCROPROCESSOR AND l.\flCROCONTROLLER LABORATORY
85
FLOECHART:
START
CLEAR CARRY FLAG
I CREMENT THE BORROW
REG
NO
STOP
CET FIRST DATA |  |  | 
 | SUB 2' OPERAND I ACC |  | 
STORE TT-JE SUM | 

## Slide 86
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
86
8 BIT SUBTRACTION
OUTPUT:
RESULT:
Thus the 8051 ALP for subtraction of two 8 bit numbers is executed.
ADDRESS | LABEL | MNEMONIC | OPERAND | HEX | COMMENTS
4100 |  | CLR | C | CODE C3 | Clear CY flag
4101 |  | MOV | A, # data1 | 74, data1 | Store data1 in accumulator
4103 |  | SUBB | A, # data2 | 94,data2 | Subtract data2 from data1
4105 |  | MOV | DPTR, # 4500 | 90,45,00 | Initialize memory Location
4108 |  | MOVX | @ DPTR, A | F0 | Store the difference in memory location
4109 | L1 | SJMP | L1 | 80,FE | Stop
INPUT |  | OUTPUT | 
Memory Data |  | Memory Data | 

## Slide 87
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
87
EX. NO: 22 DATE :
8 BIT MULTIPLICATION
AIM:
To perform multiplication of two 8 bit data and store the result in memory.
ALGORITHM:
Get the multiplier in the accumulator.
Get the multiplicand in the B register.
Multiply A with B.
Store the product in memory.

## Slide 88
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
88
FLOWCHART:
STARJ
lr
GEl' THE MULTIPLIER IN ACCUMLATOl
,lr
GKl THE MULTLlPLICANT IN B REG.
,lr
MlJLTJPLY
A&B
lr
STORE THE SUM
lr
c
STOP
)

## Slide 89
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
89
8 BIT MULTIPLICATION:
ADDRESS | LABEL | MNEMONIC | OPERAND | HEX CODE | COMMENTS
4100 |  | MOV | A ,#data1 | 74, data1 | Store data1 in accumulator
4102 |  | MOV | B, #data2 | 75,data2 | Store data2 in B register.
4104 |  | MUL | A,B | F5,F0 | Multiply both
4106 |  | MOV | DPTR, # 4500H | 90,45,00 | Initialize memory location
4109 |  | MOVX | @ DPTR, A | F0 | Store lower order result
401A |  | INC | DPTR | A3 | Go to next memory location
410B |  | MOV | A,B | E5,F0 | Store higher order
410D |  | MOV | @ DPTR, A | F0 | result
410E | STOP | SJMP | STOP | 80,FE | Stop

## Slide 90
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
90
OUTPUT:
RESULT:
Thus the 8051 ALP for multiplication of two 8 bit numbers is executed.
INPUT |  | OUTPUT | 
Memory Location | Data | Memory location | Data
4500 |  | 4502 | 
4501 |  | 4503 | 

## Slide 91
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
91
EX. NO: 23 DATE :
8 BIT DIVISION
AIM:
To perform division of two 8 bit data and store the result in memory.
ALGORITHM:
Get the Dividend in the accumulator.
Get the Divisor in the B register.
Divide A by B.
Store the Quotient and Remainder in memory.

## Slide 92
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
92
FLOWCHART:
START
,,.
GET THE DIVIDENT IN ACCUMLATOR
,,.
GET THE DIVISOR IN B REG.
•lr
DIVIDE
AbyB
•ir
STORE THE SUM
,,.
STOP

## Slide 93
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
93
8 BIT DIVISION
ADDRESS | LABEL | MNEMONIC | OPERAND | HEX CODE | COMMENTS
4100 |  | MOV | A, # data1 | 74,data1 | Store data1 in accumulator
4102 |  | MOV | B, # data2 | 75,data2 | Store data2 in B register.
4104 |  | DIV | A,B | 84 | Divide
4015 |  | MOV | DPTR, # 4500H | 90,45,00 | Initialize memory location
4018 |  | MOVX | @ DPTR, A | F0 | Store remainder
4109 |  | INC | DPTR | A3 | Go to next memory location
410A |  | MOV | A,B | E5,F0 | Store quotient
410C |  | MOV | @ DPTR, A | F0 | Move stored data
410D | STOP | SJMP | STOP | 80,FE | Stop

## Slide 94
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
94
OUTPUT:
RESULT:
Thus the 8051 ALP for division of two 8 bit numbers is executed.
INPUT |  | OUTPUT | 
Memory Location | Data | Memory location | Data
4500 |  | 4502 | 
4501 |  | 4503 | 

## Slide 95
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
95
EX. NO: 24 DATE :
SQUARE AND CUBE PROGRAM, FIND 2’S COMPLEMENT OF A
NUMBER
AIM:
To convert Square and Cube program, Find 2’s complement of a number
using 8051 micro controller
RESOURCES REQUIERED:
8051 microcontroller kit
Keyboard
Power supply

## Slide 96
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
96
PROGRAM:
SQUARE PGM USING 8051
ORG 00h
LJMP MAIN
DELAYS:
04; MOV R0,#2
MOV TMOD, #01H
MOV TH0, #HIGH (-50000)
7 MOV TL0, #LOW (-50000)
SETB TR0
JNB TF0,
10CLR TF0
12; DJNZ R0,DELAY
13RET
14MAIN:
15MOV DPTR,#300H
16MOV A,#0FFH
17MOV P1,A
18BACK:
19LCALL DELAY
20MOV A,P1
21MOVC A,@A+DPTR

## Slide 97
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
97
22;MOV P2,#00H
23;LCALL DELAY
24MOV P2,A
25SJMP BACK
26ORG 300H
27XSQR_TABLE:
28DB 0,1,4,9,16,25,36,49,64,81
29END
OUTPUT
RESULT;
Thus the Square and Cube program, Find 2’s complement of a number is
done in 8051 microcontroller
INPUT DATA | OUTPUT DATA

## Slide 98
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
98
EX. NO: 25 DATE :
UNPACKED BCD TO ASCII
AIM:
To convert BCD number into ASCII by using 8051 micro controller.
RESOURCES REQUIERED:
8051 microcontroller kit
Keyboard
Power supply

## Slide 99
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
99
FLOWCHART:
START)
•
SAYE REGISTER
+
GKI' HEX NUMBER
..
CONVERT INTO THE (BCD) DECIMAL EQUYALANT
+
UNPACK THE BCD DIGITS
ADD 3UH IN EA•CH. BCDDIGITS
c
STOP
TO GET ITS ASCII DIGITS | 
DISPLAY EACH DIGITS | 
RESTORE REGISTOR | 

## Slide 100
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
100
ALGORITHM:
00
59
AAM
08
09
AH
AL
AH AL
NOTE; 59H
TO 89 DECIMAL
08
09
ADD AX,
3030H
38
39
AH AL
AH AL
NOTE; 38h and 39h are the ASCII equivalents of 8 and 9 respectively
Save contents of all registers which are used in the routine
Get the data in al register and make AH equal to 00.
Use AAM instruction to convert number in its decimal equivalent in the unpacked format.
Add 30h in each digit to get its ASCII equivalent.
Display one by one using function 2 of INT 21h.
Routine content of register.

## Slide 101
CS6412- MICROPROCESSOR AND MICROCONTROLLER LABORATORY
101
PROGRAM;
ROUTINE: convert binary for number less than 100 passing parameter
; Hex number in al register.
; Routine to convert binary number into its
; Decimal and then ASCII equivalent, and display the number
BTA PROC NEAR
PUSH DX PUSH BX PUSH AX
MOV AX, 00H AAM
ADD AX, 3030H
MOV BX, AX
MOV DL, MOV AH, 02 INT 21H
MOV DL, BL INT 21H
BH
POP AX POP BX POP DX RET END P
RESULT:
The given number is converted into ASCII using 8051 microcontroller kit.