## Slide 1
System programing
Assistant lecturer: Abdullah Thaier Abdalsatir
Diyala university
College of engineering
Department of computer engineering
Second stage
Lec3-Addressing-Modes

## Slide 2
Chapter 3: Addressing Modes

## Slide 3: Introduction
Efficient software development for the microprocessor requires a complete familiarity with the addressing modes employed by each instruction.
This chapter explains the operation of the stack memory so that the PUSH and POP instructions and other stack operations will be understood.

## Slide 4: Chapter Objectives
Upon completion of this chapter, you will be able to:
Explain the operation of each data-addressing
mode.
Use the data-addressing modes to form
assembly language statements.
Explain the operation of each program memory-addressing mode.
Use the program memory-addressing modes to form assembly and machine language statements.

## Slide 5: Chapter Objectives
memory and used with software.
The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486 Pentium, Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Copyright ©2009 by Pearson Education, Inc.
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
Upon completion of this chapter, you will be able to:
Select the appropriate addressing mode to
accomplish a given task.
Detail the difference between addressing memory data using real mode and pro-tected mode operation.
Describe sequence of events that place data
onto the stack or remove data from the stack.
Explain how a data structure is placed in
(cont.)

## Slide 6
3–1 DATA ADDRESSING MODES
microprocessor which operation to perform
The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486 Pentium, Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Copyright ©2009 by Pearson Education, Inc.
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
MOV instruction is a common and flexible
instruction.
  provides a basis for explanation of data- addressing modes
Figure 3–1 illustrates the MOV instruction and
defines the direction of data flow.
Source is to the right and destination the left, next to the opcode MOV.
  an opcode, or operation code, tells the

## Slide 7
Figure 3-1 The MOV instruction showing the source, destination, and direction of data flow.
MOV AX,BX
Source
•
•
es
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 8
The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486 Pentium,
Figure 3–2 shows all possible variations of the
data-addressing modes using MOV.
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
These data-addressing modes are found with
all versions of the Intel microprocessor.
  except for the scaled-index-addressing mode, found only in 80386 through Core2
RIP relative addressing mode is not illustrated.
  only available on the Pentium 4 and Core2 in the 64-bit mode

## Slide 9
Figure 3-2 8086-Core2 data-addressing modes.
Type
ln.tructlon
SoUf'CI
Addt•u Genet-atlon
OeatlnatJon
Aeg,sl
MOV AX ,BX
"8J( '
AX
I
MOV CH,31\H
CH
t.A(W (1Z34H).AX
Allge!OI
All(
, OS ., 10H • OISP
1000011.- 12:34
M41mCHY
1123AH
Rogi let indlt«
OOV (BX],OL
AcQostcf
CL
•
OS "' 1C1-i •W<
1OOOOH •0300H
ldareLS
I o.'lO()o4
&..e1Jiu:p'indux
MOV [BX.si],BP
stor
tiP
OS IOH .-BX+SI
..,.
...
IOOOOH + IXJOOH + 0200H
1a.o.onH
i lor ro1a1rvo
MOV CL.{BX...t]
MP'I'IOf)'
llddr-
IOOOlH
OS " 1OH + BX + 4
1OOOOH CX)()(H •4
AOQISIDI
CL
Due re u •ndelt
MOV AMAYfWC.S IOX
ReosNr
OS l< 101 +ARRAY • BX • Sl
I OOOOH • IO()OH •0300H •0200H
()ty
ox
I·OCY·US
Scale<! Index
MOV [EBX+2 ,.ESI).AX
Roo*<
AX
.. OS )t 10ti + EBX+2 l< ESI
"'-lly
llllettoss
lcrnx.l
1OOOOH • OOOOOOOOH -+ 00000400H
No'.G$- 1::8X •()OO()(X)O()
ESI•00000200H. Ali RAY' • 1OOOti anO OS • I()()Oti
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 10: Register Addressing
The most common form of data addressing.
– once register names learned, easiest to apply.
The microprocessor contains these 8-bit register names used with register addressing: AH, AL, BH, BL, CH, CL, DH, and DL.
16-bit register names: AX, BX, CX, DX, SP, BP, SI, and DI.

## Slide 11
In 80386 & above, extended 32-bit register names are: EAX, EBX, ECX, EDX, ESP, EBP, EDI, and ESI.
64-bit mode register names are: RAX, RBX,
RCX, RDX, RSP, RBP, RDI, RSI, and R8
through R15.
Important for instructions to use registers that are the same size.
  never mix an 8-bit \with a 16-bit register, an 8- or
a 16-bit register with a 32-bit register
  this is not allowed by the microprocessor and results in an error when assembled

## Slide 12
Figure 3–3 The effect of executing the MOV BX, CX instruction at the point just before the BX register changes. Note that only the rightmost 16 bits of register EBX change.

## Slide 13
Figure 3–3 shows the operation of the MOV
BX, CX instruction.
The source register’s contents do not change.
– the destination register’s contents do change
The contents of the destination register or destination memory location change for all instructions except the CMP and TEST instructions.
The MOV BX, CX instruction does not affect
the leftmost 16 bits of register EBX.

## Slide 14: Immediate Addressing
Term immediate implies that data immediately follow the hexadecimal opcode in the memory.
  immediate data are constant data
  data transferred from a register or memory location are variable data
Immediate addressing operates upon a byte or word of data.
Figure 3–4 shows the operation of a MOV
EAX,13456H instruction.

## Slide 15: Figure 3–4 The operation of the MOV EAX,3456H instruction. This instruction copies the immediate data (13456H) into EAX.
As with the MOV instruction illustrated in Figure 3–3, the source data overwrites the destination data.

## Slide 16
In symbolic assembly language, the symbol # precedes immediate data in some assemblers.
– MOV AX,#3456H instruction is an example
Most assemblers do not use the # symbol, but represent immediate data as in the MOV AX,3456H instruction.
  an older assembler used with some Hewlett- Packard logic development does, as may others
  in this text, the # is not used for immediate data

## Slide 17
The symbolic assembler portrays immediate
data in many ways.
The letter H appends hexadecimal data.
If hexadecimal data begin with a letter, the
assembler requires the data start with a 0.
  to represent a hexadecimal F2, 0F2H is used in assembly language
Decimal data are represented as is and
require no special codes or adjustments.
  an example is the 100 decimal in the MOV AL,100 instruction

## Slide 18
An ASCII-coded character or characters may be depicted in the immediate form if the ASCII data are enclosed in apostrophes.
– be careful to use the apostrophe (‘) for ASCII
data and not the single quotation mark (‘)
Binary data are represented if the binary
number is followed by the letter B.
– in some assemblers, the letter Y

## Slide 19
Each statement in an assembly language
program consists of four parts or fields.
The leftmost field is called the label.
  used to store a symbolic name for the memory
location it represents
All labels must begin with a letter or one of the following special characters: @, $, -, or ?.
  a label may any length from 1 to 35 characters
The label appears in a program to identify the name of a memory location for storing data and for other purposes.

## Slide 20
The next field to the right is the opcode field.
designed to hold the instruction, or opcode
the MOV part of the move data instruction is an
example of an opcode
Right of the opcode field is the operand field.
  contains information used by the opcode
  the MOV AL,BL instruction has the opcode MOV and operands AL and BL
The comment field, the final field, contains a
comment about the instruction(s).
  comments always begin with a semicolon (;)

## Slide 21: Direct Data Addressing
Applied to many instructions in a typical program.
Two basic forms of direct data addressing:
  direct addressing, which applies to a MOV between a memory location and AL, AX, or EAX
  displacement addressing, which applies to almost any instruction in the instruction set
Address is formed by adding the displacement to the default data segment address or an alternate segment address.

## Slide 22: Direct Addressing
Direct addressing with a MOV instruction transfers data between a memory location, located within the data segment, and the AL (8-bit), AX (16-bit), or EAX (32-bit) register.
  usually a 3-byte long instruction
MOV AL,DATA loads AL from the data segment memory location DATA (1234H).
  DATA is a symbolic memory location, while
1234H is the actual hexadecimal location

## Slide 23
Figure 3–5 The operation of the MOV AL,[1234H] instruction when DS=1000H .
This instruction transfers a copy contents of memory location 11234H into AL.
– the effective address is formed by adding 1234H (the offset address) and 10000H (the data segment address of 1000H times 10H) in a system operating in the real mode

## Slide 24: Displacement Addressing
Almost identical to direct addressing, except the instruction is 4 bytes wide instead of 3.
In 80386 through Pentium 4, this instruction can be up to 7 bytes wide if a 32-bit register and a 32-bit displacement are specified.
This type of direct data addressing is much more flexible because most instructions use it.

## Slide 25: Register Indirect Addressing
Allows data to be addressed at any memory location through an offset address held in any of the following registers: BP, BX, DI, and SI.
In addition, 80386 and above allow register indirect addressing with any extended register except ESP.
In the 64-bit mode, the segment registers serve no purpose in addressing a location in the flat model.

## Slide 26
Figure 3–6 The operation of the MOV AX,[BX] instruction when BX = 1000H and DS
= 0100H. Note that this instruction is shown after the contents of memory are
transferred to AX.

## Slide 27
The data segment is used by default with register indirect addressing or any other mode that uses BX, DI, or SI to address memory.
If the BP register addresses memory, the
stack segment is used by default.
– these settings are considered the default for
these four index and base registers
For the 80386 and above, EBP addresses
memory in the stack segment by default.
EAX, EBX, ECX, EDX, EDI, and ESI address memory in the data segment by fault.

## Slide 28
When using a 32-bit register to address memory in the real mode, contents of the register must never exceed 0000FFFFH.
In the protected mode, any value can be used in a 32-bit register that is used to indirectly address memory.
– as long as it does not access a location outside
the segment, dictated by the access rights byte
In the 64-bit mode, segment registers are not used in address calculation; the register contains the actual linear memory address.

## Slide 29
In some cases, indirect addressing requires specifying the size of the data by the special assembler directive BYTE PTR, WORD PTR, DWORD PTR, or QWORD PTR.
– these directives indicate the size of the memory data addressed by the memory pointer (PTR)
The directives are with instructions that
address a memory location through a
pointer or index register with immediate data.
With SIMD instructions, the octal OWORD PTR, represents a 128-bit-wide number.

## Slide 30
Indirect addressing often allows a program to
refer to tabular data located in memory.
Figure 3–7 shows the table and the BX register used to sequentially address each location in the table.
To accomplish this task, load the starting location of the table into the BX register with a MOV immediate instruction.
After initializing the starting address of the table, use register indirect addressing to store the 50 samples sequentially.

## Slide 31
Figure 3-7 An array (TABLE) containing 50 bytes that are indirectly addressed through register BX.
Memory
EBX
.....-
-
-
0 0 0 0
TABLE
.
---
Table+ 49
Table+ 2
Table+ 1
Table
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 32: Base-Plus-Index Addressing
Similar to indirect addressing because it indirectly addresses memory data.
The base register often holds the beginning location of a memory array.
  the index register holds the relative position
of an element in the array
  whenever BP addresses memory data, both the stack segment register and BP generate the effective address

## Slide 33: Locating Data with Base-Plus-Index Addressing
Figure 3–8 shows how data are addressed by the MOV DX,[BX + DI] instruction when the microprocessor operates in the real mode.
The Intel assembler requires this addressing
mode appear as [BX][DI] instead of [BX + DI].
The MOV DX,[BX + DI] instruction is MOV DX,[BX][DI] for a program written for the Intel ASM assembler.

## Slide 34
Figure 3–8 An example showing how the base-plus-index addressing mode functions for the MOV DX,[BX + DI] instruction. Notice that memory address 02010H is accessed because DS=0100H, BX=100H and DI=0010H.

## Slide 35: Locating Array Data Using Base- Plus-Index Addressing
A major use is to address elements in a
memory array.
To accomplish this, load the BX register (base) with the beginning address of the array and the DI register (index) with the element number to be accessed.
Figure 3–9 shows the use of BX and DI to access an element in an array of data.

## Slide 36
Figure 3-9 An example of the base-plus-index addressing mode. Here an element (DI) of an ARRAY (BX) is addressed.
Memory
-
-
01
Element
BX
ARRAY
---
ARRAY +5
ARRAY +4
ARRAY +3
ARRAY + 2
ARRAY + 1 ARRAY
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 37: Register Relative Addressing
The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486 Pentium,
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Similar to base-plus-index addressing and displacement addressing.
– data in a segment of memory are addressed by adding the displacement to the contents of a base or an index register (BP, BX, DI, or SI)
Figure 3–10 shows the operation of the MOV AX,[BX+1000H] instruction.
A real mode segment is 64K bytes long.

## Slide 38
Figure 3-10 The operation of the MOV AX, [BX=1000H] instructon, when BX=1000H and DS=0200H .
Memory
.---
EAX
EBX
Register array
76 /1.
2222
AO
A 0
03101H
03100H ..._
"-
A076
0000
--- -
0 1
00
-
-
7 6
0100H
,.
1000H
+
,1100H
--..,....,
OS X 10H
.. +
2000H
3100H
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 39: Addressing Array Data with Register Relative
The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486 Pentium,
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
It is possible to address array data with
register relative addressing.
  such as with base-plus-index addressing
In Figure 3–11, register relative addressing is illustrated with the same example as for base- plus-index addressing.
  this shows how the displacement ARRAY adds to index register DI to generate a reference to an array element

## Slide 40
Figure 3-11 Register relative addressing used to address an element of ARRAY. The displacement addresses the start of ARRAY, and Dl accesses an element.
Memory
-
-
Element
Displacement
ARRAY
---
ARRAY + 6
ARRAY +5
ARRAY +4
ARRAY +3
ARRAY + 2
ARRAY + 1 ARRAY
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 41: Base Relative-Plus-Index Addressing
Similar to base-plus-index addressing.
  adds a displacement
  uses a base register and an index register to
form the memory address
This type of addressing mode often addresses a two-dimensional array of memory data.

## Slide 42: Addressing Data with Base Relative-Plus-Index
Least-used addressing mode.
Figure 3–12 shows how data are referenced if the instruction executed by the microprocessor is MOV AX,[BX + SI + 100H].
– displacement of 100H adds to BX and SI to form the offset address within the data segment
This addressing mode is too complex for
frequent use in programming.

## Slide 43
Figure 3-12 An example of base relative-plus-index addressing using a MOV AX,[BX+SI=1 OOOH] instruction. Note: DS=1OOOH
EAX EBX ECX EDX
ESP EBP ESI
Memory
-
Register array
vt
A 3
10131H
10130H
A316
1 6
....
0020H
0030H
:. +
0130H
--
0 0 1 0
+
+
-
0010H
10130H
-------
10000H
0100H
OS X 10H
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.
 | A 3 | 1 6 | N
 | 0 0 | 2 0 | 

## Slide 44: Addressing Arrays with Base Relative-Plus-Index
The Intel Microprocessors: 8086/8088, 80186/80188, 80286, 80386, 80486 Pentium,
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Suppose a file of many records exists in
memory, each record with many elements.
– displacement addresses the file, base register addresses a record, the index register addresses an element of a record
Figure 3–13 illustrates this very complex form
of addressing.

## Slide 45
Figure 3-13 Base relative-plus-index addressing used to access a FILE that contains multiple records (REC).
Memory
..
I
I
I
I
EDI
Element
EBX I
I
RECC
I
REC A
Displacement
I
FILE
I I
REC C
REC B
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 46: Scaled-Index Addressing
Unique to 80386 - Core2 microprocessors.
  uses two 32-bit registers (a base register and
an index register) to access the memory
The second register (index) is multiplied by a
scaling factor.
  the scaling factor can be 1x, 2x, 4x, 8x
A scaling factor of is implied and need not be included in the assembly language instruction (MOV AL,[EBX + ECX]).

## Slide 47: RIP Relative Addressing
Uses the 64-bit instruction pointer register in the 64-bit mode to address a linear location in the flat memory model.
Inline assembler program available to Visual does not contain any way of using this mode or any other 64-bit addressing mode.
The Microsoft Visual does not at present
support developing 64-bit assembly code.

## Slide 48: Data Structures
Used to specify how information is stored in a memory array.
– a template for data
The start of a structure is identified with the STRUC assembly language directive and the end with the ENDS statement.

## Slide 49
3–2 PROGRAM MEMORY-
ADDRESSING MODES
Used with the JMP (jump) and CALL
instructions.
Consist of three distinct forms:
– direct, relative, and indirect

## Slide 50: Direct Program Memory Addressing
Used for all jumps and calls by early microprocessor; also used in high-level languages, such as BASIC.
– GOTO and GOSUB instructions
The microprocessor uses this form, but not as often as relative and indirect program memory addressing.
The instructions for direct program memory
addressing store the address with the opcode.

## Slide 51
Figure 3-14 The 5-byte machine language version of a JMP [1OOOOH] instruction.
Opcode
Offset (low)
Offset (high)
o o I o o .l
Segment (low)
I1 ....- o o .l I 1 o I
Segment (high)
......_I
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.

## Slide 52
This JMP instruction loads CS with 1000H and IP with 0000H to jump to memory location 10000H for the next instruction.
  an intersegment jump is a jump to any memory
location within the entire memory system
Often called a far jump because it can jump to
any memory location for the next instruction.
  in real mode, any location within the first 1M byte
  In protected mode operation, the far jump can jump to any location in the 4G-byte address range in the 80386 - Core2 microprocessors

## Slide 53
The only other instruction using direct program addressing is the intersegment or far CALL instruction.
Usually, the name of a memory address, called a label, refers to the location that is called or jumped to instead of the actual numeric address.
When using a label with the CALL or JMP instruction, most assemblers select the best form of program addressing.

## Slide 54: Relative Program Memory Addressing
Not available in all early microprocessors, but
it is available to this family of microprocessors.
The term relative means “relative to the
instruction pointer (IP)”.
The JMP instruction is a 1-byte instruction, with a 1-byte or a 2-byte displacement that adds to the instruction pointer.
An example is shown in Figure 3–15.

## Slide 55
Figure 3-15 A JMP [2] instruction. This instruction skips over the 2 bytes of memory that follow the JMP instruction.
10000 EB
10001 02
10002
10003
10004
JMP [2]
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 • All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 56: Indirect Program Memory Addressing
The microprocessor allows several forms of program indirect memory addressing for the JMP and CALL instructions.
In 80386 and above, an extended register can be used to hold the address or indirect address of a relative JMP or CALL.
– for example, the JMP EAX jumps to the
location address by register EAX

## Slide 57
If a relative register holds the address, the
jump is considered to be an indirect jump.
For example, JMP [BX] refers to the memory location within the data segment at the offset address contained in BX.
  at this offset address is a 16-bit number used as
the offset address in the intrasegment jump
  this type of jump is sometimes called an indirect- indirect or double-indirect jump
Figure 3–16 shows a jump table that is stored, beginning at memory location TABLE.

## Slide 58
Figure 3–16 A jump table that stores addresses of various programs. The exact address chosen from the TABLE is determined by an index stored with the jump instruction.

## Slide 59: 3–3 STACK MEMORY-ADDRESSING MODES
The stack plays an important role in all
microprocessors.
  holds data temporarily and stores return
addresses used by procedures
Stack memory is LIFO (last-in, first-out) memory
  describes the way data are stored and removed
from the stack

## Slide 60
Data are placed on the stack with a PUSH
instruction; removed with a POP instruction.
Stack memory is maintained by two registers:
  the stack pointer (SP or ESP)
  the stack segment register (SS)
Whenever a word of data is pushed onto the stack, the high-order 8 bits are placed in the location addressed by SP – 1.
  low-order 8 bits are placed in the location
addressed by SP – 2

## Slide 61
The SP is decremented by 2 so the next word
is stored in the next available stack location.
– the SP/ESP register always points to an area of
memory located within the stack segment.
In protected mode operation, the SS register holds a selector that accesses a descriptor for the base address of the stack segment.
When data are popped from the stack, the low- order 8 bits are removed from the location addressed by SP.
– high-order 8 bits are removed; the SP register is incremented by 2

## Slide 62
Figure 3–17 The PUSH and POP instructions: (a) PUSH BX places the contents of BX onto the stack; (b) POP CX removes data from the stack and places them into CX. Both instructions are shown after execution.

## Slide 63
Note that PUSH and POP store or retrieve
words of data—never bytes—in 8086 - 80286.
80386 and above allow words or doublewords
to be transferred to and from the stack.
Data may be pushed onto the stack from any 16-bit register or segment register.
– in 80386 and above, from any 32-bit extended register
Data may be popped off the stack into any
register or any segment register except CS.

## Slide 64
PUSHA and POPA instructions push or pop all
except segment registers, on the stack.
Not available on early 8086/8088 processors.
80386 and above allow extended registers to
be pushed or popped.
– 64-bit mode for Pentium and Core2 does not contain a PUSHA or POPA instruction

## Slide 65: SUMMARY
The MOV instruction copies the contents of the source operand into the destination operand.
The source never changes for any
instruction.
Register addressing specifies any 8-bit register (AH, AL, BH, BL, CH, CL, DH, or DL) or any 16-bit register (AX, BX, CX, DX, SP, BP, SI, or DI).

## Slide 66: SUMMARY
The segment registers (CS, DS, ES, or SS) are also addressable for moving data between a segment register and a 16-bit register/memory location or for PUSH and POP.
In the 80386 through the Core2 microprocessors, the extended registers also are used for register addressing; they consist of EAX, EBX, ECX, EDX, ESP, EBP, EDI, and ESI.
(cont.)

## Slide 67: SUMMARY
In the 64-bit mode, the registers are RAX, RBX, RCX, RDX, RSP, RBP, RDI, RSI, and
R8 through R15.
The MOV immediate instruction transfers the byte or word that immediately follows the opcode into a register or a memory location.
Immediate addressing manipulates
constant data in a program.
(cont.)

## Slide 68: SUMMARY
In the 80386 and above, doubleword immediate data may also be loaded into a 32-bit register or memory location.
The .MODEL statement is used with assembly language to identify the start of a file and the type of memory model used with the file.
If the size is TINY, the program exists in the code segment, and assembled as a command (.COM) program.
(cont.)

## Slide 69: SUMMARY
If the SMALL model is used, the program uses a code and data segment and assembles as an execute (.EXE) program.
Direct addressing occurs in two forms in the microprocessor: direct addressing and displacement addressing.
(cont.)

## Slide 70: SUMMARY
Both forms of addressing are identical except that direct addressing is used to transfer data between EAX, AX, or AL and memory; displacement addressing is used with any register-memory transfer.
Direct addressing requires 3 bytes of memory, whereas displacement addressing requires 4 bytes.
(cont.)

## Slide 71: SUMMARY
Register indirect addressing allows data to be addressed at the memory loca-tion pointed to by either a base (BP and BX) or index register (DI and SI).
In the 80386 and above, extended registers
EAX, EBX, ECX, EDX, EBP, EDI, and ESI
are used to address memory data.
(cont.)

## Slide 72: SUMMARY
Base-plus-index addressing often addresses data in an array.
The memory address for this mode is formed by adding a base register, index register, and the contents of a segment register times 10H.
In the 80386 and above, the base and index registers may be any 32-bit register except EIP and ESP.
(cont.)

## Slide 73: SUMMARY
Register relative addressing uses a base or index register, plus a displacement to access memory data.
Base relative-plus-index addressing is useful for addressing a two-dimensional memory array.
The address is formed by adding a base register, an index register, displacement, and the contents of a segment register times 10H.
(cont.)

## Slide 74: SUMMARY
Scaled-index addressing is unique to the 80386 through the Core2.
The second of two registers (index) is scaled by a factor of to access words, doublewords, or quadwords in memory arrays.
The MOV AX,[ EBX + 2*ECX] and the MOV [4 * ECX ],EDX are examples of scaled- index instructions.
(cont.)

## Slide 75: SUMMARY
Data structures are templates for storing arrays of data and are addressed by array name and field.
Direct program memory addressing is allowed with the JMP and CALL instructions to any location in the memory system.
With this addressing mode, the off-set address and segment address are stored with the instruction.
(cont.)

## Slide 76: SUMMARY
Relative program addressing allows a JMP or CALL instruction to branch for-ward or backward in the current code segment by bytes.
In the 80386 and above, the 32-bit displacement allows a branch to any location in the cur-rent code segment by using a displacement value of bytes.
The 32-bit displacement can be used only in protected mode.
(cont.)

## Slide 77: SUMMARY
Indirect program addressing allows the JMP or CALL instructions to address another portion of the program or subroutine indirectly through a register or memory location.
The PUSH and POP instructions transfer a word between the stack and a register or memory location.
A PUSH immediate instruction is available to place immediate data on the stack.
(cont.)

## Slide 78: SUMMARY
The PUSHA and POPA instructions transfer AX, CX, DX, BX, BP, SP, SI, and DI
between the stack and these registers.
In 80386 and above, the extended register and extended flags can also be transferred between registers and the stack.
A PUSHFD stores the EFLAGS, whereas a PUSHF stores the FLAGS. POPA and PUSHA are not available in 64-bit mode.