## Slide 1
System programing
Assistant lecturer: Abdullah Thaier Abdalsatir
Diyala university
College of engineering
Department of computer engineering
Second stage
Lec6-Program-Control-Instructions

## Slide 2
Chapter 6: Program Control Instructions

## Slide 3: Introduction
This chapter explains the program control instructions, including the jumps, calls, returns, interrupts, and machine control instructions.
This chapter also presents the relational assembly language statements (.IF, .ELSE,
.ELSEIF, .ENDIF, .WHILE, .ENDW, .REPEAT,
and .UNTIL) that are available in version 6.xx and above of MASM or TASM, with version
5.xx set for MASM compatibility.

## Slide 4: Chapter Objectives
Upon completion of this chapter, you will be able to:
Use both conditional and unconditional jump
instructions to control the flow of a program.
Use the relational assembly language statements .IF, .REPEAT, .WHILE, and so forth in programs.
Use the call and return instructions to include
procedures in the program structure.

## Slide 5: Chapter Objectives
Upon completion of this chapter, you will be able to:
Explain the operation of the interrupts and
interrupt control instructions.
Use machine control instructions to modify the flag bits.
Use ENTER and LEAVE to enter and leave
programming structures.
(cont.)

## Slide 6
6–1 THE JUMP GROUP
Allows programmer to skip program sections and branch to any part of memory for the next instruction.
A conditional jump instruction allows decisions based upon numerical tests.
– results are held in the flag bits, then tested by
conditional jump instructions
LOOP and conditional LOOP are also forms of the jump instruction.

## Slide 7: Unconditional Jump (JMP)
Three types: short jump, near jump, far jump.
Short jump is a 2-byte instruction that allows
jumps or branches to memory locations within
+127 and –128 bytes.
– from the address following the jump
3-byte near jump allows a branch or jump within ±32K bytes from the instruction in the current code segment.

## Slide 8
5-byte far jump allows a jump to any memory
location within the real memory system.
The short and near jumps are often called
intrasegment jumps.
Far jumps are called intersegment jumps.

## Slide 9
Figure 6-1 The three main forms of the JMP instruction. Note that Disp is either an 8- or 16-bit signed displacement or distance.
Opeode
(a)
E B
Disp
Short
Opcode
(b)
E 9
Disp Low
Disp
High
Near
Opcode
(c)
E A
I P
Low
IP
High
cs
Low
I
cs
High
Far
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 ·All rights reserved.
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.

## Slide 10: Short Jump
Called relative jumps because they can be moved, with related software, to any location in the current code segment without a change.
  jump address is not stored with the opcode
  a distance, or displacement, follows the opcode
The short jump displacement is a distance represented by a 1-byte signed number whose value ranges between +127 and –128.
Short jump instruction appears in Figure 6–2.

## Slide 11: Figure 6–2 A short jump to four memory locations beyond the address of the next
instruction.
– when the microprocessor executes a short jump, the displacement is sign-extended and added to the instruction pointer (IP/EIP) to generate the jump address
within the current code segment
– The instruction branches to this new address for the next instruction in the program

## Slide 12
When a jump references an address, a label
normally identifies the address.
The JMP NEXT instruction is an example.
  it jumps to label NEXT for the next instruction
  very rare to use an actual hexadecimal address
with any jump instruction
The label NEXT must be followed by a colon
(NEXT:) to allow an instruction to reference it
  if a colon does not follow, you cannot jump to it
The only time a colon is used is when the label is used with a jump or call instruction.

## Slide 13: Near Jump
A near jump passes control to an instruction in
the current code segment located within
±32K bytes from the near jump instruction.
  distance is ±2G in 80386 and above when
operated in protected mode
Near jump is a 3-byte instruction with opcode
followed by a signed 16-bit displacement.
  80386 - Pentium 4 displacement is 32 bits and the near jump is 5 bytes long

## Slide 14
Signed displacement adds to the instruction
pointer (IP) to generate the jump address.
– because signed displacement is ±32K, a near jump can jump to any memory location within the current real mode code segment
The protected mode code segment in the
80386 and above can be 4G bytes long.
– 32-bit displacement allows a near jump to any
location within ±2G bytes
Figure 6–3 illustrates the operation of the real
mode near jump instruction.

## Slide 15
Figure 6-3 A near jump that adds the displacement (0002H) to the contents of IP.
1000A
10009
10008
10007
10006
10005
10004
10003
10002
10001
10000
Memory
-
....,
CS = 1000H
IP = 0002H
New IP = 0005H
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
- Architecture, Programming, and Interfacing, Eighth Edition
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Upper Saddle River, New Jersey 07458 ·All rights reserved.
Barry B. Brey
PEARSON
Copyright ©2009 by Pearson Education, Inc.
r---"" |  | 
(Jump to here) |  | 
00 |  | 
02 |  | 
JMP |  | 

## Slide 16
The near jump is also relocatable because it
is also a relative jump.
This feature, along with the relocatable data segments, Intel microprocessors ideal for use in a general-purpose computer system.
Software can be written and loaded anywhere in the memory and function without modification because of the relative jumps and relocatable data segments.

## Slide 17: Far Jump
Obtains a new segment and offset address
to accomplish the jump:
  bytes 2 and 3 of this 5-byte instruction contain the new offset address
  bytes 4 and 5 contain the new segment address
  in protected mode, the segment address accesses a descriptor with the base address of the far jump segment
  offset address, either 16 or 32 bits, contains the
offset address within the new code segment

## Slide 18
Figure 6-4 A far jump instruction replaces the contents of both CS and IP with 4 bytes following the opcode.
Memory
A3129 A3128 A3127 A3126
10004
10003
10002
10001
10000
Far jump
PEARSON
- Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Architecture, Programming, and Interfacing, Eighth Edition Barry B. Brey
Upper Saddle River, New Jersey 07458 ·All rights reserved.
......,
..,.
A3
00
01
27
JMP
--
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
Copyright ©2009 by Pearson Education, Inc.
(Jump to here) | 

## Slide 19
The far jump instruction sometimes appears
with the FAR PTR directive.
another way to obtain a far jump is to define a label as a far label
a label is far only if it is external to the current
code segment or procedure
The JMP UP instruction references a far label.
– label UP is defined as a far label by the EXTRN UP:FAR directive
External labels appear in programs that
contain more than one program file.

## Slide 20: use a double colon (LABEL::)
Another way of defining a label as global is to
– required inside procedure blocks defined as near if the label is accessed from outside the procedure block
When the program files are joined, the linker inserts the address for the UP label into the JMP UP instruction.
Also inserts segment address in JMP START instruction.

## Slide 21: Jumps with Register Operands
Jump can also use a 16- or 32-bit register as
an operand.
  automatically sets up as an indirect jump
  address of the jump is in the register specified
by the jump instruction
Unlike displacement associated with the near jump, register contents are transferred directly into the instruction pointer.
An indirect jump does not add to the
instruction pointer.

## Slide 22
JMP AX, for example, copies the contents of
the AX register into the IP.
– allows a jump to any location within the current code segment
In 80386 and above, JMP EAX also jumps to
any location within the current code segment;
– in protected mode the code segment can be 4G bytes long, so a 32-bit offset address is needed

## Slide 23: Indirect Jumps Using an Index
Jump instruction may also use the [ ] form of
addressing to directly access the jump table.
The jump table can contain offset addresses for near indirect jumps, or segment and offset addresses for far indirect jumps.
– also known as a double-indirect jump if the
register jump is called an indirect jump
The assembler assumes that the jump is near unless the FAR PTR directive indicates a far jump instruction.

## Slide 24
Mechanism used to access the jump table is
identical with a normal memory reference.
– JMP TABLE [SI] instruction points to a jump address stored at the code segment offset location addressed by SI
Both the register and indirect indexed jump
instructions usually address a 16-bit offset.
  both types of jumps are near jumps
If JMP FAR PTR [SI] or JMP TABLE [SI], with
TABLE data defined with the DD directive:
  microprocessor assumes the jump table contains
doubleword, 32-bit addresses (IP and CS)

## Slide 25: Conditional Jumps and Conditional Sets
Always short jumps in 8086 - 80286.
  limits range to within +127 and –128 bytes from
the location following the conditional jump
In 80386 and above, conditional jumps are either short or near jumps (±32K).
  in 64-bit mode of the Pentium 4, the near jump distance is ±2G for the conditional jumps
Allows a conditional jump to any location
within the current code segment.

## Slide 26
Conditional jump instructions test flag bits:
sign (S), zero (Z), carry (C)
parity (P), overflow (0)
If the condition under test is true, a branch to the label associated with the jump instruction occurs.
  if false, next sequential step in program executes
  for example, a JC will jump if the carry bit is set
Most conditional jump instructions are straightforward as they often test one flag bit.
  although some test more than one

## Slide 27
Because both signed and unsigned numbers
are used in programming.
Because the order of these numbers is different, there are two sets of conditional jump instructions for magnitude comparisons.
16- and 32-bit numbers follow the same order
as 8-bit numbers, except that they are larger.
Figure 6–5 shows the order of both signed
and unsigned 8-bit numbers.

## Slide 28
Figure 6-5 Signed and unsigned numbers follow different orders.
255
254
132
131
130
129
128 -SOH
Unsigned numbers
----
-
-
-
............
+127
+126
Signed numbers
+2 -
+1
+0
-1
-2
-
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
- Architecture, Programming, and Interfacing, Eighth Edition
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Upper Saddle River, New Jersey 07458 ·All rights reserved.
Barry B. Brey
PEARSON
Copyright ©2009 by Pearson Education, Inc.
4 | -124
3 | -125
2 | -126
1 | -127
0 | -128
FFH |  | 
FEH |  | 
- 84H | 
83H | 
82H | 
81H | 
04H | 
03H | 
02H | 
01H | 
OOH | 
7FH |  | 
7EH |  | 
._ |  | 
 | 02H | 
01H |  | 
OOH |  | 
FFH |  | 
FEH |  | 
............
84H
83H
82H
81H
SOH

## Slide 29
When signed numbers are compared, use the
JG, JL, JGE, JLE, JE, and JNE instructions.
– terms greater than and less than refer to signed numbers
When unsigned numbers are compared, use
the JA, JB, JAB, JBE, JE, and JNE
instructions.
– terms above and below refer to unsigned
numbers
Remaining conditional jumps test individual
flag bits, such as overflow and parity.

## Slide 30
Remaining conditional jumps test individual
flag bits, such as overflow and parity.
– notice that JE has an alternative opcode JZ
All instructions have alternates, but many aren’t used in programming because they don’t usually fit the condition under test.

## Slide 31: The Conditional Set Instructions
80386 - Core2 processors also contain
conditional set instructions.
  conditions tested by conditional jumps put to work with the conditional set instructions
  conditional set instructions set a byte to either 01H or clear a byte to 00H, depending on the outcome of the condition under test
Useful where a condition must be tested at a point much later in the program.

## Slide 32: LOOP
A combination of a decrement CX and the JNZ
conditional jump.
In 8086 - 80286 LOOP decrements CX.
  if CX != 0, it jumps to the address indicated
by the label
  If CX becomes 0, the next sequential instruction
executes
In 80386 and above, LOOP decrements either CX or ECX, depending upon instruction mode.

## Slide 33
In 16-bit instruction mode, LOOP uses CX; in
the 32-bit mode, LOOP uses ECX.
– default is changed by the LOOPW (using CX) and LOOPD (using ECX) instructions 80386 - Core2
In 64-bit mode, the loop counter is in RCX.
– and is 64 bits wide
There is no direct move from segment register
to segment register instruction.

## Slide 34: Conditional LOOPs
LOOP instruction also has conditional forms:
LOOPE and LOOPNE
LOOPE (loop while equal) instruction jumps if CX != 0 while an equal condition exists.
  will exit loop if the condition is not equal or the CX register decrements to 0
LOOPNE (loop while not equal) jumps if CX
!= 0 while a not-equal condition exists.
  will exit loop if the condition is equal or the CX
register decrements to 0

## Slide 35
In 80386 - Core2 processors, conditional
LOOP can use CX or ECX as the counter.
– LOOPEW/LOOPED or LOOPNEW/LOOPNED
override the instruction mode if needed
Under 64-bit operation, the loop counter uses
RCX and is 64 bits in width
Alternates exist for LOOPE and LOOPNE.
  LOOPE same as LOOPZ
  LOOPNE instruction is the same as LOOPNZ
In most programs, only the LOOPE and LOOPNE apply.

## Slide 36: 6–2 CONTROLLING THE FLOW OF THE PROGRAM
Easier to use assembly language statements
.IF, .ELSE, .ELSEIF, and .ENDIF to control the flow of the program than to use the correct conditional jump statement.
– these statements always indicate a special
assembly language command to MASM
Control flow assembly language statements beginning with a period available to MASM version 6.xx, and not to earlier versions.

## Slide 37
Other statements developed include
.REPEAT–.UNTIL and .WHILE–.ENDW.
– the dot commands do not function using the Visual C++ inline assembler
Never use uppercase for assembly language
commands with the inline assembler.
– some of them are reserved by C++ and will cause problems

## Slide 38: WHILE Loops
Used with a condition to begin the loop.
  the .ENDW statement ends the loop
The .BREAK and .CONTINUE statements are
available for use with the while loop.
  .BREAK is often followed by .IF to select the break condition as in .BREAK .IF AL == 0DH
  .CONTINUE can be used to allow a DO–.WHILE
loop to continue if a certain condition is met
The .BREAK and .CONTINUE commands function the same manner in C++.

## Slide 39: REPEAT-UNTIL Loops
A series of instructions is repeated until some
condition occurs.
The .REPEAT statement defines the start of the loop.
  end is defined with the .UNTIL statement, which contains a condition
An .UNTILCXZ instruction uses the LOOP
instruction to check CX for a repeat loop.
  .UNTILCXZ uses the CX register as a counter
to repeat a loop a fixed number of times

## Slide 40
6–3 PROCEDURES
A procedure is a group of instructions that
usually performs one task.
  subroutine, method, or function is an important part of any system’s architecture
A procedure is a reusable section of the software stored in memory once, used as often as necessary.
  saves memory space and makes it easier to develop software

## Slide 41
Disadvantage of procedure is time it takes the
computer to link to, and return from it.
– CALL links to the procedure; the RET (return) instruction returns from the procedure
CALL pushes the address of the instruction following the CALL (return address) on the stack.
– the stack stores the return address when a
procedure is called during a program
RET instruction removes an address from the stack so the program returns to the instruction following the CALL.

## Slide 42
A procedure begins with the PROC directive
and ends with the ENDP directive.
– each directive appears with the procedure name
PROC is followed by the type of procedure:
  NEAR or FAR
In MASM version 6.x, the NEAR or FAR type can be followed by the USES statement.
  USES allows any number of registers to be automatically pushed to the stack and popped from the stack within the procedure

## Slide 43
Procedures that are to be used by all software
(global) should be written as far procedures.
Procedures that are used by a given task (local) are normally defined as near procedures.
Most procedures are near procedures.

## Slide 44: CALL
Transfers the flow of the program to the
procedure.
CALL instruction differs from the jump instruction because a CALL saves a return address on the stack.
The return address returns control to the instruction that immediately follows the CALL in a program when a RET instruction executes.

## Slide 45: Near CALL
3 bytes long.
  the first byte contains the opcode; the second
and third bytes contain the displacement
When the near CALL executes, it first pushes the offset address of the next instruction onto the stack.
  offset address of the next instruction appears in
the instruction pointer (IP or EIP)
It then adds displacement from bytes 2 & 3 to the IP to transfer control to the procedure.

## Slide 46
Why save the IP or EIP on the stack?
– the instruction pointer always points to the next instruction in the program
For the CALL instruction, the contents of IP/EIP are pushed onto the stack.
– program control passes to the instruction
following the CALL after a procedure ends
Figure 6–6 shows the return address (IP) stored on the stack and the call to the procedure.

## Slide 47
Figure 6-6 The effect of a near CALL on the stack and the instruction pointer.
11003
11002
11001
11000
(Procedure)
SP before CALL = FFFF SS before CALL = AOOO
IP before CALL = 0003
10004
10003
10002
10001
10000
} Near CALL
SP
AFFFF AFFFE AFFFO
Memory
Stack
00
03
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
PEARSON
- Architecture, Programming, and Interfacing, Eighth Edition
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Upper Saddle River, New Jersey 07458 ·All rights reserved.
Barry B. Brey
Copyright ©2009 by Pearson Education, Inc.
OF
FF
CALL

## Slide 48: Far CALL
5-byte instruction contains an opcode followed
by the next value for the IP and CS registers.
  bytes 2 and 3 contain new contents of the IP
  bytes 4 and 5 contain the new contents for CS
Far CALL places the contents of both IP and CS on the stack before jumping to the address indicated by bytes 2 through 5.
This allows far CALL to call a procedure located anywhere in the memory and return from that procedure.

## Slide 49
Figure 6–7 shows how far CALL calls a far
procedure.
– contents of IP and CS are pushed onto the stack
The program branches to the procedure.
  A variant of far call exists as CALLF, but should be avoided in favor of defining the type of call instruction with the PROC statement
In 64-bit mode a far call is to any memory location and information placed onto the stack is an 8-byte number.
  the far return instruction retrieves an 8-byte return
address from the stack and places it into RIP

## Slide 50
11003
11002
11001
11000
10004
Figure 6-7 The effect of a far CALL instruction.
AFFFF AFFFE AFFFO AFFFC AFFFB
SP
Memory
Slacl<
SP oofore CALL = FFFF SS before CALL • AOOO IP before CALL = 0005
""'
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
- Architecture, Programming, and Interfacing, Eighth Edition
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Upper Saddle River, New Jersey 07458 ·All rights reserved.
Barry B. Brey
PEARSON
Copyright ©2009 by Pearson Education, Inc.
(Procedure) |  | 
r--
10
00
00
05
.. --
-
11
00
00
02
CAU
10003 | 
10002 | 
10001 | 
10000 | 1.)

## Slide 51: CALLs with Register Operands
An example CALL BX, which pushes the
contents of IP onto the stack.
– then jumps to the offset address, located in register BX, in the current code segment
Always uses a 16-bit offset address, stored in any 16-bit register except segment registers.

## Slide 52: CALLs with Indirect Memory Addresses
Particularly useful when different subroutines
need to be chosen in a program.
– selection process is often keyed with a number
that addresses a CALL address in a lookup table
Essentially the same as the indirect jump that
used a lookup table for a jump address.

## Slide 53
RET
Removes a 16-bit number (near return) from the stack placing it in IP, or removes a 32-bit number (far return) and places it in IP & CS.
  near and far return instructions in procedure’s
PROC directive
  automatically selects the proper return instruction
Figure 6–8 shows how the CALL instruction links to a procedure and how RET returns in the 8086–Core2 operating in the real mode.

## Slide 54
Figure 6-8 The effect of a near return instruction on the stack and instruction pointer.
SP
AFFFF AFFFE
AFFFO
11003
11002
11001
11000
..,...--
r---""""'"
00
03
-.;::.
--
-
Stack
Near RET
SP before CALL::: FFFD
SS before CALL = AOOO
IP before CALL::: 1004
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
- Architecture, Programming, and Interfacing, Eighth Edition
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Upper Saddle River, New Jersey 07458 ·All rights reserved.
Barry B. Brey
PEARSON
Copyright ©2009 by Pearson Education, Inc.
RET | 
 | -
(Return here) | 
OF | 
FF | 
CALL | 
10004 |  | 
10003 |  | 
10002 |  | 
10001 |  | 
10000 |  | 

## Slide 55
Another form of return adds a number to the contents of the stack pointer (SP) after the return address is removed from the stack.
A return that uses an immediate operand is ideal for use in a system that uses the C/C++ or PASCAL calling conventions.
– these conventions push parameters on the stack before calling a procedure
If the parameters are discarded upon return, the return instruction contains the number of bytes pushed to the stack as parameters.

## Slide 56
Parameters are addressed on the stack by using the BP register, which by default addresses the stack segment.
Parameter stacking is common in procedures written for C++ or PASCAL by using the C++ or PASCAL calling conventions.
Variants of the return instruction:
– RETN and RETF
Variants should also be avoided in favor of using the PROC statement to define the type of call and return.

## Slide 57
6–4 INTRO TO INTERRUPTS
An interrupt is a hardware-generated CALL
  externally derived from a hardware signal
Or a software-generated CALL
  internally derived from the execution of an
instruction or by some other internal event
  at times an internal interrupt is called an exception
Either type interrupts the program by calling an interrupt service procedure (ISP) or interrupt handler.

## Slide 58: Interrupt Vectors
A 4-byte number stored in the first 1024 bytes
of memory (00000H–003FFH) in real mode.
  in protected mode, the vector table is replaced by an interrupt descriptor table that uses 8-byte descriptors to describe each of the interrupts
256 different interrupt vectors.
  each vector contains the address of an interrupt
service procedure

## Slide 59
Each vector contains a value for IP and CS that forms the address of the interrupt service procedure.
– the first 2 bytes contain IP; the last 2 bytes CS
Intel reserves the first 32 interrupt vectors for
the present and future products.
  interrupt vectors (32–255) are available to users
Some reserved vectors are for errors that
occur during the execution of software
  such as the divide error interrupt

## Slide 60
Some vectors are reserved for the
coprocessor.
– others occur for normal events in the system
In a personal computer, reserved vectors are used for system functions
Vectors 1–6, 7, 9, 16, and 17 function in the real mode and protected mode.
– the remaining vectors function only in the
protected mode

## Slide 61: Interrupt Instructions
Three different interrupt instructions available:
– INT, INTO, and INT 3
In real mode, each fetches a vector from the vector table, and then calls the procedure stored at the location addressed by the vector.
In protected mode, each fetches an interrupt
descriptor from the interrupt descriptor table.
Similar to a far CALL instruction because it places the return address (IP/EIP and CS) on the stack.

## Slide 62: INTs
256 different software interrupt instructions
(INTs) available to the programmer.
  each INT instruction has a numeric operand whose range is 0 to 255 (00H–FFH)
For example, INT 100 uses interrupt vector 100, which appears at memory address 190H–193H.
  address of the interrupt vector is determined by multiplying the interrupt type number by 4

## Slide 63
Address of the interrupt vector is determined
by multiplying the interrupt type number by 4.
– INT 10H instruction calls the interrupt service procedure whose address is stored beginning at memory location 40H (10H  4) in the mode
In protected mode, the interrupt descriptor is
located by multiplying the type number by 8
  because each descriptor is 8 bytes long
Each INT instruction is 2 bytes long.
  the first byte contains the opcode
  the second byte contains the vector type number

## Slide 64
When a software interrupt executes, it:
pushes the flags onto the stack
clears the T and I flag bits
pushes CS onto the stack
fetches the new value for CS from the
interrupt vector
pushes IP/EIP onto the stack
fetches the new value for IP/EIP from
the vector
jumps to the new location addressed by
CS and IP/EIP

## Slide 65
INT performs as a far CALL
– not only pushes CS & IP onto the stack, also pushes the flags onto the stack
The INT instruction performs the operation of a PUSHF, followed by a far CALL instruction.
Software interrupts are most commonly used to call system procedures because the address of the function need not be known.
The interrupts often control printers, video displays, and disk drives.

## Slide 66
INT replaces a far CALL that would otherwise
be used to call a system function.
– INT instruction is 2 bytes long, whereas the far CALL is 5 bytes long
Each time that the INT instruction replaces a
far CALL, it saves 3 bytes of memory.
This can amount to a sizable saving if INT often appears in a program, as it does for system calls.

## Slide 67: IRET/IRETD
Used only with software or hardware interrupt
service procedures.
IRET instruction will
  pop stack data back into the IP
  pop stack data back into CS
  pop stack data back into the flag register
Accomplishes the same tasks as the POPF
followed by a far RET instruction.

## Slide 68
When IRET executes, it restores the contents
of I and T from the stack.
– preserves the state of these flag bits
If interrupts were enabled before an interrupt service procedure, they are automatically re- enabled by the IRET instruction.
– because it restores the flag register
IRET is used in real mode and IRETD in the
protected mode.

## Slide 69: INT 3
A special software interrupt designed to
function as a breakpoint.
  a 1-byte instruction, while others are 2-byte
Common to insert an INT 3 in software to
interrupt or break the flow of the software.
  function is called a breakpoint
  breakpoints help to debug faulty software
A breakpoint occurs for any software interrupt, but because INT 3 is 1 byte long, it is easier to use for this function.

## Slide 70: INTO
Interrupt on overflow (INTO) is a conditional
software interrupt that tests overflow flag (O).
  If O = 0, INTO performs no operation
  if O = 1 and an INTO executes, an interrupt
occurs via vector type number 4
The INTO instruction appears in software that
adds or subtracts signed binary numbers.
  eith these operations, it is possible to have an overflow
JO or INTO instructions detect the overflow.

## Slide 71: An Interrupt Service Procedure
Interrupts are usually reserved for system
events.
Suppose a procedure is required to add the contents of DI, SI, BP, and BX and save the sum in AX.
– as a common task, it may be worthwhile to
develop the task as a software interrupt
It is also important to save all registers are changed by the procedure using USES.

## Slide 72: Interrupt Control
Two instructions control the INTR pin.
The set interrupt flag instruction (STI) places
1 in the I flag bit.
– which enables the INTR pin
The clear interrupt flag instruction (CLI) places a 0 into the I flag bit.
– which disables the INTR pin
The STI instruction enables INTR and the CLI
instruction disables INTR.

## Slide 73
In software interrupt service procedure, hardware interrupts are enabled as one of the first steps.
– accomplished by the STI instruction
Interrupts are enabled early because just about all of the I/O devices in the personal computer are interrupt-processed.
– if interrupts are disabled too long, severe system
problems result

## Slide 74: Interrupts in the Personal Computer
Interrupts found in the personal computer only
contained Intel-specified interrupts 0–4.
Access to protected mode interrupt structure in use by Windows is accomplished through kernel functions Microsoft provides.
– and cannot be directly addressed
Protected mode interrupts use an interrupt
descriptor table.

## Slide 75
Figure 6-9
Interrupts in a typical personal computer.
[- • ••j. of.iYl
.-bt't'.
+ ..Direct memory access (DMA)
+ ..Input/output (IO)
Interrupt reQUest (IRQ)
(JSA) 0
System timer
Easy Interne Keybord Communications Port (cor-wt2)
CommunicatiOns Pot (CO 1) Standard floppy disk controiler System CMOS/real t"me clock Numeric data processor
Primary IDE Channel
Secondary IOE Channel
rv'licrosoft ACPI-Compliant System
ALL-JN·WO .DER 9700 SERIES
Intet(r) 8280108/DSM USB Universal Host Controller- 24C2 SoundMAX lntegr ed Dig IAud o
Intet(r) 8280108/DBM USB Universal Host Controller - 24C7
Intel(r) 82801OB/OSM USS Universal Host Controller ·2 C4
ASUSTeK/Br oadcom 440x 10/100 Integrated Controller VIA OHCICompliant IEEE 1394 Host Con roller
Intef(r) 8280108/DSM USB 2.0 Enhanced Host Contro!er- 2<\CD Win XP Prornise FastTrak 376 (tm) Controller
(ISA) 1
JJ (ISA) 3
}} (JSA) 4
(ISA) 6
( SA) 8
(ISA) 13
(ISA) 14
( SA) 15
(ISA) 22 (PCI) 16 (PCI) 16
f) (PCI) 17
(PCI) 18
(PCI) 19 (PCI) 20
(PCI) 22
(PCI) 23
(PCI) 23
+ ..Memory
The Intel Microprocessors: 808618088, 80186180188, 80286, 80386, 80486 Pentium,
- Architecture, Programming, and Interfacing, Eighth Edition
Pentium Pro Processor, Pentium II, Pentium, 4, and Core2 with 64-bit Extensions
Upper Saddle River, New Jersey 07458 ·All rights reserved.
Barry B. Brey
PEARSON
Copyright ©2009 by Pearson Education, Inc.

## Slide 76: 64-Bit Mode Interrupts
The 64-bit system uses the IRETQ instruction
to return from an interrupt service procedure.
  IRETQ retrieves an 8-byte return from the stack
IRETQ also retrieves the 32-bit EFLAG register from the stack and places it into the RFLAG register.
It appears that Intel has no plans for using the
leftmost 32 bits of the RFLAG register.
  otherwise, 64-bit mode interrupts are the
same as 32-bit mode interrupts

## Slide 77
Figure 6–10 The stack frame created by the ENTER 8,0 instruction. Notice that BP is stored beginning at the top of the stack frame. This is followed by an 8-byte area called a stack frame.

## Slide 78
6–5 MACHINE CONTROL AND
MISCELLANEOUS INSTRUCTIONS
These instructions provide control of the carry bit, sample the BUSY/TEST pin, and perform various other functions.

## Slide 79: Controlling the Carry Flag Bit
The carry flag (C) propagates the carry or borrow in multiple-word/doubleword addition and subtraction.
  can indicate errors in assembly language
procedures
Three instructions control the contents of the
carry flag:
  STC (set carry), CLC (clear carry), and CMC (complement carry)

## Slide 80: WAIT
Monitors the hardware BUSY pin on 80286
and 80386, and the TEST pin on 8086/8088.
If the WAIT instruction executes while the BUSY pin = 1, nothing happens and the next instruction executes.
  pin inputs a busy condition when at a logic 0 level
  if BUSY pin = 0 the microprocessor waits for
the pin to return to a logic 1

## Slide 81
HLT
Stops the execution of software.
There are three ways to exit a halt:
  by interrupt; a hardware reset, or DMA operation
Often synchronizes external hardware
interrupts with the software system.
DOS and Windows both use interrupts extensively.
  so HLT will not halt the computer when
operated under these operating systems

## Slide 82
NOP
In early years, before software development tools were available, a NOP, which performs absolutely no operation, was often used to pad software with space for future machine language instructions.
When the microprocessor encounters a NOP,
it takes a short time to execute.

## Slide 83
If you are developing machine language programs, which are extremely rare, it is recommended that you place 10 or so NOPS in your program at 50-byte intervals.
– in case you need to add instructions at some
future point
A NOP may also find application in time delays to waste time.
A NOP used for timing is not very accurate because of the cache and pipelines in modern microprocessors.

## Slide 84: LOCK Prefix
Appends an instruction and causes the pin to
become a logic 0.
LOCK pin often disables external bus masters or other system components
– causes pin to activate for duration of instruction
If more than one sequential instruction islocked, LOCK pin remains logic 0 for duration of the sequence of instructions.
The LOCK:MOV AL,[SI] instruction is an
example of a locked instruction.

## Slide 85
ESC
Passes instructions to the floating-point
coprocessor from the microprocessor.
When an ESC executes, the microprocessor provides the memory address, if required, but otherwise performs a NOP.
Six bits of the ESC instruction provide the opcode to the coprocessor and begin executing a coprocessor instruction.
ESC is considered obsolete as an opcode.

## Slide 86: BOUND
A comparison instruction that may cause an
interrupt (vector type number 5).
Compares the contents of any 16-bit or 32-bit register against the contents of two words or doublewords of memory
– an upper and a lower boundary
If register value compared with memory is not
within the boundary, a type 5 interrupt ensues.
If it is within the boundary, the next instruction
in the program executes.

## Slide 87: ENTER and LEAVE
Used with stack frames, mechanisms used to pass parameters to a procedure through the stack memory.
Stack frame also holds local memory variables for the procedure.
Stack frames provide dynamic areas of memory for procedures in multiuser environments.

## Slide 88
ENTER creates a stack frame by pushing BP onto the stack and then loading BP with the uppermost address of the stack frame.
– allows stack frame variables to be accessed through the BP register
ENTER contains two operands:
  first operand specifies the number of bytes to reserve for variables on the stack frame
  the second specifies the level of the procedure
The ENTER and LEAVE instructions were
used to call C++ functions in Windows 3.1.

## Slide 89: SUMMARY
There are three types of unconditional jump
instructions: short, near, and far.
The short jump allows a branch to within
+127 and -128 bytes. The near jump (using a displacement of ±32K) allows a jump to
any location in the current code segment
(intrasegment). The far jump allows a jump
to any location in the memory system (intersegment).
(cont.)

## Slide 90: SUMMARY
Whenever a label appears with a JMP instruction or conditional jump, the label, located in the label field, must be followed by a colon (LABEL:). For example, the JMP DOGGY instruction jumps to memory location DOGGY:.
The displacement that follows a short or near jump is the distance from the next instruction to the jump location.
(cont.)

## Slide 91: SUMMARY
Indirect jumps are available in two forms:
  jump to the location stored in a register
and (2) jump to the location stored in a memory word (near indi-rect) or doubleword (far indirect).
Conditional jumps are all short jumps that test one or more of the flag bits: C, Z, O, P, or S. If the condition is true, a jump occurs; if the condition is false, the next sequential instruction executes.
(cont.)

## Slide 92: SUMMARY
The 80386 and above allow a 16-bit signed displacement for the conditional jump instructions.
In 64-bit mode, the displacement is 32 bits allowing a range of ±2G.
A special conditional jump instruction (LOOP) decrements CX and jumps to the label when CX is not 0.
(cont.)

## Slide 93: SUMMARY
The 80386 through the Core2 contain conditional set instructions that either set a byte to 01H or clear it to 00H.
If the condition under test is true, the operand byte is set to 01H; if the condition under test is false, the operand byte is cleared to 00H.
(cont.)

## Slide 94: SUMMARY
The .IF and .ENDIF statements are useful
in assembly language for making decisions.
The instructions cause the assembler to generate conditional jump statements that modify the flow of the program.
The .WHILE and .ENDW statements allow an assembly language program to use the WHILE construction, and the .REPEAT and
.UNTIL statements allow use of the
REPEAT-UNTIL construct.
(cont.)

## Slide 95: SUMMARY
Procedures are groups of instructions that perform one task and are used from any point in a program.
The CALL instruction links to a procedure and the RET instruction returns from a procedure. In assembly language, the PROC directive defines the name and type of procedure.
The ENDP directive declares the end of the
procedure.
(cont.)

## Slide 96: SUMMARY
The CALL construction is a combination of
a PUSH and a JMP instruction.
When CALL executes, it pushes the return address on the stack and then jumps to the procedure.
A near CALL places the contents of IP on the stack, and a far CALL places both IP and CS on the stack.
(cont.)

## Slide 97: SUMMARY
The RET instruction returns from a procedure by removing the return address from the stack and placing it into IP (near return), or IP and CS (far return).
Interrupts are either software instructions similar to CALL or hardware signals used to call procedures. This process interrupts the current program and calls a procedure.
After the procedure, a special IRET
instruction returns control to the software.
(cont.)

## Slide 98: SUMMARY
Real mode interrupt vectors are 4 bytes long and contain the address (IP and CS) of the interrupt service procedure.
The microprocessor contains 256 interrupt vectors in the first 1K bytes of memory. The first 32 are defined by Intel; the remaining 224 are user interrupts.
In protected mode, the interrupt vector is 8 bytes long and the vector table may be relocated to any section of the memory.
(cont.)

## Slide 99: SUMMARY
Whenever an interrupt is accepted by the microprocessor, the flags IP and CS are pushed onto the stack.
Besides pushing the flags, the T and I flag bits are cleared to disable both the trace function and the INTR pin.
The final event that occurs for the interrupt is that the interrupt vector is fetched from the vector table and a jump to the interrupt service procedure occurs.
(cont.)

## Slide 100: SUMMARY
Software interrupt instructions (INT) often replace system calls. Soft-ware interrupts save 3 bytes of memory each time they replace CALL instructions.
A special return instruction (IRET) must be used to return from an in-terrupt service procedure. The IRET instruction not only removes IP and CS from the stack, it also removes the flags from the stack.
(cont.)

## Slide 101: SUMMARY
Interrupt on an overflow (INTO) is a conditional interrupt that calls an interrupt service procedure if overflow flag (O) = 1.
The interrupt enable flag (I) controls the INTR pin connection.
If the STI instruction executes, it sets I to enable the INTR pin. If the CLI instruction executes, it clears I to disable the INTR pin.
(cont.)

## Slide 102: SUMMARY
The carry flag bit (C) is clear, set, and complemented by the CLC, STC, and CMC instructions.
The BOUND instruction compares the contents of any 16-bit register against the contents of two words of memory: an upper and a lower boundary.
If the value in the register compared with memory is not within the upper and lower boundary, a type 5 interrupt ensues.
(cont.)

## Slide 103: SUMMARY
The ENTER and LEAVE instructions are used with stack frames. A stack frame is a mechanism used to pass parameters to a procedure through the stack memory.
The stack frame also holds local memory variables for the procedure.
The ENTER instruction creates the stack frame, and the LEAVE instruction removes the stack frame from the stack. The BP register addresses stack frame data.