## Slide 1
Electrical Circuit-I
9th Lecture
Summary 1

## Slide 2
Circuit elements are classified into
Passive elements
Active elements such as
1-Resistor
1-Voltage source like batteries
2- Inductor
2-Current source
3- Capacitor
3-Generators
4-Operational amplifier
There are two types of elements found in electric circuits: passive elements and active elements. An active element is capable of generating energy while a passive element is not.
1.1 Resistance of the material:
The flow of charge through any material encounters an opposing force due to the collisions between electrons and between electrons and other atoms in the material, which converts electrical energy into another form of energy such as heat, is called the resistance of the material . The unit of measurement of resistance is the ohm, for which the symbol is (Ω). The circuit symbol for resistance appears in Fig. (1.1)
Figure 1.1
The resistance of any material with a uniform cross-sectional area is determined by the following four factors:
Material resistivity
Length
Cross-sectional area
Temperature
Conductors will have low resistance levels, while insulators will have high resistance characteristics. At a fixed temperature of 20°C (room temperature), the resistance is related to the other three factors by:
(1-1)
where r (Greek letter rho) is a characteristic of the material called the resistivity, l is the length of the sample, and A is the cross-sectional area of the sample.
Table 1-1

## Slide 3
1.2 TEMPERATURE EFFECTS
Temperature has a significant effect on the resistance of conductors, semiconductors, and insulators. Conductors have a generous number of free electrons, and any introduction of thermal energy will have little impact on the total number of free carriers. In fact, the thermal energy will only increase the intensity of the random motion of the particles within the material and make it increasingly difficult for a general drift of electrons in any one direction to be established. The result is that for good conductors, an increase in temperature will result in an increase in the resistance level. so, conductors have a positive temperature coefficient.
The plot of Fig.(1.2) . (a) Positive temperature coefﬁcient—conductors; (b) negative temperature coefﬁcient—semiconductors.
it is important that we have some method of determining the resistance at any temperature within operating limits. At two different temperatures, T1 and T2 , the resistance of copper is

## Slide 4
R1 and R2 , we may develop a mathematical relationship between these values of resistances at different temperatures. as shown in equation (1-2).
(1-2)
(1-3)
Table (1-2)
where |T1| indicates that the inferred absolute temperature of the material involved is inserted as a positive value in the equation. In general, therefore, associate the sign only with T1 and T2 .
EXAMPLE 1.1 If the resistance of a copper wire is 50 at 20°C, what is its resistance at 100°C (boiling point of water)?
Solution:
EXAMPLE 1.2 If the resistance of a copper wire at freezing (0°C) is 30 ,what is its resistance at 40°C?
Solution:

## Slide 5
EXAMPLE 1.3 If the resistance of an aluminum wire at room temperature (20°C) is 100 m (measured by a milliohm meter), at what temperature will its resistance increase to 120 m?
Solution:
1.3 Temperature Coefficient of Resistance
There is a second popular equation for calculating the resistance of a conductor at different temperatures. Deﬁning :
(1-4)
as the temperature coefﬁcient of resistance at a temperature of 20°C, and R20 as the resistance of the sample at 20°C, the resistance R1 at a temperature T1 is determined by
(1-5)
Equation (1-4) can be written in the following form:
(1-6)
The values of a20 for different materials have been evaluated, and a few are listed in Table
Table (1-3)

## Slide 6
SERIES CIRCUITS:
A circuit consists of any number of elements joined at terminal points, providing at least one closed path through which charge can ﬂow. The circuit of Fig. below, has three elements joined at three terminal points (a, b, and c) to provide a closed path for the current I.
-The current is the same through series elements.
-The current is the same through series elements.
- to find the total resistance of N resistors in series, the following equation is applied:
To find the total resistance of N resistors of the same value in series, simply multiply the value of one of the resistors by the number in series; that is,
the current drawn from the source can be determined using Ohm’s law, as follows:
the voltage
across
each resistor with the total resistance. using Ohm’s
law; that is,

## Slide 7
The power delivered to each resistor can then be determined using any one of three equations as listed below for R1:
The power delivered by the source is:
The total power delivered to a resistive circuit is equal to the total power dissipated by the resistive elements.
That is,
EXAMPLE: for Figure
find the total resistance for the series circuit of
Calculate the source current I .
Determine the voltages V1 , V2 , and V3 .
Calculate the power dissipated by R1 , R2 , and R3 .
Determine the power delivered by the source, and compare it to the sum
of the power levels of part (d).
Solutions:

## Slide 8
EXAMPLE : Determine RT , I, and V2 for the circuit of Fig. below
Solution: Note the current direction as established by the battery and the polarity of the voltage drops across R2 as determined by the current direction. Since
R1 = R3=R4 ,

## Slide 9
KIRCHHOFF’S VOLTAGE LAW:
Kirchhoff’s voltage law (KVL) :states that the algebraic sum of the potential rises and drops around a closed loop (or path) is zero.
A closed loop: is any continuous path that leaves a point in one direction and returns to that same point from another direction without leaving the circuit.
In Fig. 5.12, by following the current, we can trace a continuous path that leaves point a through R1 and returns through E without leaving the circuit. Therefore, abcda is a closed loop. For us to be able to apply Kirchhoff’s voltage law, the summation of potential rises and drops must be made in one direction around the closed loop.
For uniformity, the clockwise (CW) direction will be used throughout the text for all applications of Kirchhoff’s voltage law.
which for the circuit of Fig. yields (clockwise direction, following the current I and starting at point d):
the applied voltage of a series circuit equals the sum of the voltage drops across the series elements.

## Slide 10
Kirchhoff’s voltage law can also be stated in the following form:
If the loop were taken in the counterclockwise direction starting at point a, the following would result:
The application of Kirchhoff’s voltage law need not follow a path that includes current-carrying elements.
For example, in Fig. 5.13 there is a difference in potential between points a and b, even though the two points are not connected by a current- carrying element. Application of Kirchhoff’s voltage law around the closed loop will result in a difference in potential of 4 V between the two points. That is, using the clockwise direction:
EXAMPLE 5.4 Determine the unknown voltages for the networks of Fig.

## Slide 11
Solution (a):
Solution(b):
Or
EXAMPLE : Using Kirchhoff’s voltage law, determine the unknown voltages for the network shown below.

## Slide 12
Solution (a):
Solution (b):
Since the result is negative, we know that a should be negative and b should be positive, but the magnitude of 18 V is correct.
EXAMPLE : For the circuit shown
Find RT .
Find I.
Find V1 and V2.
Find the power to the 4Ω and 6Ω resistors.
Find the power delivered by the battery,
and compare
it to that
dissipated by the 4Ω and 6Ω resistors combined.
f) Verify Kirchhoff’s voltage law (clockwise direction).
Solution:

## Slide 13
EXAMPLE : For the circuit of Fig. shown:
Determine V2 using Kirchhoff’s voltage law.
Determine I.
Find R1 and R3.
Solutions:
a) Kirchhoff’s voltage law (clockwise direction):

## Slide 14
voltage divider rule : a method referred to as the voltage divider rule (VDR) that permits determining the voltage levels without first finding the current. The rule can be derived by analyzing the network shown.
where Vx is the voltage across Rx , E is the impressed voltage across the series elements, and RT is the total resistance of the series circuit
The voltage divider rule (VDR) :states that the voltage across a resistor in a series circuit is equal to the value of that resistor times the total impressed voltage across the series elements divided by the total resistance of the series elements.
EXAMPLE 5.11 Using the voltage divider rule, determine the voltages V1 and V3 for the series circuit shown in Fig.

## Slide 15
Solution:
.

## Slide 16
Parallel Circuits
Two elements, branches, or networks are inparallel if they have two
points in common. In Fig. shown below, for example, elements 1 and
2 have terminals a and b in common; they are therefore in parallel.
Different ways in which three parallel elements may appear in this Figures.
-Total Conductance and Resistance
For parallel elements, the total conductance is the sum of the individual conductance. That is, for the parallel network of Fig. , we write:
Since G =1/R, the total resistance for the network can be determined by:

## Slide 17
Determining the total resistance of parallel resistors.
EXAMPLE : Determine the total conductance and resistance for the parallel network of Fig. shown.
Solution:
EXAMPLE : Determine the effect on the total conductance and resistance of the network of previous Fig. if another resistor of 10 Ω were added in parallel with the other elements.
Solution:
*Note, as mentioned above, that adding additional terms increases the conductance level and decreases the resistance level.
EXAMPLE : Determine the total resistance for the network of Fig. below.
Solution:

## Slide 18
The above examples demonstrate an interesting and useful (for checking purposes) characteristic of parallel resistors:
The total resistance of parallel resistors is always less than the value of the smallest resistor.
-For equal resistors in parallel, the equation for the total resistance becomes significantly easier to apply. For N equal resistors in parallel :
EXAMPLE : Find the total resistance for the configuration in Fig.

## Slide 19
Solution: Redrawing the network
Special Case: Two Parallel Resistors
For two parallel resistors, the total resistance is determined by Eq. :
Multiplying the top and bottom of each term of the right side of the equation by the other resistor results in
In words, the equation states that
the total resistance of two parallel resistors is simply the product of their values divided by their sum.
EXAMPLE : Determine the total resistance for the parallel combination in Fig.
Solution:

## Slide 20
First the 1Ω and 4Ω resistors are combined, resulting in the reduced network in Fig.
Then,
KIRCHHOFF’S CURRENT LAW (KCL):
The algebraic sum of the currents entering and leaving a junction (or region) of a network is zero.
In Fig. below, for example, the shaded area can enclose an entire system or a complex network, or it can simply provide a connection point (junction) for the displayed currents. In each case, the current entering must equal that leaving,

## Slide 21
EXAMPLE : Determine currents I3 law.
and I4
in Fig. using Kirchhoff’s current
Solution:
EXAMPLE : Determine currents I3 and I5 in Fig. through applications of Kirchhoff’s current law.

## Slide 22
EXAMPLE : For the parallel dc network in Fig.
Determine the source current Is .
Find the source voltage E.
Determine R3.
Calculate RT
Solution:

## Slide 23
a)
b)
c)
d)
CURRENT DIVIDER RULE:
We now introduce the equally powerful current divider rule (CDR) for finding the current through a resistor in a parallel circuit.
-For two parallel elements of equal value, the current will divide equally.
-For parallel elements with different values, the smaller the resistance, the greater the share of input current.
-For parallel elements of different values, the current will split with a ratio equal to the inverse of their resistor values.

## Slide 24
Deriving the current divider rule:
a) parallel network of N parallel resistors
b) reduced equivalent of Fig. in (a).
The current IT can then be determined using Ohm’s law:
Since the voltage V is the same across parallel elements, the following is true:
where the product Ix Rx ,refers to any combination in the series. Substituting for V in the above equation for IT, we have
Solving for Ix , the final result is the current divider rule:

## Slide 25
which states that:
The current through any branch of a parallel resistive network is equal to the total resistance of the parallel network divided by the resistor of interest and multiplied by the total current entering the parallel configuration.
EXAMPLE : For the parallel network in Fig., determine current I1 using (CDR).
Solution:
and the smallest parallel resistor receives the majority of the current.