## Slide 1
Digital Signal Processing
Course Instructor
Dr. Ali J. Abboud
Lecture No. 1: Introduction
Third Class
Department of Computer and Software Engineering
http://www.engineering.uodiyala.edu.iq/
https://www.facebook.com/Engineer.College1

## Slide 2: Course Overview
Signals and Systems.
Classification of Discrete Digital Systems.
Time and Frequency Domains Analysis.
Signal Transformation Methods: Fourier, Wavelet and Z-transform.
Digital Filter Types: FIR and IIR Filters.
Digital Filter Design.
Analog Filter Design.
DSP Applications.

## Slide 3: Books
J.G. Proakis and D.G. Manolakis, Digital Signal Processing, 4rd edition, Prentice-Hall , 2006.
R.G Lyons, Understanding Digital Signal processing, 3rd edition, Prentice-Hall, (Amazon’s top-selling for five straight year) ,2011.
Monsons Hays, Schaums Outline of Digital Signal processing, 2nd edition ,McGraw-Hill Companies, 2012.
Richard, The Essential Guide to Digital Signal Processing, 1st edition Prentice-Hall ,ePUB, 2014.
J.G. Proakis , Digital Signal Processing Using MATLAB, 3rd edition, Cengage Learning , 2012.

## Slide 4: What is Digital Signal Processing?
Signal: It can be broadly defined as any physical quantity that varies as a time and/or space and has the ability to convey information, examples of these signals are:
Electrical signals: currents and voltages in AC circuits, radio communications signals, video signals etc.
Mechanical signals: sound or pressure waves, vibrations in a structure, earthquakes, etc.
Biomedical signals: electro-encephalogram, lung and heart monitoring, X-ray and other types of images.
Finance: time variations of a stock value or a market index.
Digital Signal: operating by the use of discrete signals to represent data in the form of numbers.

## Slide 5: What is Digital Signal Processing?
Processing: a series operations performed according to
programmed instructions.

## Slide 6: What is Digital Signal Processing?
Converting a continuously changing waveform (analog) into a series of discrete levels (digital)

## Slide 7: What is Digital Signal Processing?

## Slide 8: What is Digital Signal Processing?

## Slide 9: What is Digital Signal Processing?
discrete signal is discrete in time but continuous in amplitude.
digital signal is discrete in both time and amplitude.

## Slide 10: The Concepts of Signals and Systems
The most convenient mathematical representation of a signal is via the concept of a function, say x(t). In this notation:
x represents the dependent variable (e.g. voltage, pressure, etc.)
t represents the independent variable (e.g. time, space, etc.).
Depending on the nature of the independent and dependent variables, different types of signals can be identified such as:
Analog signals
Discrete signals
Digital signals
Multi-channel signals
Multi-dimensional signals

## Slide 11: The Concepts of Signals and Systems
System: A physical entity that operates on a set of primary signals (the inputs) to produce a corresponding set of resultant signals (the output).
The operations, or processing, may take several forms: modification, combination, decomposition, filtering, extraction of parameters, etc.
System characterization: a system can be represented mathematically as a transformation between two signal sets , as in x[n] → y[n]:

## Slide 12: The Concepts of Signals and Systems

## Slide 13: The Concepts of Signals and Systems

## Slide 14: Basic components of a DSP System
In its most general form, a DSP system will consist of three main components, as illustrated below:
The analog-to-digital (A/D) converter transforms the analog signal xc(t) at the system input into a digital signal xd[n].
The digital system performs the desired operations on the digital signal xd [n] and produces a corresponding output yd [n] also in digital form.
The digital-to-analog (D/A) converter transforms the digital output yd [n] into an analog signal yc (t) suitable for interfacing with the outside world.

## Slide 15: Basic components of a DSP System

## Slide 16: Basic components of a DSP System

## Slide 17: DSP Implementation –Analog/Digital Conversion
To implement DSP we must be able to:
(1) perform numerical operations including, for example, additions, multiplications,
data transfers and logical operations either using computer or special-purpose
hardware.
(2) convert the digital information, after being processed back to an analog signal –
involves digital-to- analog conversion and reconstruction .
e.g. text-to-speech signal (characters are used to generate artificial sound)

## Slide 18: DSP Implementation –Analog/Digital Conversion
To implement DSP we must be able to:
3) convert analog signals into the digital information - sampling & involves analog-to-digital conversion.
e.g. Touch-Tone system of telephone dialling (when button is pushed two sinusoid signals are generated (tones) and transmitted, a digital system determines the frequencies and uniquely identifies the button – digital (1 to 12) output
perform both A/D and D/A conversions
e.g. digital recording and playback of music (signal is sensed by microphones, amplified, converted to digital, processed, and converted back to analog to be played.

## Slide 19: DSP Chips : Special Purpose Hardware

## Slide 20: Limitations of DSP-Aliasing Most signals are analog in nature, and have to be sampled.
we only take samples of the signals at intervals and don’t know what happens in between

## Slide 21: Limitations of DSP - Antialiasing Filter

## Slide 22: Limitations of DSP – Frequency Resolution

## Slide 23: Limitations of DSP – Quantization Error

## Slide 24: Advantages of Digital over Analog Signal Processing
Why still do it?
• Digital system can be simply reprogrammed for other applications / ported to different hardware / duplicated (Reconfiguring analog system means hardware redesign, testing, verification)
• DSP provides better control of accuracy requirements (Analog system depends on strict components tolerance, response may drift with temperature)
• Digital signals can be easily stored without deterioration (Analog signals are not easily transportable and often can’t be processed off-line)
• More sophisticated signal processing algorithms can be implemented
(Difficult to perform precise mathematical operations in analog form)

## Slide 25: Advantages of Digital over Analog Signal Processing
Advantages:
Robustness:
Signal levels can be regenerated.
Precision not affected by external factors
Storage capability:
DSP system can be interfaced to low-cost devices for lasting storage
allows for off-line computations
Flexibility:
Easy control of system accuracy via changes in sampling rate and number of representation bits.
Software programmable → reconfiguring the DSP operations simply by changing the program.
Structure:
Easy interconnection of DSP blocks (no loading problem)
Possibility of sharing a processor between several tasks
Disadvantages:
Cost/complexity added by A/D and D/A conversion.
Input signal bandwidth is technology limited.
Quantization effects.

## Slide 26: Applications of DSP-Radar

## Slide 27: Applications of DSP: Biomedical

## Slide 28: Applications of DSP: Speech

## Slide 29: Applications of DSP: Communications

## Slide 30: Applications of DSP: Image Processing

## Slide 31: Applications of DSP: Music

## Slide 32: Applications of DSP: Multimedia

## Slide 33: Applications of DSP