## Slide 1
December 6,
2018
ELECTRICAL MACHINES & DRIVES
Q1: A 206 W, 120 V, 60 Hz, single phase IM has constants referred to the stator are; rotor impedance (3.6+j 2.6) ohm, stator impedance (1.8+j 3.5) ohm and
magnetizing reactance of stator winding = j 58.5. Find the mechanical power output?
 | ﻲﺛﻼﺜﻟا ﻢﺳﻻا
ﺔﻌﺑاﺮﻟا | ﺔﻠﺣﺮﻤﻟا
COLLEGE OF ENGINEERING ELECTRICAL POWER AND MACHINES ENGINEERING DEPARTMENT
Year: senior Time: 1:00 6/12/2019
elecTrical machines & Drives

## Slide 2
December 6,
2018
ELECTRICAL MACHINES & DRIVES
Q2 –A- Explain the basic principle of shaded pole motor?
How can we reverse the direction of rotation:-
  Split phase induction motor,
  Capacitor Start-and-Run Motor,
  Repulsion- start-induction-run motors

## Slide 3
December 6,
2018
ELECTRICAL MACHINES & DRIVES
Q3- The equivalent impedance o main and auxiliary windings in a capacitor motor are (8+j 11.75) ohm and (30+j 65) ohm respectively. While the capacitance is 6 µF. determine the line current at starting on a 230 V, 50 Hz supply?

## Slide 4
December 6,
2018
ELECTRICAL MACHINES & DRIVES
Q4 A- Explain why two winding are used in a single phase induction motor of the
split-phase type?
B - How are these winding arranged relative to each other and Why?
C- What is the point form using capacitor in some type of single phase indication motor?