## Slide 1: First Course of Special Machine
Department of Electrical Power and Machine Engineering
By Qasim Al Azze 2018

## Slide 2
C H A P T E
R36
CONTENTS
 | Learning Objectives | SINGLE-PHASE MOTORS Single phase motor
➣ Types of Single-phase Mo tors ➣ Single-phase Induction Mo tor ➣ Double-field Revolin g Theory ➣ Making Single-phase Induction Mo tor Self- starting ➣ Equivalent Circ uit of Single-phase Induction Mo tor without Core Loss ➣ Equivalent Cuicuit With Core Loss ➣ Types of Capa citors Start Mo tors ➣ Capa citor Start-and-Run Mo tor ➣ Shad ed-pole Single-phase Mo tor ➣ Repulsion Type Mo tors ➣ Repulsion Mo tor ➣ Repulsion Prin ciple ➣ Com pensated Repulsion Mo tor ➣ Repulsion-start Induction- Run Mo tor ➣ Repulsion Induction Mo tor ➣ A.C. Series Mo tors ➣ Universal Mo tor ➣ Spee d c ontrol of Universal Mo tors ➣ Reluctanc e Mo tor ➣ Hysteresis Mo tor CONTENTS |  | 

## Slide 3
1368
Electrical Technology
36.1. Types of Single-Phase Motors
Such motors, which are designed to operate from a single- phase supply, are manufactured in a large number of types to perform a wide variety of useful services in home, offices, factories, workshops and in business establishments etc. Small motors, particularly in the fractional kilo watt sizes are better known than any other. In fact, most of the new products of the manufacturers of space vehicles, aircrafts, business ma- chines and power tools etc. have been possible due to the advances made in the design of fractional-kilowatt motors. Since the performance requirements of the various applica- tions differ so widely, the motor-manufacturing industry has developed many different types of such motors, each being designed to meet specific demands.
Single-phase motors may be classified as under, depending on their construction and method of starting :
Induction Motors (split-phase, capacitor and shaded-pole etc.)
Repulsion Motors (sometime called Inductive-Series Motors)
A.C. Series Motor
Un-excited Synchronous Motors
36.2. Single- phase Induction Motor
Constructionally, this motor is, more or less, similar to a polyphase induction motor, except that
(i) its stator is provided with a single-phase winding and (ii) a centrifugal switch is used in some types of motors, in order to cut out a winding, used only for starting purposes. It has distributed stator winding and a squirrel-cage rotor. When fed from a single-phase supply, its stator winding produces a flux (or field) which is only alternating i.e. one which alternates along one space axis only. It is not a synchronously revolving (or rotating) flux, as in the case of a two- or a three-phase stator winding,
fed from a 2-or 3-phase supply. Now, an alternating or pulsating flux acting on a stationary squirrel-cage rotor cannot produce rotation (only a revolving flux can). That is why a single-phase motor is not self- starting.
However, if the rotor of such a machine is given an initial start by hand (or small motor) or otherwise, in either direction, then immediately a torque arises and the motor accelerates to its final speed (unless the applied torque is too high).
This peculiar behaviour of the motor has been explained in two ways : (i) by two -field or double- field revolving theory and (ii) by cross-field theory. Only the first theory will be discussed briefly.
36.3. Double-field Revolving Theory
This theory makes use of the idea that an alternating uni-axial quantity can be represented by two oppositely-rotating vectors of half magnitude. Accordingly, an alternating sinusoidal flux can be
Split-phase motor. Switch mechanism disconnects start winding when motor reached three-fourths of rated speed
Single-phase induction motor

## Slide 4
Single-phase Motors
1369
* For example, a flux given by  = m cos 2 ft is equivalent to two fluxes revolving in opposite directions, each with a magnitude of 1/2 and an angular velocity of 2f. It may be noted that Euler’s expressions for cos  provides interesting justification for the decomposition of a pulsating flux. His expression is
cos  =
2
e j  e j
The term e j represents a vector rotated clockwise through an angle  whereas e j represents rotation in anticlockwise direction. Now, the above given flux can be expressed as
m
 cos 2 ft =
2
m e j2 f t  e j2 f t 
The right-hand expression represents two oppositely-rotating vectors of half magnitude.
represented by two revolving fluxes, each equal to half the value of the alternating flux and each rotating synchronously (Ns = 120f/P) in opposite direction*.
As shown in Fig. 36.1 (a), let the alternating flux have a maximum value of m. Its component fluxes A and B will each be equal to m /2 revolving in anticlockwise and clockwise directions re- spectively.
Fig. 36.1
After some time, when A and B would have rotated through angle +  and  , as in Fig. 36.1 (b), the resultant flux would be
2 2
m
= 2  m cos 2  =  cos 
After a quarter cycle of rotation, fluxes A and B will be oppo- sitely-directed as shown in Fig. 36.1 (c) so that the resultant flux would be zero.
After half a cycle, fluxes A and B will have a resultant of  2 
m /2 =  m. After three-quarters of a cycle, again the resultant is
Fig. 36.2