## Slide 1: First Course of Special Machine
Department of Electrical Power and Machine Engineering
By Qasim Al Azze 2018

## Slide 2
1370
Electrical Technology
zero, as shown in Fig. 36.1 (e) and so on. If we plot the values of resultant flux against  between limits  = 0º to = 360º, then a curve similar to the one shown in Fig. 36.2 is obtained. That is why an alternating flux can be looked upon as composed of two revolving fluxes, each of half the value and revolving synchronously in opposite directions.
It may be noted that if the slip of the rotor is s with respect to the forward rotating flux (i.e. one which rotates in the same direction as rotor) then its slip with respect to the backward rotating flux is (2  s)*.
Each of the two component fluxes, while revolving round the stator, cuts the rotor, induces an
e.m.f. and this produces its own torque. Obviously, the two torques (called forward and backward torques) are oppositely-directed, so that the net or resultant torques is equal to their difference as
shown in Fig. 36.3.
g
Now, power developed by a rotor is P =
2 2
I R
s
1 
 s  2
 
 
If N is the rotor r.p.s., then torque is given by
g
T =
2 2
1
.
I R

1  s  2
 
2 N s
 
Now,
N = Ns (1 s)
 Tg =
1
I 2 R
I 2 R
s
. 2 2  k . 2 2
2 Ns s
Hence, the forward and backward torques are given by
Tf =
I 2 R
K 2 2
s
and Tb =
I 2 R
 K . 2 2
(2  s)
I 2 R
Tf = 2 2 synch.watt
I 2 R
s (2  s)
and Tb =  2 2 synch. watt
or
Total torque
T = Tf + Tb
Fig. 36.3 shows both torques and the resultant torque for slips between zero and +2. At standstill,
s = 1 and (2  s) = 1. Hence, Tf and Tb are numerically equal but, being oppositely directed, produce
no resultant torque. That ex- plains why there is no start- ing torque in a single-phase induction motor.
However, if the rotor is started somehow, say, in the clockwise direction, the clock- wise torque starts increasing and, at the same time, the anticlockwise torque starts de- creasing. Hence, there is a certain amount of net torque in the clockwise direction which accelerates the motor to full speed.
* It may be proved thus : If N is the r.p.m. of the rotor, then its slip with respect to forward rotating flux is
Ns Ns Ns
s = Ns  N  1  N or N  1  s
Keeping in mind the fact that the backward rotating flux rotates opposite to the rotor, the rotor slip with respect to this flux is
b
Ns Ns
s = Ns  ( N )  1  N  1  (1  s)  (2  s)
Fig. 36.3

## Slide 3
Single-phase Motors
1371
36.4. Making Single- phase Induction Motor Self-starting
As discussed above, a single-phase induction motor is not self-starting. To overcome this drawback and make the motor self-starting, it is temporarily converted into a two-phase motor during starting
period. For this purpose, the stator of a single-phase motor is provided with an extra winding, known as starting (or auxiliary) winding, in addition to the main or running winding. The two windings are spaced 90º electrically apart and are connected in parallel across the single-phase supply as shown in Fig. 36.4.
It is so arranged that the phase-difference between the currents in the two stator windings is very large (ideal value being 90º). Hence, the motor behaves like a two- phase motor. These two currents produce a revolving flux and hence make the motor self-starting.
There are many methods by which the necessary
phase-difference between the two currents can be created.
(i) In split-phase machine, shown in Fig. 36.5 (a), the main winding has low resistance but high reactance whereas the starting winding has a high resistance, but low reactance. The resistance of the
starting winding may be increased either by connecting a high resistance R in series with it or by choosing a high-resistance fine copper wire for winding purposes.
Hence, as shown in Fig. 36.5 (b), the current Is drawn by the starting winding lags behind the applied voltage V by a small angle whereas current Im taken by the main winding lags behind V by a very large angle. Phase angle between Is and Im is made as large as possible because the starting torque of a split-phase motor is proportional to sin . A centrifugul switch S is connected in series with the starting winding and is located inside the motor. Its function is to automatically disconnect the starting winding from the supply when the motor has reached 70 to 80 per cent of its full-load speed.
In the case of split-phase motors that are hermetically
sealed in refrigeration units, instead of internally-mounted centrifugal switch, an electromagnetic type of relay is used. As shown in Fig. 36.6, the relay coil is connected in series with main winding and the pair of contacts which are normally open, is included in the starting winding.
Fig. 36.4
Single-phase motor.
Fig. 36.5
Fig. 36.6

## Slide 4
1372
Electrical Technology
During starting period, when Im is large, relay contacts close thereby allowing Is to flow and the motor starts as usual. After motor speeds up to 75 per cent of full-load speed, Im drops to a value that is low enough to cause the contacts to open.
A typical torque/speed characteristic of such a motor is shown in Fig. 36.7. As seen, the starting torque is 150 to 200 per cent of the full-load torque with a starting current of 6 to 8 times the full-load current. These motors are often used in preference to the costlier capacitor-start motors. Typical applications are : fans and blowers, centrifugal pumps and separators, washing machines, small machine tools, duplicating machines and domestic refrigerators and oil burners etc. Commonly available sizes range from 1/20 to 1/3 h.p. (40 to 250 W) with speeds ranging from 3,450 to 865 r.p.m.
As shown in Fig. 36.8, the direction of rotation of such motors can be reversed by reversing the connections of one of the two stator windings (not both). For this purpose, the four leads are brought outside the frame.
As seen from Fig. 36.9, the connections of the starting winding have been reversed.
Fig. 36.7 Fig. 36.8 Fig. 36.9
The speed regulation of standard split-phase motors is nearly the same as of the 3-phase motors. Their speed varies about 2 to 5% between no load and full-load. For this reason such motors are usually regarded as practically constant-speed motors.
Note. Such motors are sometimes referred to as resistance-start split-phase induction motors in order to
distinguish them from capacitor-start induction run and capacitor start-and-run motors described later.
Fig. 36.10 Fig. 36.11 Fig. 36.12
(ii) Capacitor-start Induction-run motors. In these motors, the necessary phase difference between Is and Im is produced by connecting a capacitor in series with the starting winding as shown in Fig. 36.10. The capacitor is generally of the electrolytic type and is usually mounted on the outside of the motor as a separate unit (Fig. 36.11).
The capacitor is designed for extremely short-duty service and is guaranteed for not more than 20 periods of operation per hour, each period not to exceed 3 seconds. When the motor reaches about