## Slide 1
Dr. Qassem Hamed Jalut Associate Professor
Fluid Mechanics Class Note
DIMENSIONS AND UNITS

## Slide 2
Dr. Qassem Hamed Jalut Associate Professor
Fluid Mechanics Class Note

## Slide 3
Dr. Qassem Hamed Jalut Associate Professor
Fluid Mechanics Class Note
Main units are: Length (L), Mass (M), and Time (T). Most of the other quantities like force, pressure, power, and more can be derived from the main three quantities: LMT.
In fluid mechanics, there are only four primary dimensions from which all the dimensions can be derived: mass, length, time, and force. The brackets around a symbol like [M] mean “the dimension” of mass. All other variables in fluid mechanics can be expressed in terms of [M], [L], [T], and [F].
For example, acceleration has the dimensions [LT-2]. Force [F]
is directly related to mass, length, and time by Newton’s second law,
Force= Mass x Acceleration
F = m a
From this we see that, dimensionally, [F] = [MLT-2]. 1 kg-force = 9.81 Newton of force = 9.81 N

## Slide 4
Dr. Qassem Hamed Jalut Associate Professor
Fluid Mechanics Class Note
Table (1) Primary Dimensions in Fluid Mechanics in the International System of Units (SI)
Celsius C o
K=Co + 273o
Table (2) Secondary Dimensions in Fluid Mechanics in the International System of Units (SI)
Area [L2]
m2
Volume [L3]
m3
Velocity [LT-1]
m/sec
Acceleration [LT-2]
m/sec2
Pressure or stress [FL-2]
Pa= N/m2(Pascal)
Angular Velocity
sec-1
Energy, work [FL] J = Nm (Joule)
Power [FLT-1] W = J/sec (Watt)
Specific mass (ρ) [ML-3] kg/m3
Table (3) Commonly used prefixes for SI units:
Unit
Dimension
meter (m)
Length (L)
kilogram (kg)
Mass (M)
second (s)
Time (T)
Newton (N) = kg.m/s2) = MLT-2
Force (F)
Kelvin K o
Temperature (θ)
10

## Slide 5
Dr. Qassem Hamed Jalut Associate Professor
Fluid Mechanics Class Note
Fluid Properties

## Slide 6
Dr. Qassem Hamed Jalut Associate Professor
Fluid Mechanics Class Note