## Slide 1
2103-213 Engineering Mechanics I
C
O
A
B
D
K

## Slide 2
Manner Guideline in this Lecture Course
Be reasonable and act politely.
Turn off your mobile phone. If you have urgent calls
to make or answer, kindly leave the room.
No noisy chat and all other activities that can distract
the lecture should be avoided.
No food. Only water and candy are allowed.
Do not disturb your classmates.
Dress properly.

## Slide 3: Textbook
“Engineering Mechanics STATICS”
R.C. Hibbeler, Engineering Mechanics
“Engineering Mechanics DYNAMICS”
R.C. Hibbeler, Engineering Mechanics
“Engineering Mechanics, STATICS”
Meriam and Kraige
“Engineering Mechanics, DYNAMICS”
Meriam and Kraige

## Slide 4
Mechanics ?
Mechanics
Statics
Dynamics
-Equilibrium
-Selected Topics
Kinematics
Kinetics
-Particles
-Rigid Bodies
-Particles
- Rigid Bodies
  A branch of physical science which deals with ( the states of rest or motion of ) bodies under action of forces
Dynamics: Motion of bodies
Statics:
Equilibrium of bodies
(no accelerated motion)
under action of Forces

## Slide 5: Mechanics #2
Mechanics
Statics
Dynamics
Mech of Materials
Fluid Mechanics
Vibration
Fracture Mechanics
Etc.
Structures
Automotives
Robotics
Spacecrafts
MEMs
Etc.
Basic Concepts

## Slide 6
Basic Concept - Definition
Space: Collection of points whose relative positions
can be described using “a coordinate system”
Time : For relative occurrence of events
Mass : - resistance to change in velocity [Dynamics],
- quantities that influence mutual attraction
  between bodies [Statics]
position,
velocity,
acceleration

## Slide 7
Basic Concept - Definition
Particle: Body of negligible dimensions
Rigid body: Body with negligible deformations
Non-rigid body: Body which can deform
In Statics, bodies are considered rigid unless stated otherwise.
Before considering whether the body can be assumed rigid-body or not,
you need to estimate the relevant force first.

## Slide 8
In dynamics, force is an action that tends to cause acceleration of an object.
The SI unit of force magnitude is the newton (N). One newton is equivalent to one kilogram-meter per second squared (kg·m/s2 or kg·m · s – 2)
Basic Concept - Force
Force: Vector quantity that describes an action of
one body on another [Statics]

## Slide 9
SCALARS AND VECTORS
Scalars: associated with “Magnitude” alone
Vectors: associated with “Magnitude” and “Direction”
- mass, density, volume, time, energy, …
- force, displacement, velocity, acceleration, …
: Direction
or V
Magnitude:
or V
Vector :
free vector
(“math” vector)

## Slide 10: Manipulation
Vector: magnitude & direction, components
  Scalar multiplication
  Addition, subtraction
  Dot product
  Cross product
  Mixed triple product
Scalar & Vector
Mathematical Meanings
vs
Physical Meanings

## Slide 11
Vector’s Point of Application
Vectors: “Magnitude”, “Direction”
F
Free Vector
rotating motion, couple
E.g.) Force on
non- rigid body
Fixed Vector
Sliding Vector
F
F
Rigid Body
E.g.) Force on
rigid-body
=
?
line of action
“Point of Application”
The external consequence of these two forces will be the same if ….
Rigid Body
Rotational motion occurs at every point in the object.
point of action
rotation
vector
Principle of
Transmissibility
Internal
Effect –
stress
External
effect

## Slide 12
The Principle of Transmissibility
“A force may be applied at any point on its given line of action without altering the resultant effects external to the rigid body on which it acts.”
We can slide the force along its line of action.
(force can be considered as sliding vector)
=
?
The two force can be considered equivalent if
……
If we concerns only about the external resultant effects on rigid body.

## Slide 13: Physical Quantity of Vector
Vectors representing physical quantities can be classified
Fixed Vector
  Its action is associated with a unique point of application
  Described by magnitude, direction & pt of application
Sliding Vector
  Has a unique line of action in space but not a unique point of application
  Described by magnitude, direction & line of action
Free Vector
  Its action is not confined or associated with a unique line in space.
  Described by magnitude & direction

## Slide 14
PRINCIPLES OF MECHANICS
1. The Parallelogram Law
2. The Principle of Transmissibility
3. Newton’s First Law
4. Newton’s Second Law
5. Newton’s Third Law
Some principles that governs the world of Mechanics:
6. Newton’s Law of Gravitation

## Slide 15
THE PARALLELOGRAM LAW
The two vectors V1 and V2 ,treated as free vectors, can be
replaced by their equivalent V, which is the diagonal of
the parallelogram formed by V1 and V2 as its two sides.
Note: If there are not free vectors, you can sum them if and only if they have the same point of the application.

## Slide 16
The Principle of Transmissibility
“A force may be applied at any point on its given line of action without altering the resultant effects external to the rigid body on which it acts.”
We can slide the force along its line of action.
(force can be considered as sliding vector)
=
?
The two force can be considered equivalent if
……
If we concerns only about the external resultant effects on rigid body.

## Slide 17
Summation of Force
Free Vector
S
S
displacement
if there are sliding vectors
concurrent forces
non-concurrent

## Slide 18
NEWTON’S LAWS OF MOTION (1st Law)
The study of rigid body mechanics is formulated on the basis of Newton’s laws of motion.
First Law:
An object at rest tends to stay at rest and an object in motion tends to stay in motion with the same speed and in the same direction, unless acted upon by an unbalanced force.

## Slide 19
NEWTON’S LAWS OF MOTION (2nd Law)
Second Law:
The acceleration of a particle is proportional to the vector sum of forces acting on it, and is in the direction of this vector sum.
m

## Slide 20
NEWTON’S LAWS OF MOTION
Third Law: The mutual forces of action and reaction between two particles are equal in magnitude, opposite in direction,
and collinear.
Confusing?
Concept of FBD (Free Body Diagram)
Point: Isolate the body
Forces always occur in pairs – equal and opposite action-reaction force pairs.

## Slide 21
Newton’s Law of Gravitation
  - M & m are particle masses
  G is the universal constant of gravitation,
  6.673 x 10-11 m3/kg-s2
  - r is the distance between the particles.
For Gravity on earth (at sea level)
where
- m is the mass of the body in question
- g = GM/R2 = 9.81 m/s2 (32.2 ft/s2)
m
M
W=mg
M
m
r
F