## Slide 1
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Moment distribution method
Introduction
In the previous lesson we discussed the slope-deflection method. In slope-deflection analysis, the unknown displacements (rotations and translations) are related to the applied loading on the structure. The slope-deflection method results in a set of simultaneous equations of unknown displacements. The number of simultaneous equations will be equal to the number of unknowns to be evaluated. Thus, one needs to solve these simultaneous equations to obtain displacements and beam end moments. Today, simultaneous equations could be solved very easily using a computer. Before the advent of electronic computing, this really posed a problem as the number of equations in the case of multistory building is quite large. The moment-distribution method proposed by Hardy Cross in 1932, actually solves these equations by the method of successive approximations. In this method, the results may be obtained to any desired degree of accuracy. Until recently, the moment-distribution method was very popular among engineers. It is very simple and is being used even today for preliminary analysis of small structures. It is still being taught in the classroom for the simplicity and physical insight it gives to the analyst even though stiffness method is being used more and more. Had the computers not emerged on the scene, the moment-distribution method could have turned out to be a very popular method.
Sign convention
We will establish same sign convention as that established for the slope –deflection equations, clock wise moments that act on members are considered positive , whereas counter clock wise moments are negative.

## Slide 2
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Member stiffness factor
Can be defined as the amount of moment required to rotate the end of beam 1 rad.
( )
( )
( )
b- Far end is pinned
( )
( ) ( )
( )
ϴA
L
a- Far end is fixed or continuous
M A
M'
B
B
ϴA
L
M A
ϴB

## Slide 3
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
c-symmetric beam and loading
MAB=-MBA
ϴB=- ϴA (due to symmetry)
( )
d-Symmetric beam with antisymmetric loading
MAB=MBA
ϴB= ϴA (due to anti symmetry)
( )
A
B
L
A
B
L
P
P

## Slide 4
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Carry-over factor
The carry-over factor represents the fraction of M that is carried over from the pin to the fixed end. For previous example the carry-over factor is +0.5. the plus sign indicates that both moment acts in the same direction.
Joint stiffness factor
If there are many members are meeting at a joint as shown
To evaluate the total stiffness at joint B(i.e. the amount of moment MB that required to rotate joint B 1 rad)
From equilibrium at joint B MB=MBA+MBD+MBE+MBC
As joint B rotates one rad all members that connected at this joint will rotate by same amount
, because they are fixed connected to joint B
A
C
D
E
2m
5m
3m
5m
MB B

## Slide 5
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
MB=KB , KB=KBA+KBD+KBE+KBC
Distribution factors
If a moment is applied to fixed connected joint, the connecting members will each supply a portion of the resisting moment necessary to satisfy moment equilibrium at the joint. That fraction of total resisting moment supplied by the member is called the distribution factor (D.F).to obtain this value, imagine the joint is connected to n members. If an applied moment causes the joint to rotate an amount ϴ, the each member i by this same amount. Return to previous example to evaluate the distribution factor of member AB
MAB=KAB ϴB , ϴB= MAB/ KAB MB=KB ϴB , ϴB= MB/ KB MAB/ KAB= MB/ KB= MB/ ∑K D.FAB= MAB/ MB= KAB/∑K
Noting that, ∑D.F=1

## Slide 6
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Special joints
If the end is fixed(wall, no rotation allow) To evaluate the distribution factor at joint A KAB=3EI/L
KA(wall)=∞
D.F AB=(3EI/L)/( 3EI/L+∞)=0
If the end is pinned(wall, no rotation allow) To evaluate the distribution factor at joint A
KAB=3EI/L
Solution
1-F.E.M
( )
( )
A
B
L
L
B
A
B
C D
A E
5 kN
25 kN.m
KA=0
D.F AB=(3EI/L)/( 3EI/L+0)=1
Example(1):- using moment distribution method analysis the continuous beam shown , due to the applied loading and:
A settlement at support D=18 mm downward , rotational slip at E=0.002 rad C.C.W. use EI=3(104) kN.m2
18 kN
12 kN/m
2 m
6 m
4 m
2 m
5 m
I 2I
3I

## Slide 7
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
( )
( )
( )
( )
2-distribution factor (D.F)
a-for joint c
( )
b-for joint D
( )

## Slide 8
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
joint |  | B | C |  | D |  | E
member |  | BC | CB | CD | DC | DE | ED
D.F |  | 1 | 0.273 | 0.727 | 0.357 | 0.643 | 0
Cycle1 | F.E.M | 10 | -25 |  | -128 | 291.8 | 269.8
 |  |  | 36 | -224 |  |  | 
 |  | -36 |  |  |  |  | 
 | Balance moment | 26 | 58.149 | 154.851 | -58.477 | -105.323 | 0
Cycle2 | C.O.M |  | 13 | -29.239 | 77.426 | 0 | -52.662
 | Balance moment |  | 4.433 | 11.806 | -27.641 | -49.785 | 0
Cycle3 | C.O.M |  | 0 | -13.821 | 5.903 | 0 | -24.893
 | Balance moment |  | 3.773 | 10.048 | -2.107 | -3.796 | 0
Cycle4 | C.O.M |  | 0 | -1.054 | 5.024 | 0 | -1.898
 | Balance moment |  | 0.288 | 0.766 | -1.794 | -3.23 | 0
Cycle5 | C.O.M |  | 0 | -0.897 | 0.383 | 0 | -1.615
 | Balance moment |  | 0.245 | 0.652 | -0.137 | -0.246 | 0
summation |  | 0 | 115.89 | -90.89 | -129.42 | 129.42 | 188.73
A
B
C
D
E
5 kN
25 kN.m
12 kN/m
2 m
6 m
4 m
2 m
5 m
I
2I
3I
10
5
115.89
90.89
18 kN
129.42
129.42
188.73
16.685
55.315
78.718
11.28233.63
93.63
A
B
C
D
E
5 kN
25 kN.m
18 kN
12 kN/m
2 m
6 m
4 m
2 m
5 m
I
2I
3I
21.685
134.033
22.348
188.73
93.63

## Slide 9
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
In 2011, Thaar Al-Gasham has developed new procedure in order to reduce calculations necessary for the method of moment distribution. He names this procedure as modified moment distribution. In this method, joints of internal supports are entered in calculations only, joints of external supports either pinned support or fixed support are omitted from calculation, depending upon:
External pinned or hinged support have not resisting moment so opposite moment to its fixed end moment is applied to this joint in order to became moment at it equals to zero. Noting, opposite joint to pinned will take 0.5 from applied moment.
The moment at external fixed end equals to its fixed end moment plus 0.5 increment of moment at opposite joint.
To illustrate this method numerically, previous example is reanalyzed using this alternative method
Same steps 1&2 for classical moment distribution are considered here 3- Modified F.E.M
( )
joint |  | C |  | D | 
member |  | CB | CD | DC | DE
D.F |  | 0.273 | 0.727 | 0.357 | 0.643
Cycle1 | F.E.M | -25 |  | -128 | 291.8
 |  | 49 | -224 |  | 
 | Balance moment | 54.6 | 145.4 | -58.477 | -105.323
Cycle2 | C.O.M | 0 | -29.289 | 72.7 | 0
 | Balance moment | 7.996 | 21.293 | -25.954 | -46.746
Cycle3 | C.O.M | 0 | -12.977 | 10.647 | 0
 | Balance moment | 3.343 | 9.434 | -3.801 | -6.846
Cycle4 | C.O.M | 0 | -1.901 | 4.717 | 0
 | Balance moment | 0.519 | 1.382 | -1.684 | -3.033
Cycle5 | C.O.M | 0 | -0.842 | 0.691 | 0
 | Balance moment | 0.23 | 0.612 | -0.247 | -0.445
summation |  | 115.89 | -90.89 | -129.41 | 129.41

## Slide 10
Solution
1-F.E.M
( )
( )
2- modification of F.E.M
( )
3-D.F
A
B
C
D
2m
2m
5m
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
( )
Example:- using moment distribution, analysis the beam shown. EI is constant
48 kN/m

## Slide 11
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
joint |  | B | 
member |  | BA | BC
D.F |  | 0.789 | 0.211
Cycle1 | F.E.M | 24 | -100
 | Balance moment | 59.964 | 16.036
Cycle2 | C.O.M | 0 | 0
 | Balance moment | 0 | 0
summation |  | 83.964 | -83.964
A
2m
48 kN/m
84
6
90
84
5m
48 kN/m
84
120
120
6
2m
5m
48 kN/m
A
A
D 6
B 210
C 210

## Slide 12
Solution
1- F.E.M
( )( )
( )( )
( )( )
( )( )
( )( )
( )( )
A
B
D
D'
I
2I
1.5I
3m
1m
30mm
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Analysis of Frame
1- Frame without side sway
Example:- using moment distribution method analyze the beam shown, it is subjected to system of forces as well as to rotational slip at C of 0.003 rad C.W, 30mm downward settlement at D and horizontal movement at D of 16 mm toward east. Take EI=104 kN.m2
6m 2m 4m
2
m
16mm
80KN
36KN
10KN/M
0.003RAD
A
C
D
D'
I
2I
1.5I
3m
1m
30mm
2m 4m
C 6m
2
m
16mm
80KN
36KN
10KN/M
0.003RAD
B30mm

## Slide 13
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
( )( )
2- D.F
D.F is calculated at B only
( )
Moment at fixed ends
( ( ))
joint |  | B |  | 
member |  | BA | BC | BD
D.F |  | 0.4 | 0.3 | 0.3
Cycle1 | F.E.M | -20 |  | 
 |  | -100 | 58 | 45
 | Balance moment | 6.8 | 5.1 | 5.1
summation |  | -93.2 | 63.1 | 50.1

## Slide 14
A
B
C
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
( )
( )
Now, all moments are determined. Therefore, all horizontal and vertical reactions can be easily determined.
3- Frame with side sway
Example:- analyze the beam using moment distribution. Take EI=1.5(104) kN.m2
D
I
1.5I
2I
6 KN/M
18KN
4m
4m
1cm
2m
1m
6m
A
B
C
D
I
1.5I
2I
6 KN/M
18KN
4m
4m
1cm
2m
1m
6m
1cm

## Slide 15
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Step 1:- analyze without side sway
1- F.E.M
( )
( ) ( )
( ) ( )
( )
( )( )
Modified F.E.M
( )
D.F
At joint C
joint |  | C | 
member |  | CB | CD
D.F |  | 0.273 | 0.727
Cycle1 | F.E.M | 18.75 | 0
 | Balance moment | -5.119 | -13.631
summation |  | 13.631 | -13.631

## Slide 16
1- F.E.M
Let EIΔ=100f
( )
( )( )
( )( )
2- MODIFIED F.E.M
A
B
C
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Final moments due to non side sway are
( )
2- Due to side sway
D
I
1.5I
2I
m
3m
6m
B'
C' | 4m
 | 4m
 | 1c
B"
Δ
Δ
B
B'
B"
4
5
3
Δ

## Slide 17
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Final moments due to side sway are
( )
Total moment=M(non side)+ M(side)
joint |  | C | 
member |  | CB | CD
D.F |  | 0.273 | 0.727
Cycle1 | F.E.M | 9.4f | 75f
 | Balance moment | -23.04f | -61.36f
summation |  | -13.64f | 13.64f
A
C
D
4m
4m
3m
6m
MAB
MDC
o
VD
10m
18
1m B
24
2m
VA
MDC

## Slide 18
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
( ) ( )
SUMMATION MOMENT ABOUT O =O
Then actual moments are,
Now, all moments are determined. Therefore, all horizontal and vertical reactions can be easily determined.
Example:- determine the moment at each joint of the frame shown. EI is constant
A
B
C
D
4m
5m
6m
200kN
A
B C
D
4m
5m
6m
200kN
Δ Δ

## Slide 19
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
There are no fixed ends moments due to applied loads. Therefore, there is no effect of non- side sway
1-D.F
At joint B
At joint C
EFFECT OF SIDE SWAY
Let EIΔ=100f
2-F.E.M

## Slide 20
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Final moments due to side sway are
( )
( )
joint |  | B |  | C | 
member |  | BA | BC | CB | CD
D.F |  | 0.556 | 0.444 | 0.545 | 0.455
Cycle1 | F.E.M | -37.5f | 0 | 0 | -16.7f
 | Balance moment | 20.85f | 16.65f | 9.102f | 7.595f
Cycle2 | C.O.M | 0 | 4.551f | 8.325f | 0
 | Balance moment | -2.53f | -2.021f | -4.537f | -3.788f
Cycle3 | C.O.M | 0 | -2.269f | -1.011f | 0
 | Balance moment | 1.262f | 1.007f | 0.551f | 0.46f
Cycle4 | C.O.M | 0 | 0.276f | 0.504f | 0
 | Balance moment | -0.153f | -0.123f | -0.275f | -0.229f
Cycle5 | C.O.M | 0 | -0.138f | -0.062f | 0
 | Balance moment | 0.077f | 0.061f | 0.034f | 0.028f
summation |  | -17.994f | 17.994f | 12.63f | -12.63f

## Slide 21
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
∑
A
B
C
D
4m
5m
6m
200kN
MAB
MDC
VA
VD