## Slide 1
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Deflections using castigliano's theory
It is method for determining the deflection and slope at a point in structure be is a truss, beam, or frame. It was developed by Italian railroad engineer Alberto Castigliano in 1879; sometime, it is known as least work method.
This method is applied only to structures that have: 1- Constant temperature
Unyielding supports
Materials are within elastic limits
In this theorem, the displacement or slope at a point in a structure is equal to first partial derivative of elastic energy in the structure with respect to the force or moment acting at this point in the same direction of displacement or slope, respectively.
1- Trusses
∑
Δ=external joint displacement of a truss
P=external force applied to the truss joint in the direction of Δ
N=internal force in a member caused by both the force P and loads on the truss L= length of a member
A=cross-sectional area of a member E=modulus of elasticity of a member
Example:- using Castigliano theorem, determine the horizontal deflection at joint B of the truss shown in figure. Each member has cross-sectional area of 300 mm2 and modulus of
elasticity of 200GPa.
4m
3m
3m
A
B
C
80kN

## Slide 2
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Member | N | δN/ δp | N(P=0) | L | N(δN/ δp)L
AB | -66.66+0.625P | 0.625 | -66.66 | 5 | -208.31
BC | 66.66+0.625P | 0.625 | 66.66 | 5 | 208.31
AC | 40-0.375P | -0.375 | 40 | 6 | -90
∑ |  |  |  |  | -90
∑
Example:- using Castigliano theorem, determine the vertical deflection at joint B of the truss shown in figure. Each member has cross-sectional area of 300 mm2 and modulus of elasticity
of 200GPa.
4m
3m
3m
A
B
C
P
53.33-0.5P
53.33+0.5P
40-0.375P
-66.66+0.625P80kN
66.66+0.625P
4m
3m
3m
A
B
C
80kN

## Slide 3
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Member | N | δN/ δp | N(P=0) | L | N(δN/ δp)L
AB | -66.66-0.83P | -0.83 | -66.66 | 5 | 276.64
BC | 66.66+0.83P | 0.83 | 66.66 | 5 | 276.64
AC | 40+0.5P | 0.5 | 40 | 6 | 120
∑ |  |  |  |  | 673.3
∑
∫ ( )
2- beams and frames
∫ ( )
Δ=external displacement of a point caused by the real loads acting on the beam or frame
ϴ= slope of a point caused by the real loads acting on the beam or frame M=internal moment in the beam or frame
P=external loads is applied to the beam or frame at point that required to determine the displacement in the direction of Δ
4m
3m
3m
A
80kN
P
B
53.33+0.67P
53.33+0.67P
40+0.5P
-66.66-0.83 P
C 66.66+0.83P

## Slide 4
PORTION | ORIGIN | LIMIT | M | dM/dM' | M(M'=0)
AB | A | 0-10 | (-2.5-0.1M')X | -0.1X | -2.5X
CB | C | 0-5 | -X2 | 0 | -X2
∫ ( ) ∫
∫
[ ]
A
C
10m
B5m
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
M'= external moments is applied to the beam or frame at point that required to determine the slope in the direction of ϴ
Example:- use the method of least work and determine the slope at B of the steel beam.E=200GPa and I=70(10)6mm4.
2kN/m
A
C
10m
B5m
2kN/m
X
M'
X
2.5+0.1M'
12.5+0.1M'

## Slide 5
∫ ( ) ∫ ∫
[ ]
[ ]
4- Composite structures
∫ ( ) ∑
PORTION | ORIGIN | LIMIT | M | dM/dP | M(P=0)
AB | A | 0-L | PL+0.5wL2 | L | 0.5wL2
CB | C | 0-L | PX+0.5wX2 | X | 0.5wX2
L
A
B
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
Example;- the L-shaped frame is made from two segments, each length of L and flexural stiffness EI. Determine the horizontal deflection at point C by using castigliano's theorem .
C
L
wkN/m
L
L
B
C
wkN/m
P
AP+wL
PL+0.5wL2
X
X

## Slide 6
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
∫ ( ) ∑
1-FOR TRUSS MEMBER
Member | N | δN/ δM' | N(M'=0) | L | N(δN/ δ M')L
DC | 16.67+M'/3 | 1/3 | 16.67 | 2 | 11.11
A
D
Example:- beam AB has a square cross section of 100mm by 100mm. bar CD has a diameter of 10mm. if both members are made of steel, determine the slope at A due to the loading of 10kN.E=200GPa
C
B
10kN
3m
2m
2m
D
B
3m
2m
16.67+M'/3
10kN
6.67+M'/3
M'
A
X
X

## Slide 7
THEORY OF STRUCTURES -------------------- DR. WISSAM D. SALMAN
2-for flexural member
∫ ( ) ∑ ∫
( )
PORTION | ORIGIN | LIMIT | M | dM/dM' | M(M'=0)
AD | A | 0-3 | M'-6.67X-M'/3 X | 1-1/3 X | -6.67X
DB | B | 0-2 | -10X | 0 | -10X