## Slide 1: Highway Planning & Design Lecture - 2
Designed and presented
By
Asst. Prof. Dr. Raquim Nihad Zehawi

## Slide 2
Highway Design Standards
The first step in the design of any highway is the selection of the appropriate set of geometric design standards
There is no single set of geometric standards can be used for all highways
The characteristics of the highway should be considered in selecting the geometric design standards
1- Design Hourly Volume
2- Design Speed
3- Design Vehicle
5- Cross-Section Elements
4- Maximum Highway Grades
Width of Travel Lanes
Shoulders
Medians
Roadside and Median Barriers
Curbs and Gutters
Guard Rails
Sidewalks
Cross Slopes
Right of Way

## Slide 3
1- Design Hourly Volume
The design hourly volume (DHV) is the projected hourly volume (up to the design year) that is used for design
It is usually taken as a percentage of the expected ADT on the highway
The average daily traffic is estimated for the future depending on many factors that influence its growth
The future average daily traffic is calculated:
Projected “Future” (AADT)
Traffic projection factor
If r=6% , x= 2 years , l =20 years T.P.F = 3.6
F= future traffic (AADT)
C= current traffic
r = annual rate of increase of traffic
x= years of construction
l : is the average design life (years)
It is referred to as “Annual Average Daily Traffic” (AADT) for it is the:
annual traffic averaged on a daily basis in both directions

## Slide 4
The 30th-highest hourly volume is usually selected as the DHV
The 30th-highest hourly volume for rural highways is usually between 12 and 18 percent of the ADT
The DHV is typically between the 10th and 50th highest volume hour of the year
K-factor is the ratio between DHV and AADT

## Slide 5
Directional distribution factor (D) is the Factor reflecting the proportion of peak-hour traffic traveling in the peak direction
Directional design-hour volume (DDHV) is calculated

## Slide 6
2- Design Speed
Design speed is defined as a selected speed to determine the various geometric features of the roadway.
It depends on:
the functional classification of the highway
the topography of the area
the land use of the adjacent area
For highway design, topography is:
Level terrain: relatively flat. Horizontal and vertical sight distances are long
Rolling terrain: has natural, occasional steep slopes that often restrict the normal vertical and horizontal alignments.
Mountainous terrain: has sudden changes in ground elevation in both the longitudinal and transverse directions

## Slide 7
Design speeds range from 20 mi/h to 70 mi/h, with intermediate values of 5 mi/h increments
freeways are designed for 60 to 70 mi/h
design speeds for other arterial roads range from 30 mi/h to 60 mi/h

## Slide 8
A design vehicle is selected to represent all vehicles on the highway
3- Design Vehicle
Its weight, dimensions, and operating characteristics are used to establish the design standards of the highway
The design vehicle is: The largest vehicle that is likely to use the highway with considerable frequency
It is used to determine critical design features such as radii at intersections and turning roadways as well as highway grades

## Slide 9
4- Maximum Highway Grades
The selection of maximum grades for a highway depends on the design speed and the design vehicle
Steep grades affect the performance of heavy vehicles as well as that of of passenger cars
grades of 4 to 5 percent have little or no effect on passenger cars
Maximum grades have been established based on the operating characteristics of the design vehicle
Minimum grades depend on the drainage conditions of the highway
Zero percent grades may be used on uncurbed pavements with adequate cross slopes
Longitudinal grade should be provided, when pavements are curbed
It is customary to use a minimum of 0.5 - 3 percent in such cases

## Slide 12
5- Cross-Section Elements
The principal elements of a highway cross section
The marginal elements of a highway cross section
1- travel lanes
2- shoulders
3- medians
1- barriers
2- curbs and gutters
3- guard rails
4- sidewalks
6- side slopes
5- cross Slopes
7- right of way

## Slide 14
1- Width of Travel Lanes
Travel lane widths usually vary from 9 to 12 ft. Most arterials have 12-ft travel lanes
The capacity of a highway decreases significantly as the lane width is reduced from 12 ft,
2- Shoulders
The shoulder is always contiguous with the traveled lane so as to provide an area along the highway for vehicles to stop when necessary
Shoulder width range from 2 ft on minor roads to 12 ft on major arterials
Shoulders are also used to laterally support the pavement structure
The shoulder width is known as either graded or usable
shoulder width is measured from the edge of the pavement to the intersection of the shoulder slope and the plane of the side slope
Recommended slopes are 2 to 6 percent for bituminous and concrete-surfaced shoulders, and 4 to 6 percent for gravel or crushed-rock shoulders

## Slide 15
3- medians
It is the section of a divided highway that separates the lanes in opposing directions.
The width of a median is the distance between the edges of the inside lanes
Median widths vary from a minimum of 4 to 80 ft or more
The functions of a median include:
• Providing a recovery area for out-of-control vehicles
• Separating opposing traffic
• Providing stopping areas during emergencies
• Providing storage areas for left-turning and U-turning vehicles
• Providing refuge for pedestrians
• Reducing the effect of headlight glare
• Providing temporary lanes and cross-overs during maintenance operations

## Slide 16
1- barriers
The marginal elements of a highway cross section
median barrier is a longitudinal system used to prevent an errant vehicle from crossing the portion of a divided highway separating the traveled ways for traffic in opposite directions
Roadside barriers protect vehicles from obstacles or slopes on the roadside
They also may be used to shield pedestrians and property from the traffic stream.
2- curbs and gutters
Curbs are raised structures that are used mainly on urban highways to delineate (define) pavement edges and pedestrian walkways
Curbs are also used to: control drainage, improve aesthetics, and reduce right of way
Gutters (drainage ditches) are usually located on the pavement side of a curb to provide the principal drainage facility for the highway
usually have cross slopes of 5 to 8 percent and are 1 to 6 ft wide

## Slide 18
Guard rails are the longitudinal barriers placed on the outside of sharp curves and at sections with high fills. Their main function is to prevent vehicles from leaving the roadway
3- guard rails
installed at embankments higher than 8 ft and when shoulder slopes are greater than 4:1
The weak post system provides for the post to collapse on impact, with the rail deflecting and absorbing the energy due to impact
Sidewalks are usually provided on roads in urban areas (uncommon in rural areas)
4- sidewalks
Generally, sidewalks should be provided when pedestrian traffic is high along main or high-speed roads in either rural or urban areas

## Slide 19
5- cross Slopes
Pavements on straight sections of two-lane and multilane highways without medians are sloped from the middle downward, resulting in a transverse or cross slope
the highest point of the pavement (called the crown) is slightly rounded
Cross slopes on divided highways are provided by either crowning the pavement in each direction, or by sloping the entire pavement in one direction
w
w
w
stright
stright
parabolic
Parabolic shape
Straight line camber
Combination

## Slide 20
The right of way is the total land area acquired for the construction of a highway. The width should be sufficient to accommodate all the elements of the highway cross section, any planned widening of the highway, and public-utility facilities that will be installed along the highway.
7- right of way
6- side slopes
Side slopes are provided on embankments and fills to provide stability for earthworks. They also serve as a safety feature by providing a recovery area for out-of-control vehicles.