## Slide 1: Highway Planning & Design Lecture - 7
Designed and presented
By
Asst. Prof. Dr. Raquim Nihad Zehawi

## Slide 2
HORIZONTAL CURVES
Four types of horizontal curves:
1- Simple - curve with single constant radius.

## Slide 3
2- Compound – two or more
curves in succession, turning in
the same direction.

## Slide 4
3- Reverse – two simple curves with equal radii
turning in opposite directions with a
common tangent.

## Slide 5
4- Spiral – also called transition curves;
placed between tangents and circular
curves or between two adjacent circular
curves having substantially different
radii.

## Slide 6
Horizontal Curve Formulas
It is a measure of the sharpness of the curve
Degree of Curve (D) – angle subtended by 100 ft or meter arc, along horizontal curve
degree of curve can be determined if the radius is known

## Slide 7
Example 7
The intersection angle of a 4° curve is 55°25’, and the PC is located at station 238 + 44.75. Determine the length of the curve, the station of the PT
Solution:
Length of curve
Radius of curve
2- The station at PT = station at PC + L
= 23844.75 + 1385.4 = 252 + 30.17
1- Determine the radius using degree of the curve D = 4°

## Slide 8
Formulas for Simple Curves

## Slide 9
Sight Distance on Horizontal Curves
Stopping Sight Distance
The stopping sight distance is measured along the centerline of the inside lane around the curve
The sight line is a chord of the curve
Since

## Slide 10
A more simplified approach is adopted
If SSD < L
If SSD > L

## Slide 11
If the direct length of the line of sight at a horizontal curve = 30m, the radius to the inside centerline of the curve= 50m. Find the minimum distance an object can be placed from the centerline of the inside lane of the curve without reducing the required SSD.
Example 8
A horizontal curve having R = 240m , design speed= 60km/hr. Determine the minimum distance an object can be placed from the centerline of the inside lane of the curve without reducing the required SSD. Assume a flat road segment, perception- reaction time =2.5 sec, f=0.34.
Example 9
H.W

## Slide 12
TRANSITION CURVE
The purpose of transition curves is to permit the gradual introduction of centrifugal forces
The form of the transition curve should be (spiral) so that the rate of change in radial acceleration (C) is constant
45
o
45
o
cubic parabola
Bernouilli`s lemniscates
spiral
Major axis
The radial acceleration experienced by the vehicle travelling at a given velocity (V )changes from zero on the tangent to (V2/R) when on the circular arc
Types of transition curves
Transition curve provides a convenient space
for super-elevation runoff and widening

## Slide 13
Spiral curve formula
Centripetal Acceleration ()
On circular curve at S.C
On tangent at T.S
Time for such change
Since C is the rate of change in centripetal acceleration
in m
in Km/h
R in m
C in m//s
C = 0.9 – 1.4 for comfort and safety

## Slide 15
SUPERELEVATION
The inclination of the roadway toward the center of the curve is known as superelevation
When a vehicle is moving around a circular curve it endures a centrifugal acceleration
In order to balance the effect of the centrifugal acceleration, the road is inclined toward the center of the curve