## Slide 1: A Lecture on Highway Traffic &Planning
Ass. Prof .Dr. Ali Hussein Hameed

## Slide 2
Transportation is essential for a country’s development and growth. In both the public and private sector
Elements are constantly being added to the world’s highway, rail, airport, and mass transit systems, and new techniques are being applied for operating and maintaining the systems safely and economically.
Many organizations and agencies exist to plan, design, build, operate, and maintain the country’s transportation system.
The speed, cost, and capacity of available transportation have a significant impact on the economic vitality of an area and the ability to make maximum use of its natural resources.
Examination of most developed and industrialized societies indicates that they have been noted for high-quality transportation systems and services.

## Slide 5
The infrastructure required:

## Slide 6
Transportation, the road-building process includes
1. Planning (6 to 24 months)
2. Design (15 to 24 months)
3. Environment (9 to 36 months)
4. Right-of-Way (6 to 21 months)
5. Construction (12 to 36 months)
Thus, total project time can range from 4 to 12 years, depending on the physical characteristics, scope, and community support for the project.

## Slide 7
Transportation Planning
Transportation planning deals with the:
• selection of projects for design and construction.
• defining the problem, gathering and analyzing data, and evaluating various alternative solutions.
• process are forecasts of future traffic; estimates of the impact of the facility on land use, the environment, and the community;
• determination of the benefits and costs that will result if the project is built.
• investigates the physical feasibility of a project and makes comparisons between various alternatives to determine which one will accomplish the task at the lowest cost— consistent with other criteria and constraints.

## Slide 8
Transportation Infrastructure Design
For highway design, the process involves :
• the selection of dimensions for all geometrical features, such as the longitudinal profile, vertical curves and elevations, the highway cross section, pavement widths, shoulders, rights-of-way, drainage ditches, and fencing.
• the pavement and structural requirements for base courses and the concrete or asphalt surface material.
• Highway design also includes bridges and drainage structures as well as provision for traffic control devices, roadside rest areas, and landscaping.
• The highway designer must be proficient in civil engineering subjects (such as soil mechanics, hydraulics, land surveying, pavement design, and structural design), and is concerned primarily with the geometric layout of the road, its cross section, paving materials, roadway thickness, and traffic-control devices.
• Special appurtenances (such as highway bridges and drainage structures) are usually designed by specialists in these areas.

## Slide 9
Highway Construction
- Highway construction involves all aspects of the building process beginning with:
• clearing of the native soil,
• preparation of the surface,
• placement of the pavement material,
• and preparation of the final roadway for use by traffic.
-Advances in construction equipment have made the rapid building of large highway sections possible.
• devices test compaction of soil and base courses,
• Global Positioning Systems (GPS) and Geographic Information Systems (GIS) are used to establish line and grade,
• specialized equipment for handling concrete and bridge work.

## Slide 10
Traffic Operations and Management
- The operation of the nation’s highway system involves the integration of vehicle, driver, and pedestrian characteristics to improve the safety and capacity of streets and highways.
-Among the elements of concern are:
• traffic accident analyses.
• parking, and loading.
• design of terminal facilities.
• traffic signs.
• markings.
• signals.
• speed regulation.
• highway lighting.

## Slide 11
Maintenance Operations and Management
- Highway maintenance involves all the work necessary to ensure that
the highway system is kept in proper working order.
-Maintenance includes:
• replacing worn or damaged signs,
• repairing damaged roadway sections.
• redesign of existing highway sections,
• Economic evaluation of maintenance programs,
• testing of new products.
• maintain an inventory of traffic signs and markings and ensure that
they are in good condition.
• pavement patching and repair,
• to ensure that the roadway pavement is at a desired level of serviceability.

## Slide 12
Traffic studies may be grouped into three main categories:
(1) inventories,
(2) administrative studies,
(3) dynamic studies.
1-Inventories provide a list or graphic display of existing information, such as street widths, parking spaces, transit routes, traffic regulations, and so forth. Some inventories—for example, available parking spaces and traffic regulations—change frequently and therefore require periodic updating; others, such as street widths, do not.
2-Administrative studies use existing engineering records, available in government
agencies and departments. This information is used to prepare an inventory of the relevant
data. Inventories may be recorded in files but are usually recorded in automated
data processing (ADP) systems. Administrative studies include the results of surveys,
which may involve field measurements and/or aerial photography.
3-Dynamic traffic studies involve the collection of data under operational conditions
and include studies of speed, traffic volume, travel time and delay, parking, and
crashes. Since dynamic studies are carried out by the traffic engineer to evaluate current
conditions and develop solutions,

## Slide 13
Factors Bad for Transportation.
• Industry and employment moving from the central city
• Increased suburb-to-suburb commuting
• Migration of the population
• Growth in private vehicle ownership
• Increased diversity in vehicle types such as pickup trucks, and RVs
• High labor costs
• Higher prices of gasoline
Factors Good for Transportation.
• Trends toward higher-density living
• Rule to encourage smart growth
• Location of mega-centers in suburbs
• Need for airport access
• Increased number of seniors for transit

## Slide 14: Demand and supply with cost delays occur and the travel time increases. Since “time is money,” the increased time has been converted to $/mi.

## Slide 15: The four main components of the highway mode of transportation are :
Drivers’ Characteristics
Pedestrian Characteristics
Vehicle Characteristics
Road Characteristics

## Slide 16
Driver Characteristics :The Human Response Process
Visual Reception
The principal characteristics of the eye are visual acuity, peripheral vision, color vision, glare vision and recovery, and depth perception.
2- Visual Acuity. Visual acuity is the ability to see fine details of an object. the optimal time required for identification of an object with no relative movement is between 0.5 and 1.0 seconds.
3-Peripheral Vision. Age also influences peripheral vision. For instance, at about age 60, a significant change occurs in a
person’s peripheral vision.
4-Color Vision. Combinations of black and white and black and yellow have been shown to be those to which the eye is most sensitive.
5-Glare Vision and Recovery. Studies have shown that this time is about 3 seconds when moving from dark to light and can be 6 seconds or more when moving from light to dark. Glare vision is of great importance during night driving; it contributes to the problem of serving older people, who see much more poorly at night. This phenomenon should be taken into account in the design and location of street lighting so that glare effects are reduced to a minimum.
6-Depth Perception. Depth perception affects the ability of a person to estimate speed and distance. It is particularly important on two-lane highways during passing maneuvers,

## Slide 17
Older Drivers’ Characteristics This group also suffers from narrower visual fields, greater sensitivity to glare, higher reaction times, and reduced muscle strength, which may result in the older driver having a higher crash risk.
Pedestrian Characteristics relevant to traffic and highway engineering practice include those of the driver, For example, the design of an all-red phase, which permits pedestrians to cross an intersection with heavy traffic, requires knowledge of the walking speeds of pedestrians. Observations of pedestrian movements have indicated that walking speeds vary between 3.0 and 8.0 ft /sec. Significant differences have also been observed between male and female walking speeds.
Bicyclists and Bicycles Characteristics
Three classes of bicyclists (A, B, and C) have been identified in the Guide for the Development of Bicycle Facilities by AASHTO ,the minimum design speed for bicycles on level terrain is 20 mi/h.

## Slide 18: Perception-Reaction Process
The process through which a driver, cyclist, or pedestrian evaluates and reacts to a stimulus can be divided into four sub processes:
Perception: the driver sees a control device, warning sign, or object on the road
2. Identification: the driver identifies the object or control device and thus understands
the stimulus
3. Emotion: the driver decides what action to take in response to the stimulus; for example, to step on the brake pedal, to pass, to swerve, or to change lanes
4. Reaction or volition: the driver actually executes the action decided on during the emotion sub-process.
The American Association of State Highway and Transportation Officials (AASHTO) stipulate 2.5 seconds for stopping-sight distances. This
encompasses the decision times for about 90 percent of drivers under most highway
conditions. Note, however, that a reaction time of 2.5 second may not be adequate.

## Slide 20: Vehicle Characteristics