## Slide 1: Traffic Engineering
University of Diyala
College of Engineering
Civil Engineering Department

## Slide 2
Traffic Intersections
An Intersection is the general area where two or more highways join or cross each other, at same level or different level.
There are three classes of intersections:
1-Intersection at grade

## Slide 3
2-Grade separations without ramps
3-Interchange.

## Slide 4
Driver and vehicular characteristics
Driver: (age, gentle, driving skill, experience)
Vehicle: (size, speed, acceleration/ deceleration)
Sight distance requirement
Traffic volume and pedestrian movement
Approaching speed and angle.
Factors of Intersection Design

## Slide 5
Characteristics \\ Maneuvers:

## Slide 6
Characteristics \\ Maneuvers:

## Slide 7
Characteristics \\ Maneuvers:

## Slide 8
Characteristics \\ Conflict Points:
16 Crossing Points
8 Diverging Points
8 Merging Points
It is potential accident spots that occur on vehicle paths at diverging, merging, and cross location.

## Slide 9
Characteristics \\ Conflict Points:
The conflict points for 4-legs Intersection & 3- legs Intersection & Roundabout

## Slide 10
Types \\ 3- Legs Intersection

## Slide 11
Types \\ 4- Legs Intersection

## Slide 12
Types \\ Multi- Legs Intersection

## Slide 13
Roundabout

## Slide 14
Questions - ?

## Slide 15
Categories of Intersection
1- Priority Intersection:
Occur where one of the intersecting roads is given definite priority over the other.
(Two way stop controlled intersection- TWSC)

## Slide 16
Categories of Intersection
2- Uncontrolled intersection:
Are the most common type of intersection usually occurs where the intersecting roads are relatively equal importance and found in areas where there is not much traffic.

## Slide 17
Categories of Intersection
3- Space sharing intersection:
Are intended to permit fully equally priority and to permit continuous movement for all intersecting vehicle flows; example would be rotaries and other weaving areas.

## Slide 18
4- Time Sharing Intersection:
Are those at which alternative flows are given the left of way at different point in time. This type of intersection is controlled by traffic signal or by police officer.
Categories of Intersection

## Slide 19
Design principles of Intersection
1- Reduction of the Area of Conflict:
The impact area is decreased when Channelization is provided, and hence the probability of conflicts is also reduced.

## Slide 20
Design principles of Intersection
2- Merging traffic streams at small angles:
Merging at small angles permits the flow of traffic streams with minimum speed differentials. Hence, the gap acceptance time is also small in such cases.

## Slide 21
Design principles of Intersection
3- Reduction of the speed of incoming traffic by bending or funneling its path:

## Slide 22
Design principles of Intersection
4- Protection for turning vehicles/crossing conflicting traffic streams:
Provision of a refuge area between the two opposing streams allows the driver of a crossing vehicle to select a safe gap in one stream at a time and also provides a safer crossing maneuver.

## Slide 23
Design principles of Intersection
5- Discourage prohibited turns by island placement and shape:
Undesirable and prohibited turns can be discouraged by the proper selection of shape and location of the islands.

## Slide 24
Design principles of Intersection
6- Providing locations of traffic control devices:
Channelization may provide locations for the installation of essential traffic control devices, such as stop and directional signs, signals etc.

## Slide 25
Questions - ?

## Slide 26
Grade- Separated Intersections

## Slide 27
Diamond

## Slide 28
Partial Cloverleaf

## Slide 29
Rotary

## Slide 30
Interchange

## Slide 31
Trumpt Interchange

## Slide 32
Three Leg Directional Interchange

## Slide 33
Cloverleaf Interchange

## Slide 34
All Directional 4-Legs

## Slide 35
Questions - ?