## Slide 1
Lecture 2: Introduction to Basic Aerodynamics

## Slide 2: READING AND HOMEWORK ASSIGNMENTS
Reading: Introduction to Flight, 7th Edition, by John D. Anderson, Jr.
  Chapter 4

## Slide 3: REVIEW OF BASIC DEFINITIONS
Streamline
  Set of points that form a line that is everywhere tangent to local velocity vector
  No flow across streamlines
  For a steady flow, moving fluid element traces out a fixed path in space
Stream tube
  A set of streamlines that intersect a closed loop in space
Steady Flow: A flow that does not fluctuate with time
Unsteady Flow: A flow that varies with time
Equation of State for a Perfect Gas ,applies at a point
  Ideal Gas Law: p = rRT or pv = RT (v = 1/r)
  R universal = 8,314 J/kg mole K
    R for air = 8,314 / 28.96 = 287 J/kg K (or 1,716 ft lb / slug R)

## Slide 4: EXAMPLE: STREAMLINES AND STREAM TUBES IN STEADY FLOW
Streamlines
Stagnation
Point

## Slide 5: WATER STREAMLINES ON F-16 MODEL
http://www.aerolab.com/water.html

## Slide 6: TYPES OF FLOWS: FRICTION VS. NO-FRICTION
Viscous: Flows with friction
  All real flows are viscous
  Inviscid flow is a useful idealization
  By neglecting friction analysis of flow is usually much easier!
Inviscid: Flows with no friction
Flow very close to surface of airfoil is
Influenced by friction and is viscous
(boundary layer flow)
Stall (separation) is a viscous phenomena
Flow away from airfoil is not influenced
by friction and is wholly inviscid

## Slide 7: LAMINAR VERSUS TURBULENT FLOW
Two types of viscous flows
  Laminar: streamlines are smooth and regular and a fluid element moves smoothly along a streamline
  Turbulent: streamlines break up and fluid elements move in a random, irregular, and chaotic fashion

## Slide 8: FRCTION EXAMPLE: AIRFOIL STALL
Key to understanding: Friction causes flow separation within boundary layer
  Boundary layers are either laminar or turbulent
  All laminar B.L. → turbulent B.L.
  Turbulent B.L. ‘fuller or fatter’ than laminar B.L., more resistant to separation
Separation creates another form of drag called pressure drag
  Dramatic loss of lift and increase in drag

## Slide 9: AUTOMOTIVE EXAMPLES
http://exa.com/automotive.html

## Slide 10: CYCLING AERODYNAMICS
Bike and rider aerodynamics
Peloton vs. single rider

## Slide 11: BOBSLED AERODYNAMICS

## Slide 12: TYPES OF FLOWS: COMPRESSIBLE VS. INCOMPRESSIBLE
Compressible: Density of fluid elements may change from point to point
  All real flows are compressible
  Important for gases (rarely important for liquids)
  Most important at high speeds
Incompressible: Density of fluid elements is always constant
General Rule of Thumb:
  If flow speed is less than about 100 m/s (or less than 225 MPH) → flow can be considered incompressible
  or
  If flow is less than Mach 0.3, flow can be considered incompressible
    Mach number, M: ratio of local velocity to local speed of sound, V/a

## Slide 13: KEY TERMS: CAN YOU DEFINE THEM?
Streamline
Stream tube
Steady flow
Unsteady flow
Viscid flow
Inviscid flow
Compressible flow
Incompressible flow
Laminar flow
Turbulent flow

## Slide 14: BASIC AERODYNAMICS

## Slide 15: EXAMPLES OF WHAT WE WILL BE ABLE TO DO
Wind Tunnels
Air Speed
Supersonic Flow

## Slide 16: CONSERVATION OF MASS
Stream tube
As long as flow is steady, mass that flows through cross section at point 1 (at entrance) must be same as mass that flows through point 2 (at exit)
Flow cannot enter or leave any other way (definition of a stream tube)
Also applies to solid surfaces, pipe, funnel, wind tunnels, airplane engine
“What goes in one side must come out the other side”
A1
A2
V1
V2
Funnel wall

## Slide 17: CONSERVATION OF MASS (4.1)
Stream tube
Consider all fluid elements in plane A1
During time dt, elements have moved V1dt and swept out volume A1V1dt
Mass of fluid swept through A1 during dt: dm=r1(A1V1dt)
A1: cross-sectional area
of stream tube at 1
V1: flow velocity
Normal (perpendicular) to A1

## Slide 18: SIMPLE EXAMPLE
p1=1.2x105 N/m2
T1=330 K
V1=10 m/s
A1= 5m2
p2=?
T2=?
V2=30 m/s
A2=?
IF flow speed < 100 m/s assume flow is incompressible (r1=r2)
Given air flow through converging nozzle, what is exit area, A2?
Conservation of mass could also give velocity, V2, if A2 was known
Conservation of mass tells us nothing about p2, T2, etc.