## Slide 1: Thermodynamics
University of Diyala
College of Engineering
Mechanical Engineering Department
Class: Second Year
Second Semester
ME210 : Thermodynamics
ME210- CHAPTER 7
ENTROPY
By
Lecturer
Sameer D. Ali
Layth Abed Hassnawe

## Slide 2: Objectives
2
Apply the second law of thermodynamics to processes.
Define a new property called entropy to quantify the second- law effects.
Establish the increase of entropy principle.
Calculate the entropy changes that take place during processes for pure substances, incompressible substances, and ideal gases.
Examine a special class of idealized processes, called isentropic processes, and develop the property relations for these processes.
Derive the reversible steady-flow work relations.
Develop the isentropic efficiencies for various steady-flow devices.
Introduce and apply the entropy balance to various systems.
Thermodynamics-CH7

## Slide 3: ENTROPY
3
The system considered in the development of the Clausius inequality.
Clasius inequality
The equality in the Clausius inequality holds for totally or just internally reversible cycles and the inequality for the irreversible ones.
Formal definition of entropy

## Slide 4: A quantity whose cyclic
integral is zero (i.e., a property like volume)
Entropy is an extensive property of a system.
The net change in volume (a property) during
a cycle is always zero.
The entropy change between two specified states is the same whether the process is reversible or irreversible.
A Special Case: Internally Reversible Isothermal Heat Transfer Processes
This equation is particularly useful for determining
the entropy changes of thermal energy reservoirs.
4

## Slide 5: THE INCREASE OF ENTROPY PRINCIPLE
The equality holds for an internally reversible process and the inequality for an irreversible process.
A cycle composed of a reversible and an irreversible process.
Some entropy is generated or created during an irreversible process, and this generation is due entirely to the presence of irreversibilities.
The entropy generation Sgen is always a positive quantity or zero.
Can the entropy of a system during a process decrease?
5

## Slide 6
The entropy change of an isolated system is the sum of the entropy changes of its components, and is never less than zero.
A system and its surroundings form an isolated system.
The increase of entropy principle
Thermodynamics-CH7

## Slide 7: Some Remarks about Entropy
The entropy change of a system can be negative, but the entropy generation cannot.
Processes can occur in a certain direction only, not in any direction. A process must proceed in the direction that complies with the increase of entropy principle, that is, Sgen ≥ 0. A process that violates this principle is impossible.
Entropy is a nonconserved property, and there is no such thing as the conservation of entropy principle. Entropy is conserved during the idealized reversible processes only and increases during all actual processes.
The performance of engineering systems is degraded by the presence of irreversibilities, and entropy generation is a measure of the magnitudes of the irreversibilities during that process. It is also used to establish criteria for the performance of engineering devices.
Thermodynamics-CH7

## Slide 8: ENTROPY CHANGE OF PURE SUBSTANCES
8
The entropy of a pure substance is determined from the tables (like other properties).
Schematic of the T-s diagram for water.
Entropy is a property, and thus the value of entropy of a system is fixed once the state of the system is fixed.
Entropy change

## Slide 9: ISENTROPIC PROCESSES
9
During an internally reversible, adiabatic (isentropic) process, the entropy remains constant.
A process during which the entropy remains constant is called an isentropic process.
The isentropic process appears as a
vertical line segment on a T-s diagram.
Thermodynamics-CH7

## Slide 10: PROPERTY DIAGRAMS INVOLVING ENTROPY
10
On a T-S diagram, the area under the process curve represents the heat transfer for internally reversible processes.
For adiabatic steady-flow devices, the vertical distance ∆h on an h-s diagram is a measure of work, and the horizontal distance ∆s is a measure of irreversibilities.
Mollier diagram: The h-s diagram

## Slide 11: WHAT IS ENTROPY?
The level of molecular disorder (entropy) of a substance increases as
A pure crystalline substance at absolute zero temperature is in perfect order, and its entropy is zero (the third law of thermodynamics).
Disorganized energy does not create much useful effect, no matter how large it is.
Boltzmann relation
it melts or evaporates.
11

## Slide 12
In the absence of friction, raising a weight by a rotating shaft does not create any disorder (entropy), and thus energy is not degraded during this process.
The paddle-wheel work done on a gas increases the level of disorder (entropy) of the gas, and thus energy is degraded
during this process.
During a heat transfer process, the net entropy increases. (The increase in the entropy of the cold body more than offsets the decrease in the entropy of
the hot body.)
12

## Slide 13
FIGURE 7-27
As i n mechanical systems. fri ction in the workplace is bou nd to generate entropy and redu ce performan ce.
13

## Slide 14: THE T ds RELATIONS
The T ds relations are valid for both reversible and irreversible processes and for both closed and open systems.
the first T ds, or Gibbs equation
the second T ds equation
Differential changes in entropy in terms of other properties
Thermodynamics-CH 7

## Slide 15: ENTROPY CHANGE OF LIQUIDS AND SOLIDS
Since
for liquids and solids
Liquids and solids can be approximated as incompressible substances since their specific volumes remain nearly constant during a process.
For an isentropic process of an incompressible substance
Thermodynamics-CH 7

## Slide 16: THE ENTROPY CHANGE OF IDEAL GASES
From the first T ds relation From the second T ds relation
A broadcast from channel IG.
Thermodynamics-CH 7

## Slide 17: Constant Specific Heats (Approximate Analysis)
Under the constant-specific- heat assumption, the specific heat is assumed to be constant at some average value.
Entropy change of an ideal gas on a unit–mole basis
Thermodynamics-CH 7

## Slide 18: Variable Specific Heats (Exact Analysis)
We choose absolute zero as the reference temperature and define a function s° as
The entropy of an ideal gas depends on both T and P. The function so represents only the temperature-dependent part of entropy.
On a unit–mole basis
On a unit–mass basis
Thermodynamics-CH 7

## Slide 19: Isentropic Processes of Ideal Gases
Constant Specific Heats (Approximate Analysis)
Setting this eq. equal to
zero, we get
The isentropic relations of ideal gases are valid for the isentropic processes of ideal gases only.
Thermodynamics-CH 7

## Slide 20: Isentropic Processes of Ideal Gases
21
Variable Specific Heats (Exact Analysis)
Relative Pressure and Relative Specific Volume
T/Pr is the relative specific volume vr.
exp(s°/R) is the relative pressure Pr.
The use of Pr data for calculating the final temperature during an isentropic
process.
The use of vr data for calculating the final temperature during an isentropic process

## Slide 21: REVERSIBLE STEADY-FLOW WORK
Reversible work relations for steady- flow and closed systems.
The larger the specific volume, the greater the work produced (or consumed) by a steady-flow
When kinetic and potential energies are negligible
For the steady flow of a liquid through a device that involves no work interactions (such as a pipe section), the work term is zero (Bernoulli equation):
device.
22

## Slide 22: Proof that Steady-Flow Devices Deliver the Most and Consume the Least Work when the Process Is Reversible
A reversible turbine delivers more work than an irreversible one if both operate between the same end states.
Taking heat input and work output positive:
Actual
Reversible
Work-producing devices such as turbines deliver more work, and work- consuming devices such as pumps and compressors require less work
when they operate reversibly.

## Slide 23: MINIMIZING THE COMPRESSOR WORK
P-v diagrams of isentropic, polytropic, and isothermal compression processes between the same pressure limits.
When kinetic and potential energies are negligible
Isentropic (Pvk = constant):
Polytropic (Pvn = constant):
Isothermal (Pv = constant):
The adiabatic compression (Pvk = constant) requires the maximum work and the isothermal compression (T = constant) requires the minimum. Why?

## Slide 24: Multistage Compression with Intercooling
The gas is compressed in stages and cooled between each stage by passing it through a heat exchanger called an intercooler.
P-v and T-s diagrams for a two- stage steady-flow compression
process.
To minimize compression work during two-stage compression, the pressure ratio across each stage of the compressor must be the same.

## Slide 25: ISENTROPIC EFFICIENCIES OF STEADY- FLOW DEVICES
26
The isentropic process involves no irreversibilities and serves as the ideal process for adiabatic devices.
Isentropic Efficiency of Turbines
The h-s diagram for the actual and isentropic processes of an adiabatic turbine.

## Slide 26: Isentropic Efficiencies of Compressors and Pumps
27
The h-s diagram of the actual and
isentropic processes of an
adiabatic compressor.
Compressors
are sometimes intentionally cooled to minimize the work input.
Isothermal efficiency
When kinetic and potential energies are negligible
For a pump
Can you use isentropic efficiency for a non-adiabatic compressor?
Can you use isothermal efficiency for
an adiabatic compressor?

## Slide 27: Isentropic Efficiency of Nozzles
The h-s diagram of the actual and
isentropic processes of an adiabatic nozzle.
If the inlet velocity of the fluid is small relative to the exit velocity, the energy balance is
Then,
A substance leaves actual nozzles at a higher temperature (thus a lower velocity) as a result of friction.

## Slide 28: ENTROPY BALANCE
Energy and entropy balances for a system.
Entropy Change of a System, ∆Ssystem
When the properties of the system are not uniform

## Slide 29: Mechanisms of Entropy Transfer, Sin and Sout
30
1 Heat Transfer
Entropy transfer by heat transfer:
Entropy transfer by work:
Heat transfer is always accompanied by entropy transfer in the amount of Q/T, where T is the boundary temperature.
No entropy accompanies work as it crosses the system boundary. But entropy may be generated within the system as work is dissipated into a less useful form of energy.

## Slide 30: 2 Mass Flow
31
Entropy transfer by mass:
When the properties of the mass change during the process
Mass contains entropy as well as energy, and thus mass flow into or out of system is always accompanied by energy and entropy transfer.
Thermodynamics-CH7

## Slide 31: Entropy Generation, Sgen
32
Mechanisms of entropy transfer for a
general system.
Entropy generation outside system boundaries can be accounted for by writing an entropy balance on an extended system that includes the system and its immediate surroundings.
Thermodynamics-CH7

## Slide 32: Closed Systems
33
The entropy change of a closed system during a process is equal to the sum of the net entropy transferred through the system boundary by heat transfer and the entropy generated within the system boundaries.
Thermodynamics-CH7

## Slide 33: Control Volumes
34
The entropy of a substance always increases (or remains constant in the case of a reversible process) as it flows through a single-stream, adiabatic, steady- flow device.
The entropy of a control volume changes as a result of mass flow as well as heat transfer.

## Slide 34: EXAMPLES
35
Entropy balance for heat transfer through a wall
Entropy balance for a throttling process
Thermodynamics-CH7

## Slide 35: Entropy Generated when a Hot Block Is Dropped in a Lake
36
or
Entropy Generation in a Heat Exchanger

## Slide 36: Entropy generation associated with a heat transfer process
37
Graphical representation of entropy generation during a heat transfer process
through a finite temperature difference.

## Slide 37: Summary
38
Entropy
The increase of entropy principle
Entropy change of pure substances
Isentropic processes
Property diagrams involving entropy
What is entropy?
The T ds relations
Entropy change of liquids and solids
The entropy change of ideal gases
Reversible steady-flow work
Minimizing the compressor work
Isentropic efficiencies of steady-flow devices
Entropy balance
Thermodynamics-CH7