## Slide 1
جامعة ديالى / كلية الهندسة
8085 Microprocessor
قسم الهندسة الإلكترونية
2018
Lecture 1
المدرس إياد قيس عبد الكريم

## Slide 2
Introduction
2018
The microprocessor plays a significant role in the everyday functioning of industrialized societies.
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية
The microprocessor communicates and oper­ates in the binary numbers 0 and 1, called bits.
Each microprocessor has a fixed set of instructions in the form of binary patterns called a machine language..
The microproces­sor can be embedded in a larger system, can be a standalone unit controlling processes, or it can function as the CPU of a computer called a micro­computer.

## Slide 3
Organization of a Microprocessor-Based System
2018
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية
Timing
And
Control Unit
Register
Array
ALU
I / O
Input / Output
ROM
Memory Unit
RWM

## Slide 4
Arithmetic/Logic Unit
2018
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية
This is the area of the microprocessor where various computing functioning) function are performed on data. The ALU unit performs such arithmetic operations as sing 8-bit addition and subtraction, and such logic operations as AND, OR, and exclusive OR. Results are stored either in registers or in memory.

## Slide 5
Register Array
2018
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية
This area of the microprocessor consists of various registers. These registers are primarily used to store data temporarily during the execution of a program. Some of the registers are accessible to the user through instructions.

## Slide 6
Timing and control unit
2018
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية
This unit synchronizes all the microprocessor operations with the clock and generate the control signals necessary for communication between the microprocessor and peripheral the control signals are similar to a sync pulse in an oscilloscope. The RD and WR signals are sync pulses indicating the availability of data on the data bus.

## Slide 7
2018
شكراً لإصغائكم ...
أسئلة ؟