## Slide 1
جامعة ديالى / كلية الهندسة
8085 Microprocessor
قسم الهندسة الإلكترونية
2018
Lecture 3
المدرس إياد قيس عبد الكريم

## Slide 2
Memory
2018
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية
Memory
What is memory? It is a circuit that can store bits high or low,
generally voltage levels or capacitive charges representing 1 and 0.
A Flip-flop or a latch is a basic element of memory
. To write or store a bit in the latch,
we need an input data bit Din and an enable signal (EN).

## Slide 3
2018
As shown in Figure. In this latch, the stored bit always available on the output of it to avoid unintentional change in the input and control the availability of the output, we can use two tri-state buffers on the latch, as shown in Figure . Now we can write into the latch by enabling the input buffer and read from it by enabling the output buffer. Figure shows the Write signal as WR and Read signal as RD; these are active low signals indicated by the bar. This latch, which can store one binary bit is called a memory cell.
.
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية

## Slide 4
D
Din
Q
Qout
EN
EN
RD
D
Din
Q
Qout
EN
EN
WR

## Slide 5
2018
Figure (8-A) shows four such cells or latches grouped together, this is a register, which has four input lines and four output lines and can store four bits: thus the size of the memory word is four bits. The size of this register is specified either as 4-bit or 1 X 4-bit, which indicates one register with four cells or four I/O lines. Figures (8-B) and (8-C) show simplified block diagrams of the 4-bit register.
جامعة ديالى / كلية الهندسة
قسم الهندسة الإلكترونية

## Slide 7
2018
شكراً لإصغائكم ...
أسئلة ؟