## Slide 1
جامعة ديالى
كلية الهندسة
قسم الهندسة الكيمياوية
Unit Operations
Lecturer
Dr Salah N. Farhan

## Slide 2
Membrane Separation Processes

## Slide 3
What is Membrane?
Membranes are materials which have voids in them, letting some molecules pass more conveniently than some other molecules.
A semi-permeable membrane is a VERY THIN film that allows some types of matter to pass through while leaving others behind

## Slide 4
Membrane separation processes are used for separation that is difficult to be carried outin a classical separation such as sedimentation, filtration, or centrifuge. Typical cases are:
Finely dispersed solids
Solids which have a density close to that of the liquid phase
Solids which have gelatinous nature
Low molecular weight and non-volatile organics
Pharmaceuticals
Dissolved salts
Sensitive biological materials
Membrane separation is a natural phenomenon to separate active materials biologically.

## Slide 5
Membranes are materials which have voids in them letting some molecules pass more conveniently than some other.
How separation occurs?
Difference in permeabilities through a membrane:
Difference in size,
Affinity to the membrane,
Charge, etc.
Driving forces
Pressure difference,
Concentration difference
Voltage difference, etc

## Slide 6
Advantages of Membrane Separation
Continuous separation
Low energy requirement
Meet variousseparation demands
Disadvantages
Fouling
Short service periods

## Slide 7
Classification of Membrane Processes
Industrial membrane processes may be classified according to the size range of materials which they are to separate and the driving force used in separation. The most common pressure driven membrane separation processes classified according to pore size are:
Microfiltration (MF) – filtration of suspensions with micro scale particles
Ultrafiltration (UF) - paint plants in the car industry, dairy industry
Nanofiltration (NF) - pharmaceutical processing and water treatment
Reverse osmosis (RO) – desalination of brackish and sea water, dairy industry See Table 8.1 for the classification of membrane processes

## Slide 8
Membrane Materials
Cellulosic membrane
Polyamide membrane
Polysulphone membrane
Polycarbonate membrane
Reverse Osmosis
Only remove some suspended materials larger than 1 micron
The process eliminates the dissolved solids, bacteria, viruses and other germs contained in the water
Only water molecules allowed to pass via very big pressure
Asymmetric type membranes (decrease the driving pressure of the flux)
Almost allmembranes are made polymers, cellulosic acetate and matic polyamide types rated at 96%-99+% NaCl rejection

## Slide 9
Extensive Applications:
Potable water from sea or brackish water
Ultrapure water for food processing and electronic industries
Pharmaceutical grade water
Water for chemical, pulp & paper industry
Waste treatment
Future Directions:
  Municipal and industrial waste treatment
  Process water for boilers
  De-watering of feed streams
  Processing high temperature feed- streams

## Slide 10
Microfiltration
Largest pores
A sterile filtration with pores 0.1-10.0 microns
Micro-organisms cannot pass through them
Operated at low pressure differences
Used to filter particles.
May or may not be asymmetric

## Slide 11
Wide array of applications:
  Sterile water for pharmaceutical industry
  Food & beverages
  Chemical industry
  Microelectronics industry
  Fermentation
  Laboratory/analytical uses
Applications in the near future:
  Biotechnology (concentration of biomass)
  Diatomaceous earth displacement (Diatomaceous earth is a filter media used for the same purposes but needs periodic replacement)
  Non-sewage waste treatment (removing intractable particles in oily fluids)
  Paints (separating solvents from pigments)

## Slide 12
Ultrafiltration
To separate a solution; mixture of desirable and undesirable components
Has smaller pores than microfiltration membranes
Driving force→pressure differential (2-10 bars to 25-30 bars)
Used to separate species with pore sizes 10-1000 Å(10-3-0.1 microns)
Can be obtained down to a molecular weight cutoff (MWCO) level of 1000 and up to as high as 1 000 000.
Aasymmetric; the pores are small
Wide range of applications :
  Oil emulsion waste treatment
  Treatment of whey in dairy industries
  Concentration of biological macromolecules
  Concentration of textile sizing
  Concentration of heat sensitive proteins for food additives

## Slide 13
Wide range of applications in the near future:
  Ultrafiltration of milk
Bioprocessing (separation and concentration of biologically active components)
  Protein harvesting (production of protein on field)
  Refining of oils
Nanofiltration
Less pore sizes than ultrafiltration membranes
The mass transfer mechanismis diffusion& separate small molecules from the solution (asymmetric)
Cellulosic acetate and aromatic polyamide type membranes (salt rejections; 95% for divalent salts to 40% for monovalent salts)
Can typically operate at higher recoveries; conserving total water usage due to a lower concentrate stream flow rate (advantage over reverse osmosis)
Not effective on small molecular weight organics (e.g.methanol)

## Slide 14
Typical applications:
Desalination of food, dairy and beverage products or byproducts
Desalination of whey, UF permeate or retentate as required
Desalination of dyes and optical brighteners
Purification of spent clean-in-place (CIP) chemicals
Color reduction or manipulation of food products
Concentration of food, dairy and beverage products or byproducts
Membrane Process Characteristics

## Slide 15
General Membrane Equation
The general membrane equation takes the form:
Where J is the membrane flux, expressed as volumetric rate per unit area
is the pressure difference applied across the membrane (trans membrane pressure).
Is the difference in osmotic pressure across the membrane.
Rm is the resistance of the membrane.
Rc is the resistance of layers deposited on the membrane, the filter cake and gel foulants.

## Slide 16
If the membrane is only exposed to pure solvent, say water, then the above equation reduces to
It is clear that the trans membrane pressure must exceed the osmotic pressure for flow to occur.
The separation of a solute by a membrane gives rise to an increased concentration of that solute at the membrane surface, an effect known as concentration polarization.

## Slide 17
Cross-Flow Microfiltration
The classical filtration processes are limited to concentrating particles above 5 μm.
For solutions with particles of less than 5 μm down to 0.1 μm, the suitable separation process is the microfiltration. It is necessary that the particles concentration is small in order not to clog the micro filter.

## Slide 18
A flow diagram of a simple cross-flow system is shown in the figure below

## Slide 19
The feed is pumped at a velocity in the range 1–8 m/s parallel to the face of the membrane and with a pressure difference of 1 – 5kPa/m2 across the membrane. The liquid permeates through the membrane and the feed emerges in a more concentrated form at the exit of the module. See Fig. 8.5 of flow diagram for a simple cross-flow system and Fig. 8.6 for the variation of permeation flow with time.
For microfiltration accompanied with fouling on the membrane the membrane flux can be written as
Rc now represents the resistance of the cake, which if all filtered particles remain in the cake, may be written as:
Where
r is the specific resistance of the deposit
V is the total volume filtered
Vsis the volume of particles deposited
Cbis the bulk concentration of particles in the feed (particle volume/feed volume) Amis the membrane area.

## Slide 20
where e is the void volume of the cake and ds the mean particle diameter.
Combining the above equations gives
The specific resistance can be expressed as
Solution of the above equation for V at constant pressure gives:
Yielding a straight line on plotting t/V against V