## Slide 1
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE
Chemical Reaction Engineering
By
Dr Salah N. Farhan
Senior lecturer. Chem. Eng. Dept.
College of Engineering
University of Diyala

## Slide 2
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE
Chapter 10: Non Isothermal Reactor

## Slide 34
للشكل اعلاه في حالة التوازن لتفاعل باعث للحرارة ,كلما زادت الحرارة فان سير التفاعلExtent of reaction تقل لذك عند درجة واطئة فان Extent عالية وبالعكس.
وعند اجراء التفاعل في حالة isothermal فان النقطة الموضحة في الشكل اعلاه,نحصل على 0.7 تقريبا.
لكن عند اجراء العمل في ظروف Adiabatic فانه لا توجد اضافة او سحب للحرارة ولدينا تفاعل باعث للحرارة
فان هناك ميل لارتفاع درجة الحرارة لذلك تقل Extent لحدود 0.4 على الخط الموضح في الرسم اعلاه.
لذلك يجب ان يجرى التفاعل باسرع وقت وايضا القلق من ان يحدث تفاعل عكسي.
لذلك في تفاعلات الحرارة الثابتةIsothermal نحصل على تحول عالي باقل درجة حرارة وهذا يعني معدل تفاعل اقل.

## Slide 36: Topics to be covered in this Module
Module 6a (Sections 8.2, 8.3, 8.4, 8.6.1 – Fogler, 4th Edition)
Develop Energy Balance equations for flow reactors.
Enthalpy, Heat Capacity, and Heat of Reaction and relationship between them
Heat transfer rates for CSTR and PFR/PBR
Algorithms for Non-isothermal CSTR and PFR
Module 6b (Sections 8.5 and 8.7)
Equilibrium Conversion (Reversible Reactions) in Reactors
  Conversion attainable during adiabatic operation of endothermic and exothermic reactors
  Increasing Conversion by inter-stage cooling and heating

## Slide 37: Why Do We Need Energy Balance ?
Every reaction proceeds with release or absorption of heat.
The amount of heat released or absorbed depends on
  the nature of reacting system
  the amount of material reacting
  temperature and pressure of reacting system
  and can be calculated from heat of reaction (HRxn)
Most industrial reactors will require heat input or heat removal, hence, we need energy balance.

## Slide 38: Energy Balance for Single Reaction
An exothermic reaction is carried out in an adiabatic plug flow reactor.
How would you calculate the reactor volume required to achieve a certain amount of conversion, X ?
We need to relate X and T ----> Energy Balance Equation

## Slide 39: User-Friendly Design Equations

## Slide 40: User-Friendly Design Equations
We would like to understand how these design equations were developed

## Slide 41: General Form of Energy Balance
Rate of accumulation of the energy within the system
–
+
–
=
Rate of work done by the system on the surroundings
Rate of flow of heat to the system from the surrounding
Rate of energy added to the system by mass flow into the system
Rate of energy leaving the system by mass flow out of the system
Control Volume

## Slide 42: General Form of Energy Balance (for multi component system)
Next, we will evaluate the “W” and “E” terms

## Slide 43: Understanding Work and Energy Terms in the EB equation

## Slide 44: Evaluation of the Work (W) term
Rate of flow work is rate of work to get mass into and out of the system
In a chemically reacting systems, there are usually two types of work that need to be accounted for – (i) Shaft Work (e.g. work done by impellers in a CSTR and batch reactor) and (ii) Flow Work

## Slide 45: Evaluation of the E term
Energy Ei is the sum of internal, kinetic, potential and any other type of energies.
For a majority of reactors, only internal energy is important

## Slide 46: General Form of Energy Balance (for multi component system)

## Slide 47: Energy Balance Equation in terms of Enthalpy
Now,
We now have, Energy Balance Equation in terms of Enthalpy
Substituting appropriate values of Ei and Rate of Work
Next, we will focus on the enthalpy terms

## Slide 48: Here’s what we’ll do with Enthalpy terms
Express Hi in terms of Enthalpy of Formation (Hio ) and Heat Capacity (Cpi)
Express Fi in terms of conversion (for single reaction) or rates of reaction
Define Heat of Reaction (HRxn)
Define  Cp

## Slide 49: Enthalpy Relationships: Single Reaction System
T0
T
Fi in terms of FA0 and X
from stoichiometry
If A is the limiting reactant

## Slide 50: Enthalpy Relationships: Single Reaction System
DHRxn
Next, we will evaluate the different terms of RHS

## Slide 51: Expressing Hi(T) in terms of Hio and Cpi
Therefore,
Hi is available from Chemical Engg handbook
For no phase change
Enthalpy at any given temperature is related to enthalpy at a reference temperature and heat capacity
And,

## Slide 52: Heat of Reaction (DHRxn)
where,
Heat of reaction is defined as:
Enthalpy at any given temperature is:

## Slide 53: General Form of Energy Balance
Energy Balance Equation in terms of Enthalpy
Energy Balance Equation in terms of Conversion

## Slide 54: Heat Transfer (Q) to/from Reactors

## Slide 55: Heat Transfer (Q) to a CSTR
Assuming CSTR temperature,T, is spatially uniform
For high coolant flow rates (Ta1  Ta2=Ta):
Heat transferred between coolant and reactor
(from energy balance on the coolant)

## Slide 56: Heat Transfer (Q) to a PFR
Total heat transferred to the reactor
Heat transfer rate at a given location in a PFR
Remember, in PFR/PBR the concentration and reaction rates vary along the reactor length. Q will likely vary too.
T
Ta
a = heat exchange area/volume

## Slide 57: Non-Isothermal Reactors

## Slide 58: Non-isothermal Flow Reactor
Application-1 Special Case: Adiabatic Reactor with No Shaft Work
T
XEB
If Cp term<<DHRxn
Applying Q = 0 and Ws=0 in the above equation, we get

## Slide 59: Non-isothermal Flow Reactor
Application-2: CSTR with Heat Exchange; no shaft work
Let us see if we can apply these concepts to solve a CSTR problem.
Applying Ws=0 in the above equation, we get

## Slide 60: Class Problem #6
The following liquid-phase reaction is carried out in a CSTR with heat exchange:
The feed stream contains A and B in equimolar ratio. The total molar flow rate is 20 mol/s. The inlet temperature is 325 K, the inlet concentration of A is 1.5 molar, and the ambient temperature in the heat exchanger is 300 K.
Calculate the reactor volume necessary to achieve 80% conversion.
Additional information
U= 80 J/m2 s K
A=2 m2
DHRxn(298) = -10,000 J/mol
CpA = CpB= 100 J/mol K
CpC = 150 J/mol K
E=25,000 J/mol
k298 = 0.014 L/mol-s

## Slide 61: Non-isothermal Flow Reactor
Application-3: PFR with Heat Exchange
Differentiating the Energy Balance equation with respect to V, we get
V
V+DV
T
FA0
T0
FAe
Te

## Slide 62: Non-isothermal Flow Reactor
V
V+DV
Ta
T
a = specific surface area for heat transfer = area/volume
U = overall heat transfer coefficient
Ta = Temperature of heat transfer fluid (outside of the reactor)
The first term on LHS can be written as
Application-3: PFR with Heat Exchange (cont.)
Let us evaluate the differential terms of the EB equation

## Slide 63: Non-isothermal Flow Reactor
Application-3: PFR with Heat Exchange (cont.)
Let us evaluate the differential terms of the EB equation
The derivative in the third term on LHS can be written as
Recall, that for a reaction: aA + bB → cC + dD, the reaction rates are related by the stoichiometric coefficients

## Slide 64: Non-isothermal Flow Reactor
Application-3: PFR with Heat Exchange (cont.)
Let us evaluate the differential terms of the EB equation
The derivative in the fifth term on LHS can be written as
The fifth term on LHS can be written as

## Slide 65: Non-isothermal Flow Reactor
Rearranging the above equation in terms of dT/dV, we get
Substituting, the derivative terms into the Energy Balance Equation we get
Application-3: PFR with Heat Exchange (cont.)

## Slide 66: Non-isothermal Flow Reactor
How do we solve non-isothermal PFR problems?
or
We MUST solve the two differential equations, g(X,T) and f(X,T),
simultaneously.
We will need Ordinary Differential Equation (ODE) solver -- MATLAB
Application-3: PFR with Heat Exchange (cont.)

## Slide 67: Other forms of EB equation for PFRs
You may note that for exothermic reaction, this term will result in an increase in T
For single reaction systems in term of conversion
For single reaction systems

## Slide 68: Class Problem #7
It is proposed to design pilot plant for the production of Allyl Chloride. The feed stream comprises 4 moles propylene/mole chlorine. The reactor will be vertical tube of 2 inch ID. The combined feed molar flow rate is 0.6 g-mol/h. The inlet pressure is 2 atmospheres. The feed stream temperature is 275 C. Calculate Allyl Chloride production as a function of tube length for the following 2 cases:
Case-1: PFR jacketed with heat exchange fluid circulated at 275 C Case-2: Adiabatic operation of PFR

## Slide 69: Class Problem #7 (cont.)
T is in Kelvin and p is in atm
U = 28 W/m2-K
-DHRxn1(298)=110,000 J/mol
-DHRxn2(298)=181,500 J/mol
MAIN REACTION: Cl2 + C3H6 → CH2=CH-CH2Cl + HCl
SIDE REACTION: Cl2 + C3H6 → CH2Cl-CHCl-CH3

## Slide 70
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 71
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 72
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 73
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 74
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 75
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 76
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 77
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 78
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 79
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 80
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE

## Slide 81
Salah N. Farhan College of Engineering Diyala University
Fundamentals of CRE